## Slide 1: Coding Tools Using Parametric Representations to Improve Coding Efficiency
LG Electronics
JCTVC-A021
Notes: <number>

## Slide 2: Adaptive Warped Reference (AWR)
Traditional ME/MC
  Just use 2D translation to explain every kinds of motions.
  hard to explain complex motions: Zoom, 3D rotation
AWR
  handles complex motions
  still uses 2D translation motion vectors
  generates additional reference pictures by warping reference pictures
  uses parametric image transformation function (homography)
<number>
Notes: <number>

## Slide 3: Computation of warping parameters
<number>
Reference picture (#:0)
Current picture
Detect feature points in a current picture
& Track the detected features in a reference picture
Notes: <number>

## Slide 4: Computation of warping parameters
<number>
Reference picture (#:0)
Current picture
(xi,yi)
(xi’,yi’)
Segment the features into groups so that the features in one group moves together
& Compute homography parameters H for each group of features
Notes: <number>

## Slide 5: Generating warped reference pictures
<number>
Warp the reference picture using H
& Insert warped reference pictures to reference picture list
Reference picture (#:0)
Current picture
Warped reference picture (#:1)
warp the reference picture using “H”
Notes: <number>

## Slide 6: Encoding with AWR
<number>
Normal coding process
Reference picture (#:0)
Current picture
Warped reference picture (#:1)
Encode the current picture
according to normal coding process
Notes: <number>

## Slide 7: Parameter encoding
Homography transform function has 8 parameters
  Warping results are very sensitive to quantization errors of the 8 parameters
New representation
  Encode the displacement vectors of 4 corner points by H
  Decoder can compute H from the displacement vectors
  8 homography parameters hij are converted to (dx1,dy1, ...,dx4,dy4)
H
(dx1,dy1)
(dx2,dy2)
(dx3,dy3)
(dx4,dy4)
Notes: <number>

## Slide 8: 2-pass coding structure & fast decision rule
2-pass coding structure
  1st pass: normal coding
  2nd pass: coding with AWR
  Then, select one of the two coding results are selected based on RD criterion
Fast decision ruls
  2-pass coding is inefficient; every pictures should be encoded 2 times.
  For hierarchical coding structure
    if AWR is not selected for previously coded upper level picture, then the AWR is not considered for current picture
b
b
b
B
b
b
b
P
Level
Encoding order
3
3
2
1
3
3
2
0
AWR selected
AWR not selected
?
decision rule turns off AWR
automatically
Notes: <number>

## Slide 9: Experimental results without fast decision rule
Anchor: LG CfP model, constraint set 1, 2-pass coding BD-rate(%) |  | 
Class | Sequence | AWR
B | BasketballDrive | -0.09
 | BQTerrace | 0.53
 | Cactus | -7.08
 | Kimono | 0.05
 | ParkScene | 0.05
 | Average | -1.31
C | BasketballDrill | -0.10
 | BQMall | 0.06
 | PartyScene | -0.14
 | RaceHorses | -0.29
 | Average | -0.12
D | BasketballPass | -0.15
 | BlowingBubbles | -0.09
 | BQSquare | -0.17
 | RaceHorses | -0.14
 | Average | -0.14
- | Jets 720p | -8.22
Notes: <number>

## Slide 10
<number>

## Slide 11
<number>

## Slide 12: Experiment results with fast decision rule
Anchor: LG CfP model, constraint set 1, 2-pass coding with fast decision rule |  |  | 
Class | Sequences | BD-rate (%) | Relative encoding time
- | Jets 720p60 (100 frames) | -11.35 | 2.28
B | Cactus (50 frames) | -6.17 | 2.17
D | BasketballPass (full sequence) | 0.09 | 1.00
 | BQSquare (full sequence) | -0.04 | 1.00
Fast decision rule efficiently reduces encoding time.
  Increased encoding time to keep high coding performance
  Decrease encoding time when sequences do not require AWR.
Notes: <number>

## Slide 13: Introduction
AIF was proposed in KTA.
AIF
  Reduces the energy of prediction error
  Requires side information (filter coefficients)
  Is influenced by quantization error of filter coefficients.
<number>
Notes: <number>

## Slide 14: Introduction
PAIF
  an interpolation filter with a few parameters instead of individual coefficients
Why PAIF?
  To reduce the side information for adaptive filter
  To reduce the influence of quantization error of AIF coefficient
<number>
Notes: <number>

## Slide 15: Design of parametric filter
Motivated from Lanczos function
Follows the shape of h.264 filter
<number>
<impulse response with initial parameters>
: [0.5, 1.0], initially π/4
: [0, π/11], initially π/12
: [-0.1, 0.1], initially 0
Notes: <number>

## Slide 16: Parameter estimation
Initial values are fixed.
  To be close to the standard AVC/H.264 filter.
Numerical method is used
  BFGS Quasi-Newton
  Golden section search
Error distribution with respect to the parameters(α1 and α2)
Notes: <number>

## Slide 17: Parameter coding
Uniform quantization
Fixed Length Coding
62 bits for parameter set
  11 bits for each
  13 bits for each
  14 bits for (1 bit for sign)
<number>
Notes: <number>

## Slide 18: Offset
Offset is added to prediction samples after filtering
  One offset value for each reference frame
  Precision : 0.1
<number>
Notes: <number>

## Slide 19: Complexity
Like other AIF techniques, we use 2-pass encoding structure.
  1st pass: normal coding
  2nd pass: coding with PAIF
  Then, select one of the two coding results are selected based on RD criterion
Notes: <number>

## Slide 20: Experimental results
<number>
Anchor: LG CfP model with high precision h.264 filter, constraint set 1, BD-rate(%) |  |  |  | 
Class | seq. | singlepass SIFO | 2D-AIF | P-AIF
C | BasketballDrill | -0.46 | -0.31 | -0.56
 | BQMall | -0.25 | -0.40 | -0.68
 | PartyScene | -0.71 | -0.90 | -1.79
 | RaceHorses | -0.37 | -0.48 | -0.02
Class C Avg. |  | -0.45 | -0.52 | -0.76
D | BasketballPass | 0.42 | -0.08 | -0.13
 | BlowingBubbles | -0.32 | 0.28 | -1.83
 | BQSquare | -2.72 | -1.19 | -8.89
 | RaceHorses | 0.64 | 0.04 | 0.15
Class D Avg. |  | -0.49 | -0.24 | -2.67
Notes: <number>

## Slide 21: Experimental results
<number>
Notes: <number>

## Slide 22: Experimental results
<number>
Notes: <number>

## Slide 23: Conclusion
Two parametric coding tools are proposed.
AWR showed high coding efficiency for the sequences with evident complex motions
  Cactus: -7.08%, Jets: -8.22%
AWR is a useful coding tool because the zooming, rotation, and panning are frequently used camera motions
PAIF showed high coding efficiency for most sequences
in class C and D
  class C : -0.76%
  class D : -2.67% (-8.89% at BQSquare)
PAIF showed more effect than reducing side information
  High performance at high bit rate as well as low bit rate
Notes: <number>