## Slide 1: Coding Tools Using Parametric Representations to Improve Coding Efficiency
LG Electronics
JCTVC-A021
Notes: <number>

## Slide 2: Adaptive Warped Reference (AWR)
Traditional ME/MC
  Just use 2D translation to explain every kinds of motions.
  hard to explain complex motions: Zoom, 3D rotation
AWR
  handles complex motions
  still uses 2D translation motion vectors
  generates additional reference pictures by warping reference pictures
  uses parametric image transformation function (homography)
<number>
Notes: <number>

## Slide 3: Computation of warping parameters
<number>
Reference picture (#:0)
Current picture
Detect feature points in a current picture
& Track the detected features in a reference picture
Notes: <number>

## Slide 4: Computation of warping parameters
<number>
Reference picture (#:0)
Current picture
(xi,yi)
(xi’,yi’)
Segment the features into groups so that the features in one group moves together
& Compute homography parameters H for each group of features
Notes: <number>

## Slide 5: Generating warped reference pictures
<number>
Warp the reference picture using H
& Insert warped reference pictures to reference picture list
Reference picture (#:0)
Current picture
Warped reference picture (#:1)
warp the reference picture using “H”
Notes: <number>

## Slide 6: Encoding with AWR
<number>
Normal coding process
Reference picture (#:0)
Current picture
Warped reference picture (#:1)
Encode the current picture
according to normal coding process
Notes: <number>

## Slide 7: Parameter encoding
Homography transform function has 8 parameters
  Warping results are very sensitive to quantization errors of the 8 parameters
New representation
  Encode the displacement vectors of 4 corner points by H
  Decoder can compute H from the displacement vectors
  8 homography parameters hij are converted to (dx1,dy1, ...,dx4,dy4)
H
(dx1,dy1)
(dx2,dy2)
(dx3,dy3)
(dx4,dy4)
Notes: <number>

## Slide 8: Experimental results
LG CfP model as anchor, BD-rate(%) |  | 
Class | Sequence | AWR
B | BasketballDrive | -0.09
 | BQTerrace | 0.53
 | Cactus | -7.08
 | Kimono | 0.05
 | ParkScene | 0.05
 | Average | -1.31
C | BasketballDrill | -0.10
 | BQMall | 0.06
 | PartyScene | -0.14
 | RaceHorses | -0.29
 | Average | -0.12
D | BasketballPass | -0.15
 | BlowingBubbles | -0.09
 | BQSquare | -0.17
 | RaceHorses | -0.14
 | Average | -0.14
* | Jets 720p | -8.22
Notes: <number>

## Slide 9: Introduction
AIF was proposed in KTA.
AIF
  Reduce the energy of prediction error
  Side information
  Quantization error
<number>
Notes: <number>

## Slide 10: Introduction
PAIF
  an interpolation filter using a few parameters
  instead of individual coefficients
Why PAIF?
  reduce the side information for adaptive filter
  reduce the quantization error of AIF coefficient
<number>
Notes: <number>

## Slide 11: Design of parametric filter
Motivated from Lanczos function
Follows the shape of h.264 filter
<number>
<impulse response with initial parameters>
: [0.5, 1.0], initially π/4
: [0, π/11], initially π/12
: [-0.1, 0.1], initially 0
Notes: <number>

## Slide 12: Parameter estimation
Initial values are fixed.
  close to the standard AVC/H.264 filter.
Numerical method is used
  BFGS Quasi-Newton
  Golden section search
<number>
“α”
min
point
Direction
Vector
“d”
(Gradient)
Error Function
Determination of d and α by BFGS
Notes: <number>

## Slide 13: Parameter coding
Uniform quantization
Fixed Length Coding
62 bits for parameter set
  11 bits for each
  13 bits for each
  14 bits for (1 bit for sign)
<number>
Notes: <number>

## Slide 14: Offset
Offset values are used with a PAIF
  One offset value for each reference frame
  Precision : not integer but 0.1
<number>
Notes: <number>

## Slide 15: Experimental results
<number>
High precision h.264 filter as anchor, BD-rate(%) |  |  |  | 
Class | seq. | singlepass SIFO | 2D-AIF | P-AIF
C | BasketballDrill | -0.46 | -0.31 | -0.56
 | BQMall | -0.25 | -0.40 | -0.68
 | PartyScene | -0.71 | -0.90 | -1.79
 | RaceHorses | -0.37 | -0.48 | -0.02
Class C Avg. |  | -0.45 | -0.52 | -0.76
D | BasketballPass | 0.42 | -0.08 | -0.13
 | BlowingBubbles | -0.32 | 0.28 | -1.83
 | BQSquare | -2.72 | -1.19 | -8.89
 | RaceHorses | 0.64 | 0.04 | 0.15
Class D Avg. |  | -0.49 | -0.24 | -2.67
Notes: <number>

## Slide 16: Experimental results
<number>
Notes: <number>

## Slide 17: Experimental results
<number>
Notes: <number>

## Slide 18: Conclusion
Two parametric coding tools are proposed.
AWR showed high coding efficiency for the sequences with evident complex motions
  Cactus: -7.08%, Jets: -8.22%
AWR is a useful coding tool because the zooming, rotation, and panning are frequently used camera motions
PAIF showed high coding efficiency for most sequences
in class C and D
  class C : 0.76%
  class D : 2.67% (8.89% at BQSquare)
PAIF showed the probability of improving the existing filter techniques
Notes: <number>