## Slide 1
15 April 2010
Flexible Macroblock Partition
Xiaozhen Zheng
Haoping Yu
JCTVC-A029
Dresden, DE, 15-23 April 2010

## Slide 2: Introduction
The basic idea of proposed technique has been implemented in A111
Natural image contains plentiful texture
Object’s boundary always divides a block into irregular partitions
Conventional quad-tree structured representation can not deal with those cases efficiently

## Slide 3: General idea
Use more flexible block partitions for inter-frame coding
A rectangular block can be divided into irregular partitions
  two triangles
  two unsymmetrical size rectangles
  one triangle and one pentagon

## Slide 4: FMP mode coding
Representation of boundary’s position
  Boundary between two blocks can be controlled by points a and b
  Use two position parameters’ value and symbol to locate the position of points a and b
  Two position parameters (xpos, ypos) are coded

## Slide 5: FMP mode coding (continue)
Simplified representation of boundary’s position
  +45 degree partitioning: (1, pos)
  -45 degree partitioning: (pos, 1)
  Vertical partitioning: (pos, 0)
  Horizontal partitioning: (0, pos)
Predictive coding of the position parameter
  Use neighboring blocks’ position parameter to form the predictor for that of the current macroblock

## Slide 6: Motion Vector Predictor
The motion vectors of neighboring blocks, which has same FMP mode as that of current macroblock, are used to form current macroblock’s motion vector predictor
The position parameters of neighboring blocks are also used to form current macroblock’s motion vector predictor

## Slide 7: Experiment
Test condition
  Implemented in KTA2.6r1
  Implemented on 16x16 blocksize
  +/- 45 degree partitioning, vertical partitioning and horizontal partitioning are used
  Configure to CfP Beta’s configuration
  5 QP points are chose for every sequences, QP values are same as CfP Beta anchors

## Slide 8: Experiment (continue)
WQVGA |  | Bitrate Saving | PSNR Gain | WVGA | Bitrate Saving | PSNR Gain
BasketballPass | Low | -3.92% | 0.18 | BasketballDrill | -2.44% | 0.12
 | High | -2.67% | 0.13 |  | -3.56% | 0.14
BlowingBubbles | Low | -1.01% | 0.04 | BQMall | -2.47% | 0.13
 | High | -1.15% | 0.05 |  | -3.07% | 0.15
BQSquare | Low | -0.91% | 0.04 | PartyScene | -2.12% | 0.07
 | High | -2.20% | 0.08 |  | -1.88% | 0.07
RaceHorses | Low | -3.77% | 0.17 | RaceHorses | -4.48% | 0.18
 | High | -2.85% | 0.15 |  | -4.43% | 0.18
Average | Low | -2.40% | 0.11 | Average | -2.88% | 0.13
 | High | -2.22% | 0.10 |  | -3.24% | 0.14

## Slide 9: Closing remarks
FMP provides more flexible macroblock partitioning
FMP can get satisfied coding efficiency at the areas with plentiful texture
Implemented on P frame
Compression efficiency can be further improved after integrating FMP to 8x8 block and 32x32 block

## Slide 10
Thank you!
www.hisilicon.com