## Slide 1: A Highly Parallel and Highly Efficient System for Video Coding JCTVC-A105: Sharp Response to JCT-VC Call for Proposals A. Segall, T. Yamamoto, J. Zhao, Y. Kitaura, Y. Yasugi and T. Ikai

## Slide 2: Overview
Overview
  High Level Description of Proposed System
  Novel Features
  Performance

## Slide 3: High Level Algorithm Description
Goal
  We propose a video coding system that has both higher parallelism and higher coding efficiency than state-of-the-art.
  Parallel approaches to common bottlenecks
    8x parallelism for intra-prediction
    Arbitrary parallelism for entropy decoding
  Coding efficiency
    21% coding efficiency improvement for higher delay
    35%/12% coding efficiency improvement for lower delay using IPPP
    Most notable – very, (very!) small coding efficiency loss through introduction of parallel tools. In some cases, we observe gains.
Our video system is in the spirit of existing MPEG-AVC/ITU-T H.264. Specifically, it is
  Block based
  Motion compensated
  with Transform coding

## Slide 4: High Level Description of Algorithm
Compared to MPEG-AVC/ITU-T H.264, we incorporate the following changes that should be well understood by experts
  Larger coding block sizes
    We employ a superblock that contains a 2x2 group of macroblocks
  Larger transforms
    We employ a 16x16 integer transform
  Adaptive prediction and filtering
    We employ the E-AIF and QALF tools
  Motion vector competition
  High precision filtering

## Slide 5: High Level Description of Algorithm
In addition to the previous tools, we also incorporate the following
  Parallel intra-prediction with Adaptive Multi-Directional Intra Prediction (AMIP)
  Parallel entropy coding
  Multiple E-AIF
  Loop Filtering with Codeword Restrictions
We describe these systems in the following slides

## Slide 6
Parallel Intra Prediction

## Slide 7: Parallel Intra Prediction
Parallel intra prediction
  Goal is to remove the serial bottleneck existing in legacy intra-prediction
  Approach
    Divide blocks into two partitions
    Predict first partition from pixels in neighboring macroblocks
    Predict second partition from:
      Pixels in first partition
      Pixels in neighboring macroblocks
Second pass blocks
First pass blocks

## Slide 8: Parallel Intra Prediction
Prediction of First Pass Blocks
  Uses only pixels in neighboring macroblocks
  Predicted using “adaptive multi-directional intra prediction”
    Three mode sets: default, horizontal and vertical
    Mode sets derived from mode sets of neighbors
    Prediction mode selected from modes [0,8] of corresponding mode set
  For DC prediction, we compute the DC as a weighted function of the distance between the block and the horizontal and left macroblock boundaries
  Mode is predicted from first block above and to the left of current block that is either in neighboring macroblock or current partition
0: default mode set
1: horizontal mode set
2: vertical mode set
mode: pType
0: VERT
1: HOR
2: DC
3: DIAG_DOWN_LEFT
4: DIAG_DOWN_RIGHT
5: VERT_RIGHT
6: HOR_DOWN
7: VERT_LEFT
8: HOR_UP
mode: pType
0: HOR
1: HOR_P15
2: HOR_M15
3: HOR_P5
4: HOR_M5
5: HOR_P10
6: HOR_M10
7: DC
8: VERT
mode: pType
0: VERT
1: VERT_P15
2: VERT_M15
3: VERT_P5
4: VERT_M5
5: VERT_P10
6: VERT_M10
7: DC
8: HOR
0
3
2:DC
4
5
6
7
8
1
0
1
2
6
4
3
5
7:DC
8
0
3
5
1
4
6
2
8
7:DC

## Slide 9: Parallel Intra Prediction
Prediction of Second Pass Blocks
  Uses pixels in neighboring macroblocks AND pixel in first pass blocks
  Notice that bottom and right boundaries may be available
    We introduce additional modes to account for bottom and right neighbors
    Additional modes combine two predictions that are out of phase
      For example, mode 1 and mode 10
      Predictions are weighted based on distance from boundary
Mode | Name of Mode
9 | Vertical 2
10 | Horizontal 2
11 | DC 2
12 | Diagonal Down Left 2
13 | Diagonal Down Right 2
14 | Vertical Right 2
15 | Horizontal Down 2
16 | Vertical Left 2
17 | Horizontal Up 2
Example for Default Mode Set. Extension to other mode sets are straightforward

## Slide 10: Parallel Intra Prediction
Prediction of Second Pass Modes
  To signal intra-prediction mode, we transmit:
    Prediction mode
    Weighting flag
  Prediction mode is restricted when there are few intra-prediction modes in the first set
    In this case, fewer bits are transmitted

## Slide 11: Performance
Tool performance
  Parallelism
    4x4:
      Sharp: 2 prediction/refinement steps
      Serial: 16 prediction/refinement steps
    8x8
      Sharp: 2 prediction/refinement steps
      Serial: 4 prediction/refinement steps
  Coding Efficiency impact
    For Class B (improvement)
      All Intra: -.9% BD-rate
      IPPP: -.16% BD-rate
      HierB: -.32% BD-rate
Second pass blocks
First pass blocks

## Slide 12
Parallel Entropy Coding

## Slide 13: Entropy Slices
Goal
  Allow for high degree of parallelization with smaller coding efficiency loss
Our approach: Entropy Slice
  Introduce partitioning of slices into smaller “entropy” slices
  Entropy slice
    Reset context models
    Restrict definition for neighborhood
    Process identical to current slice by entropy decoder
    Key difference: reconstruction uses information from neighboring entropy slices

## Slide 14: Entropy Slices
Syntax
  Slice header
  Indicate slice is “entropy slice”
  Send information necessary for entropy decoding

## Slide 15: Entropy Slices
Advantages:
  Flexible - little impact on single thread/core applications
    Decode all entropy slices prior to reconstruction
    OR
    Decode entropy slice and then reconstruct without neighbourhood reset
  Can be combined with any entropy coding engine
  Allows degree of parallelism to be guaranteed and expressed as profile/level restrictions.
Results
  HierB
    For 16x parallelism: -.025% BD-rate (improvement)
    For 45x parallelism: .54% BD-rate
  IPPP
    For 16x parallelism: .071% BD-rate
    For 45x parallelism: .57% BD-rate

## Slide 16
Multiple E-AIF

## Slide 17: Multiple Filter E-AIF
Multiple Filter E-AIF
  Extends the concept of AIF to support multiple filters
    Encoder transmits two filter descriptions
      One is assigned to list0
      One is assigned to list1
    Decoder selects appropriate filter automatically based on reference list
  Filter coefficients transmitted sequentially in the bit-stream

## Slide 18
Codeword Restriction Model

## Slide 19: Codeword Restriction
Codeword Restriction
  Use knowledge of original data to constrain the output of adaptive loop filter.
  Note: It’s more likely (compared to previous standards) to exceed the dynamic range of the original data due to the adaptively.
  Process
    Signal maximum and minimum codewords
    Replace existing clipping operation with operation to clip to maximum and minimum codewords
De-blocking
Operation
Adaptive
Loop Filter
Codeword
Restriction
Reference Buffer/Display
Reference Buffer/Display
Bit-stream
Adaptive
Loop Filter
Codeword
Restriction
De-blocking
Operation
Adaptive
Loop Filter
Codeword
Restriction

## Slide 20: Codeword Restriction
Performance
  Depends on characteristics of original data
    More improvement when more pixels are close to max/min value
  For sequences such as BayQuarter material
    We observe approximately 2% reduction in bit-rate
    Basically no increase in complexity

## Slide 21
Overall Performance

## Slide 22: Performance
We have measured the performance of our algorithm according to the CfP conditions
Results follow:
  CS1 BD-Rate
    Average: -20.7%
    ClassA: -19.3%
    ClassB: -22.85%
    ClassC: -20.13%
    ClassD: -19.4%
Note: BD-rate percentages are relative to JCTVC anchors. A value of -N% means that the proposal provides a N% reduction in bit-rate compared to the anchor.

## Slide 23: Performance
CS2-Gamma BD-Rate
  Average: -34.31%
  ClassB: -40.9%
  ClassC: -30.72%
  ClassD: -26.7%
  ClassE: -38.27%
CS2-Beta BD-Rate
  Note that we use IPPP coding in our proposal and not Hier-P
  Average: -12.21%
  ClassB: -19.98%
  ClassC: -9.83%
  ClassD: -0.53%
  ClassE: -18.01%
Note: BD-rate percentages are relative to JCTVC anchors. A value of -N% means that the proposal provides a N% reduction in bit-rate compared to the anchor.

## Slide 24
Software

## Slide 25: Software
Software
  Derived from JM15.1
  Compiler:
    Visual Studio
    GNU Compiler Collection (gcc)
  Execution environment
    Linux and Windows
  External libraries – not used
  Parallel processing – not used
    Note: separate OpenMP version of software exists containing parallel implementation of parallel intra and entropy coding technology)

## Slide 26
Conclusions

## Slide 27: Conclusions
Conclusions
  Video coding system that has both higher parallelism and higher coding efficiency than state-of-the-art
    Parallelism - Intra
      Uses two prediction and refinement steps for 8x8 and 4x4 blocks
      Compared to serial prediction: 8x and 2x degree of parallelism for 4x4 and 8x8, respectively
      No loss from parallelism – actually small gains for Class B (All Intra: .9% BD-rate)
    Parallelism – Entropy
      Uses slice mechanism applied separately to entropy and reconstruction operations
      Applicable to any entropy coding system
      No or small loss from parallelism – .07% BD-rate for 16x IPPP; .025% improvement for HierB
      Very amenable for standardization – easy to guarantee any degree of parallelism as part of profile/level
  These approaches are incorporated with known techniques for higher coding efficiency: Larger coding block sizes, Larger transforms, Adaptive prediction and filtering, Motion vector competition, High precision filtering
  Proposes new technology
    Parallel intra-prediction with adaptive multi-directional intra-prediction (AMIP)
    Parallel entropy coding
    Multiple E-AIF
    Loop Filtering with Codeword Restrictions
Propose CE to study proposed techniques

## Slide 28: A Highly Parallel and Highly Efficient System for Video Coding JCTVC-A105: Sharp Response to JCT-VC Call for Proposals A. Segall, T. Yamamoto, J. Zhao, Y. Kitaura, Y. Yasugi and T. Ikai