## Slide 1: Description of video coding technology proposal by Huawei Technologies & Hisilicon Technologies (JCTVC-A111 )
26/7/29
Haitao Yang, Jiali Fu, Sixin Lin, Jin Song, Dong Wang, Mingyuan Yang, Jiantong Zhou, Haoping Yu
Huawei Technologies
Changcai Lai, Yongbin Lin, Lingzhi Liu, Jianhua Zheng, Xiaozhen Zheng
Hisilicon Technologies
Notes: <number>

## Slide 2
Contents
Proposed coding tools
Software implementation
Compression performance
Closing remarks

## Slide 3
Summary of the proposed coding tools
Intra-frame coding
  Prediction
    Resample-based intra prediction
    Line based intra prediction
  Transform
    Rate-distortion optimized transform
  Quantization
    Adaptive frequency weighting quantization
Inter-frame coding
  Motion representation
    Flexible macroblock partition
  Motion compression
    Template based motion derivation
  Residual prediction
    Inter-frame DC offset
    Second order prediction
  Transform
    Directional transform
  Quantization
    Adaptive frequency weighting quantization
Large MB size is not supported currently
Notes: The block based hybrid coding framework is still used in the proposed codec.
Incorporating the proposed coding tool into the framework, several modules within the framework are modified.
Intra-coding, inter-coding, modules are modified.
AFWQ is used in both intra-coding and inter-coding.
Since the proposed codec is developed from the MPEG4-AVC/H.264 conformant software, the same notations as specified in MPEG4-AVC/H.264 standard are used hereinafter to describe the proposed video coding algorithms. Unless otherwise specified, the implementation is the same as KTA2.6r1. It should be noted that though large macroblock segmentation is implemented in KTA 2.6r1, it is switched off in the proposed codec. Therefore by macroblock (MB) we mean 16x16 blocks in the following description.

## Slide 4
Resample-based intra prediction (RIP)
Three new MB coding modes
  Resampling: hierarchical decomposition
  Side information coding

## Slide 5
Resample-based intra prediction (continued)
Block I0
  Conventional Intra-coding
Block P1 & P2
  Prediction Interpolation of I0 using 4-tap filter [-1 5 5 -1]
  Residual coding
Block P3
  Prediction Averaging four neighboring pixels
  Residual coding
Other modifications
  Block based QP
  Loop filter inside the RIP MB disabled
Complexity
Notes: Take the Intra_RIP_8x8 mode as an example for illustration.

## Slide 6
Line-based intra prediction (LIP)
Motivation
4 LIP modes
  1x16, 16x1, 2x8 and 8x2
Side information
  One flag
  One symbol
Directional prediction
DCT of size
  1x16, 16x1, 2x8 or 8x2
Modified zigzag scan
Residual coding unchanged
Complexity
Notes: Intra predictions in MPEG4-AVC/H.264 perform zero-order extrapolation using the adjacent boundary pixels of reconstructed neighboring blocks to get the prediction of the entire coding block.
One problem of such an intra prediction design is that the prediction error increases as the distance from the reference pixel to the current prediction pixel increases.
To solve the problem, a line based intra prediction (LIP) coding method is proposed.

## Slide 7
Rate-distortion optimized transform (RDOT)
Motivation
Transform matrices
  Separable KLT
  I4MB mode: 2 matrices
  I8MB mode: 4 matrices
  I16MB mode: 8 matrices
Side information
  One flag
  Two symbols for column and row transform matrices respectively
Complexity
Notes: Motivation: diversity in the residual after intra prediction

## Slide 8
Flexible macroblock partition (FMP)
Motivation
4 FMP modes are proposed
Side information coding
  FMP modes signaling
  FMP parameter coding
Motion vector prediction
Complexity

## Slide 9
Template based motion derivation (TBMD)
Motivation
TBMD for non-direct coding modes
  P16x16, P16x8, P8x16, P8x8, B16x16, B16x8, B8x16
Template composition
Candidate based template matching
Multiple reference pictures and multi-hypothesis prediction
Side information
Complexity

## Slide 10
TBMD for B direct mode – spatial temporal direction mode (STDM)
Replacement of
  B_SKIP, B_DIRECT_16x16, and B_DIRECT_8x8 modes
Procedures
MV set composition for candidate based STDM
Cost function
Complexity
Notes: Motivation: the shortcoming of the existing method, this is proposed as an improvement

## Slide 11
Inter-frame DC offset (IDCO)
Motivation
Incorporated into P16x16 mode in the current implementation
Encoding and decoding process
Template based DC offset estimation
Complexity

## Slide 12
Second order prediction (SOP)
Motivation
Reconstruction of blocks using SOP
Intra prediction as the SOP method
  4x4 and 8x8 IP modes are used and are distinguished by the 8x8 transform flag
Construction of reference pixels for intra prediction
Side information
  A flag to indicate the usage
  Most probable mode derivation
  Intra prediction mode coding based on the most probable mode
Complexity

## Slide 13
Directional transform (DT)
Motivation
Non-separable KLT is used as an initial try
An alternative to DCT for 8x8 block, 8 direction are selected
Side information
  A flag to indicate the usage
  An index to specify the direction
Spatial-temporal predictive coding of direction information
Temporal predictor – texture direction of prediction
Complexity
Notes: Motivation: the shortcoming of the existing method, this is proposed as an improvement

## Slide 14
Adaptive frequency weighting quantization (AFWQ)
Motivation
Three 7-parameter frequency band distribution models
Three sets of frequency band weighting parameters are used
  One for textured region, one for flat region, one uniform quantization
For each slice,
  1 distribution model + 3 sets of parameters = 3 quantization matrix

## Slide 15
Adaptive frequency weighting quantization (continued)
MB level adaptation of quantization matrix
  Preserve more high frequency components for the textured region
  Preserve more low frequency components the flat region
  The spatial complexity is measured by the coding parameters of neighboring encoded MBs
Slice level side information coding
  2-bit index to indicate the selection of distribution model
  Predictive coding of the two sets of weighting parameters, with reference to the default values stored in encoder & decoder
AFWQ is applied to luma8x8, luma4x4, and chroma4x4 residual
Complexity

## Slide 16
Software implementation
All the tools work together by RDO selection
Based on the KTA software (version 2.6r1), following tools are switched on
  EAIF
  QALF
  MDDT
  RDOQ = 1

## Slide 17
Compression performance
Constraint set 1
  Max -34.58%/1.67dB in low rate case
  Max -31.92%/1.41dB in high rate case
Constraint set 2
  Max -24.37%/1.08dB in low rate case
  Max -25.78%/1.05dB in high rate case
  HP prediction structure
Subjective quality is consistent with objective quality

## Slide 18
Complexity analysis
Platform for encoding
Encoding complexity
  Encoding time is a few times more than that of the KTA software
  Detailed data are available in the attached Excel sheet
Memory usage of encoder
  As can be seen from the algorithm description, the proposed tools do not introduce significant memory usage at the encoder

## Slide 19
Complexity analysis
Platform for decoding
Decoding complexity
  YUV output is enabled and reference input disabled
  Decoding time is a few times more than that of the anchors
  Detailed data are available in the attached Excel sheet
Memory usage of decoder
  As can be seen from the algorithm description, the proposed tools do not introduce significant memory usage at the decoder

## Slide 20
Closing remarks
The performance of MPEG4-AVC/H.264 video coding technique can be greatly improved by the proposed codec
Encoder implementation is not optimized, which result in Extra computational complexity
Synergy of these new tools need to be further studied
Suggestion: establish AhGs for representative coding techniques

## Slide 21
Notes: <number>