## Slide 1: Description of video coding technology proposal by FUJITSU (JCTVC-A115)
Copyright 2010 FUJITSU LIMITED
K.Kazui, J.Koyama, and A.Nakagawa
FUJITSU LABORATORIES LTD.
1st JCT-VC meeting, Dresden/Germany
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 2: Summary
<number>
Copyright 2010 FUJITSU LIMITED
Improvement of the coding efficiency of the sign (+/-) of a DCT coefficient
  Conventional method codes the sign using the bypass process of CABAC
    The occurrence of ‘+’ is 50%
  Proposed method estimates the sign from neighboring blocks and codes the difference (0: same, 1: different) between estimated sign and original sign using CABAC
  The occurrence of the difference tends to ‘0’ (same) when the precision of sign estimation is high enough. Thus it is possible to code the sign better than conventional method
Implementation
  JM 16.2
Coding gain
  Alpha anchor: 0.04 dB in BD-PSNR and -1.0 % in BD-Bitrate
  Beta anchor: 0.03dB in BD-PSNR and -0.75% in BD-Bitrate
Increase in computational complexity and memory usage (vs. JM16.2)
  Complexity: 9% (encoder), 5% (decoder)
  Memory usage : less than 0.1% (encoder/decoder)
Merit
  Can improve the coding efficiency of the sign with small increase in complexity
  Can co-exist with other coding tools
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 3: Concept of sign estimation
<number>
Copyright 2010 FUJITSU LIMITED
Signs which minimizes |A-B|^2 are considered as most probable signs of current block

## Slide 4: Encoding Process Overview
<number>
Copyright 2010 FUJITSU LIMITED
Number of signs for estimation is limited up to 4 (4x4 block) or 6 (8x8 block)
Reason: Estimation result of signs for coefficients with small absolute level tends to be wrong (i.e. coding gain becomes small)

## Slide 5: Technical detail
<number>
Copyright 2010 FUJITSU LIMITED
Syntax (coeff_sign_diff)
Sorting of DCT coefficients
Sign estimation
CABAC encoding of coeff_sign_diff

## Slide 6: 1) Syntax (1/2)
<number>
Copyright 2010 FUJITSU LIMITED
residual_block_cabac( coeffLevel, startIdx, endIdx, maxNumCoeff ) {
if( “current block is luma” ) {
lumaFlag = 1
numCoefEval = ( maxNumCoeff == 16) ? (4) : (6)
}
else lumaFlag = 0
numSignificantCoeff = 0, state = 0
if( maxNumCoeff != 64 ¦ ¦ ChromaArrayType = = 3 ) coded_block_flag
for( i = 0; i < maxNumCoeff; i++ ) coeffLevel[ i ] = 0
if( coded_block_flag ) {
numCoeff = endIdx + 1
i = startIdx
do {
significant_coeff_flag[ i ]
if( significant_coeff_flag[ i ] ) {
numSignificantCoeff ++
last_significant_coeff_flag[ i ]
if( last_significant_coeff_flag[ i ] )
numCoeff = i + 1
}
i++
} while( i < numCoeff − 1 )
coeff_abs_level_minus1[ numCoeff − 1 ]

## Slide 7: 1) Syntax (2/2)
<number>
Copyright 2010 FUJITSU LIMITED
if(( MbPartPredMode( mb_type, 0 ) != Intra_16x16 ) && ( lumaFlag == 1 )) {
for( i = numCoeff − 2; i >= 0; i− − ) {if( significant_coeff_flag[ i ] ) coeff_abs_level_minus1[ i ]}
for( i = 0; i < min(numSignificantCoeff, numCoefEval ); i ++ ) {
coeff_sign_diff[ i ]
if( coeff_sign_estimated[ i ] == 1 ) state = 1
}
for( i = min(numSignificantCoeff, numCoefEval ); i < numSignificantCoeff; i ++ ) coeff_sign_flag[ i ]
estimateSign( numSignificantCoeff, maxNumCoeff, coeff_sign_estimated, coeff_sign_flag, coeff_abs_level_minus1, coeffLevel )
}
else {
coeff_sign_flag[ numCoeff – 1 ]
coeffLevel[ numCoeff − 1 ] = ( coeff_abs_level_minus1[ numCoeff − 1 ] + 1 ) * ( 1 − 2 * coeff_sign_flag[ numCoeff − 1 ] )
for( i = numCoeff − 2; i >= 0; i− − )
if( significant_coeff_flag[ i ] ) {
coeff_abs_level_minus1[ i ]
coeff_sign_flag[ i ]
coeffLevel[ i ] = ( coeff_abs_level_minus1[ i ] + 1 ) * ( 1 − 2 * coeff_sign_flag[ i ] )
}
}
}
}
Note
Proposed technique is not applied to chroma coefficients and INTRA16x16 MB at current implementation
Transimission order of coeff_sign_diff[] and coeff_sign_flag[] is modified
Variable state is used to switch context

## Slide 8: 2) Sorting of DCT coefficients
<number>
Copyright 2010 FUJITSU LIMITED
Sorted in the descending order of |Level|
When coefficients have the same |Level|, sorted in the descending order of zigzag scan

## Slide 9: 3) Sign Estimation (1/4)
<number>
Copyright 2010 FUJITSU LIMITED
Prediction from neighboring blocks
  q[], predicted pixels at the boundary of current block, are extrapolated from p[], pixels in neighboring blocks (top, left, top-left) using 3x2-tap filter
  Cx, the coefficients of 3x2-tap filter, are switched by the edge direction in p[]
    D = [0, 24], the index of 3x2-tap filter, is obtained from D1 and D2, which are the edge direction in two 2x2 subblocks
    The coefficients are empirically obtained from varies kinds of sequences
Derivation of D
5 types of edge direction

## Slide 10: 3) Sign Estimation (2/4)
Signs which minimizes |q[] – ps[]|2 are defined as estimated signs
  q[] : Predicted pixel values extrapolated from neighboring blocks
  ps[]: Reconstructed pixel values of current block using the combination of signs s
<number>
Copyright 2010 FUJITSU LIMITED
Introduction of fast sign estimation method
  Without fast method: 2M times of IQ/IDCT/MC operation is necessary
  With fast method: equivalent result can be obtained with (2M – 1) times of “2 times of multiplication and 7 times of addition”

## Slide 11: 3) Sign Estimation (3/4)
Fast sign estimation method
  Instead of directly calculating SSD of each combination of signs, the fast method calculates the difference of SSD between combinations of signs among which only one sign of coefficients is different.
  The calculation of the difference of SSD consists of only two times of multiplication and 5 times of addition of pre-calculated values.
    Additional two times of addition is for updating the pre-calculated values
  The calculation is performed in the order of M-bit Gray code
    Main property of Gray code is that only one bit is different among adjacent words
    SSD values of all signs relative to that of signs (+, +, …, +) (= Gray code (0, … , 0)) are obtained by accumulating the difference of SSD: SSD[k+1] = SSD[k] – c(k)
<number>
Copyright 2010 FUJITSU LIMITED
Example
(Number of coefficients = 3)
c(): The difference of SSD between “adjacent” signs

## Slide 12: 3) Sign Estimation (4/4)
SSD(k)-SSD(k+1) = -skj *
{(SqValH[k] * ((SqCoefH[uk] << 1) + SqValH[k]) + (SqValV[k] * ((SqCoefV[vk] << 1)
+ SqValV[k]) + LnVal[k]}
<number>
Copyright 2010 FUJITSU LIMITED
Variable | Value
skj | j-th sign of signs #k. Only the j-th sign is different between signs #k and #(k+1)
SqValH[m] | 2*A[um]*T[0, um]*Level[m]
SqValV[m] | 2*A[vm]*T[0, vm]*Level[m]
SqCoefH[i] | ΣSqValH[m'], where m' satisfies (um' = i) Updated at each iteration: SqCoefH[uk] += -skj * SqValH[k]
SqCoefV[j] | ΣSqValV[m'], where m' satisfies (vm' = j) SqCoefV[vk] += -skj * SqValV[k]
LnVal[m] | - Level[m]*{Σk(q"[k, -1]* T[um, k]) * T[0, um] +Σk(q"[-1, k]* T[vm, k]) * T[0, vm])}
Level[m] | The absolute value of m-th inverse-quantized coefficient
m | = [0, (M' - 1)]. M’=min(M, numSignificantCoeff)
q’’[] | = q[] - pred[] – p’[] pred[]: Intra/Inter-predicted pixel p’[]: IQ+IDCT result of coefficients which are coded as coeff_sign_flag
um | Horizontal frequency of mth coefficient (0 <= um < N)
vm | Vertical frequency of mth coefficient (0 <= vm < N)
A[] | Scaling factor for restoring the orthogonal property of DCT
T[x, y] | N*N matrix of N-point one-dimensional inverse transform as defined in current specification

## Slide 13: 4) CABAC encoding of coeff_sign_diff
Additional 80 contexts are used for coeff_sign_diff
  80 = 4 * 10 * 2
  4: block type (Intra4x4, Intra8x8, Inter4x4, Inter8x8)
  10: |Level| (1, 2, 3, … , 9, >=10)
  2: state (0, 1)
    Initialized 0 at the beginning of block processing
    When coeff_signs_diff = 1, state = 1 for the following coefficients in the sorted list
    This is based on the fact that the estimation of the sign appears later in the sorted list tends to be wrong when that of the sign appears early is wrong
  The values of (m, n) for initializing contexts are obtained experimentally
<number>
Copyright 2010 FUJITSU LIMITED

## Slide 14: Compression Performance
Alpha anchor
<number>
Copyright 2010 FUJITSU LIMITED
Class A | BD-PSNR: 0.053, BD-Bitrate: -1.15%
Class B | BD-PSNR: 0.042, BD-Bitrate: -1.29%
Class C | BD-PSNR: 0.038, BD-Bitrate: -0.90%
Class D | BD-PSNR: 0.033, BD-Bitrate: -0.72%
Overall | BD-PSNR: 0.040, BD-Bitrate: -1.01% Coding gain tends to increase as the image size increases.
Class B | BD-PSNR: 0.033, BD-Bitrate: -0.95%
Class C | BD-PSNR: 0.033, BD-Bitrate: -0.81%
Class D | BD-PSNR: 0.028, BD-Bitrate: -0.61%
Class E | BD-PSNR: 0.022, BD-Bitrate: -0.55%
Overall | BD-PSNR: 0.030, BD-Bitrate: -0.75% Coding gain is smaller than that of alpha anchor.
Beta anchor

## Slide 15: Complexity Analysis
Compared with JM16.2
Hardware/OS
  Xeon X5570 (2.93Gz), 4GB memory
  Windows Server 2003R2 (32-bit)
Encoding/Decoding time
  Encoding: Average +8% (Variance = 4)
  Decoding: Average +5% (Variance = 40)
Memory usage
  Less than +0.1%
Other issues
  No impact to ME/MC, Intra-prediction, Transform, In-loop filter
  Parallel processing of CABAC: Same as original H.264
<number>
Copyright 2010 FUJITSU LIMITED

## Slide 16
<number>
Copyright 2010 FUJITSU LIMITED
Copyright 2010 FUJITSU LIMITED
<number>
Notes: Copyright 2010 FUJITSU LIMITED
<number>
Copyright 2007 FUJITSU LIMITED
<number>

## Slide 17: Precision of sign estimation
Example: Sequence S03 at R1(lowest) and R5(Highest)
Total bits of signs in anchor bitstream
  R5: 16% (all signs), 11 % (signs under estimation)
  R1: 10% (all signs), 8% (signs under estimation)
Saved bits by proposed method
  R5: 21% of total bits of signs under estimation -> 77% of signs are correctly estimated
  R1: 15% -> 73% of signs are correctly estimated

## Slide 18: Annex: Coefficients of 3x2-tap Filter
<number>
Copyright 2010 FUJITSU LIMITED
int coef_filter[25][6] = {
// C0 C1 C2 C3 C4 C5
{ 140, 84, 137, -31, -71, -3},
{ 118, -56, 271, -17, -216, 156},
{ 44, 243, 172, -15, -41, -147},
{ 13, 235, 101, -5, -34, -54},
{ 151, 91, -1, -23, 18, 20},
{ 230, -45, 184, 147, -232, -28},
{ 126, 13, 148, 19, -66, 16},
{ 57, 101, 182, 29, -20, -93},
{ 124, 118, 114, 75, -127, -48},
{ 197, 44, 27, 46, -84, 26},
{ -8, 104, 169, 36, -36, -9},
{ -10, 63, 208, 41, -88, 42},
{ -13, 154, 169, 28, -13, -69},
{ -30, 222, 126, 27, -28, -61},
{ 35, 151, 24, 15, 13, 18},
{ 83, 217, 38, -41, -54, 13},
{ 93, 150, 134, -48, -156, 83},
{ 55, 226, 96, -14, -80, -27},
{ 60, 328, 64, -27, -141, -28},
{ 129, 218, -25, -61, -33, 28},
{ 157, 238, 35, -122, -61, 9},
{ 156, 124, 49, -74, -30, 31},
{ 102, 151, 109, -35, -24, -47},
{ 94, 209, 55, -20, -72, -10},
{ 170, 145, -7, -62, -19, 29},
};

## Slide 19: Annex: Values of m and n for additional 80 contexts
<number>
Copyright 2010 FUJITSU LIMITED
ctxIdx Offset |  |  | ctxIdx Offset | Value of cabac_init_idc |  |  |  |  | 
 |  |  |  | 0 |  | 1 |  | 2 | 
 | m | n |  | m | n | m | n | m | n
0 | 0 | 54 | 40 | -6 | 68 | -6 | 68 | -6 | 68
1 | 4 | 42 | 41 | -7 | 64 | -7 | 64 | -7 | 64
2 | 6 | 33 | 42 | -8 | 60 | -8 | 60 | -8 | 60
3 | 5 | 35 | 43 | -13 | 64 | -13 | 64 | -13 | 64
4 | 6 | 30 | 44 | -15 | 64 | -15 | 64 | -15 | 64
5 | 7 | 27 | 45 | -21 | 70 | -21 | 70 | -21 | 70
6 | 4 | 30 | 46 | -18 | 60 | -18 | 60 | -18 | 60
7 | -4 | 45 | 47 | -14 | 50 | -14 | 50 | -14 | 50
8 | 8 | 20 | 48 | -28 | 73 | -28 | 73 | -28 | 73
9 | 8 | 15 | 49 | -5 | 23 | -5 | 23 | -5 | 23
10 | 7 | 51 | 50 | 3 | 57 | 3 | 57 | 3 | 57
11 | 12 | 44 | 51 | 9 | 47 | 9 | 47 | 9 | 47
12 | 16 | 37 | 52 | 12 | 42 | 12 | 42 | 12 | 42
13 | 12 | 46 | 53 | 8 | 50 | 8 | 50 | 8 | 50
14 | 10 | 51 | 54 | -1 | 68 | -1 | 68 | -1 | 68
15 | 3 | 65 | 55 | -1 | 68 | -1 | 68 | -1 | 68
16 | -2 | 74 | 56 | -4 | 72 | -4 | 72 | -4 | 72
17 | 8 | 57 | 57 | -11 | 87 | -11 | 87 | -11 | 87
18 | -11 | 92 | 58 | -43 | -122 | -43 | -122 | -43 | -122
19 | 4 | 63 | 59 | -12 | 81 | -12 | 81 | -12 | 81
20 | 0 | 53 | 60 | -4 | 63 | -4 | 63 | -4 | 63
21 | 4 | 39 | 61 | -4 | 57 | -4 | 57 | -4 | 57
22 | 6 | 30 | 62 | -4 | 48 | -4 | 48 | -4 | 48
23 | 9 | 22 | 63 | -3 | 41 | -3 | 41 | -3 | 41
24 | 10 | 18 | 64 | -5 | 40 | -5 | 40 | -5 | 40
25 | 8 | 19 | 65 | -2 | 29 | -2 | 29 | -2 | 29
26 | 8 | 18 | 66 | -1 | 23 | -1 | 23 | -1 | 23
27 | 12 | 8 | 67 | -6 | 28 | -6 | 28 | -6 | 28
28 | 7 | 15 | 68 | 1 | 10 | 1 | 10 | 1 | 10
29 | 10 | 7 | 69 | 0 | 8 | 0 | 8 | 0 | 8
30 | 4 | 55 | 70 | 2 | 58 | 2 | 58 | 2 | 58
31 | 10 | 44 | 71 | 9 | 45 | 9 | 45 | 9 | 45
32 | 19 | 29 | 72 | 18 | 29 | 18 | 29 | 18 | 29
33 | 20 | 30 | 73 | 15 | 35 | 15 | 35 | 15 | 35
34 | 13 | 45 | 74 | 12 | 42 | 12 | 42 | 12 | 42
35 | 18 | 35 | 75 | 12 | 44 | 12 | 44 | 12 | 44
36 | 16 | 41 | 76 | 14 | 40 | 14 | 40 | 14 | 40
37 | 18 | 36 | 77 | 10 | 48 | 10 | 48 | 10 | 48
30 | 23 | 31 | 78 | 0 | 69 | 0 | 69 | 0 | 69
39 | 8 | 57 | 79 | -12 | 90 | -12 | 90 | -12 | 90