## Slide 1
<number>
Video coding technology proposal by Tandberg, Nokia, Ericsson
JCTVC-A119
1st JCT-VC meeting, Dresden Germany
April 2010

## Slide 2: Summary
<number>
TENTM algorithm has less complexity than H.264/AVC Baseline Profile
Class B Subjective results show that TENTM brings
  around 30% gain on average over H.264/AVC High Profile on CS1
  more than 40% gain on average over H.264/AVC High Profile on CS2
TENTM encoder and decoder runs significantly faster than JM17.0 and KTA 2.7
TENTM represents a clean, back-to-basics design :
  TENTM is ideal to be used in collaborative phase to test various tools on a clean environment with good software
Syntax&Semantics document and TENTM software are provided
  To make sure concrete work starts at this meeting

## Slide 3: Overview
<number>
Requirements of mobile, video-conferencing industries:
  Significant coding efficiency improvement over H.264/AVC.
  Faster standardization of the low complexity operating point with complexity not higher than H.264/AVC Baseline profile.
TENTM was designed to fulfill those requirements:
  Significant subjective quality improvement over H.264/AVC with less complexity than H.264/AVC BP
Clean design: Useful for working towards a high coding efficiency operating point for other use cases, such as broadcast:
  Design from scratch : Clean and efficient software
  No obsolete H.264/AVC tools

## Slide 4: Performance – Coding Efficiency
<number>
Main focus has been on producing good subjective quality - especially at high resolutions.
Analysis of subjective results for Class B sequences show that TENTM achieves:
  around 30% gain on average over H.264/AVC High Profile on CS1
  more than 40% gain on average over H.264/AVC High Profile on CS2
TENTM is highly competitive to other proposals with significantly lower complexity
  Very few proposals outperform TENTM consistently but with a small margin (Class B is examined only)

## Slide 5: Performance - Complexity
<number>
TENTM decoder algorithm has roughly 75% complexity of H.264/AVC Baseline Profile (educated guess on typical platforms)
  Low complexity deblocking and interpolation filters
  Low complexity VLC
  No motion partitions smaller than 8x8
  Low complexity B frames (Integer MV for SKIP and DIRECT)
  TENTM decoder runs more than 2x faster than JM17.0
    Clean implementation with C (no low level optimizations)

## Slide 6: TENTM Software
Clean and fast software written from scratch using C
TENTM decoder is 2-3 times faster than JM17.0 decoder
TENTM encoder is 25 times faster than JM17.0 encoder
TENTM encoder is around 400 times faster than KTA2.7 encoder
Because of its low complexity and clean design TENTM software is ideal to test various tools
  Easily extendable towards high coding efficiency operating point in collaborative phase
TENTM encoder represents a practical encoder useful for future extensions:
  Entire CS2 test-set is encoded in less than 4 hours on a single core
  Does not utilize the full potential of the TENTM syntax

## Slide 7: Motion Representation
<number>
Following candidates for motion partitions:
  64x64 and 32x32 large MBs
  16x16 traditional MBs with 16x16, 16x8, 8x16, 8x8 motion partitions
Improved SKIP mode
  Runs of SKIP are always signaled on the 16x16 MB level
  SKIP MB can have up to two motion vector candidates (selection indicated in the bitstream)
  Motion vectors are rounded to integer for SKIP in B pictures
Low complexity DIRECT mode:
  Motion vectors are rounded to integer to avoid interpolation
Reference index indicate forward, backward or bi-predictive coding:
  Reference index is coded predictively.

## Slide 8: Motion Representation
<number>
2 Reference Frames are used
  Concept of long-term reference is used for generating CS2 bitstreams
High Quality & Low Complexity Interpolation
  Combination of Directional Interpolation Filters (DIF) and Separable Filters (SF)
  1 bit is signaled if the MV points to one of the 9 central positions
  DIF uses strong filter for the middle position
  SF rounds the intermediate values to 8-bits to achieve 16-bit operation
I
P
P
P
HQR- P
P
P
P
HQR Period = 4
HQR- P

## Slide 9: Intra Frame Prediction
<number>
Following INTRA prediction alternatives:
  INTRA 16x16 : DC, vertical, horizontal and planar prediction.
    Planar prediction reconstructs smooth regions in a visually pleasing way
  INTRA 8x8 : DC and angular prediction with 32 directions.
    Angular prediction reconstructs directional structures in a visually pleasing way by defining additional prediction directions
  INTRA 4x4 : DC, vertical, and horizontal.

## Slide 10: Intra Frame Prediction
<number>
Planar Prediction: Used to reconstruct smooth regions in a visually pleasing way
  Signal the bottom-right sample and reconstruct the macroblock using upper row, left column and signalled sample
Step – 1: Interpolate rightmost and bottom samples
Step – 2: Bi-linear interpolation of middle samples

## Slide 11: Transforms and Quantization
<number>
4x4, 8x8, 16x16, 32x32, 64x64 transforms
  16-bit implementation is used for all the transform sizes.
For coding INTER modes, a spatially varying transform (SVT) is used as additional mode:
  The position of transform block within macroblock is varied
  Additional 16x4 and 4x16 transforms are utilized

## Slide 12: In-loop Filtering
<number>
Reduced complexity compared to H.264/AVC
  Only applied on block boundaries of 8x8 (no 4x4 filtering)
  Significantly less complex logic compared to H.264/AVC filtering.
Uses a combination of strong and weak filters
  Improved visual quality with low complexity
Interpolative filtering if two macroblocks are coded in planar mode

## Slide 13: Entropy Coding
<number>
VLC based entropy coding
Main features:
  Improved context adaptivity:
    Use adaptive sorting tables
    Adapt the VLC table based on the coding statistics.
  Improved coefficient coding
    Lower complexity than H.264/AVC but improved coding efficiency
code number = 7
before sorting:
after sorting:
12
3
9
3
12
9
0
6
7
0
6
7
table_index = 12

## Slide 14: Entropy Coding
<number>
All the transform sizes use the same 8x8 coefficient coding engine
  16x16, 32x32, 64x64 transforms are truncated (always the 8x8 lowest frequency coefficients are coded)
Overview of coefficient coding:
  Position of last non-zero coefficient and whether its magnitude is larger than 1 is signaled
  Runs of zeros are signaled in reverse scan order.
  Switch to level mode based on magnitude and position of previously coded coefficients
    Level mode codes each remaining coefficient one by one.
Coefficient coding is less complex than H.264/AVC CAVLC

## Slide 15: Future Extensions
<number>
Several well-know tools could be added during the course of standardization:
  CABAC
  Additional reference frames
    3-4 % gain
  Sub LMB partitions (e.g. 64x32, etc.):
    1-2 % gain
  Improved MV coding
    1-2% gain
  Adaptive in-loop filtering
  Decoder side MV derivation
  Larger LMBs (128x128)
  Adaptive Interpolation Filtering (AIF)

## Slide 16: Conclusions
<number>
We believe the information brought to this meeting attest significant coding efficiency improvement is possible with very low complexity.
Many requests to MPEG and VCEG earlier for the need of low complexity operating point in a short timeframe
We request JCT-VC to start a concentrated effort as soon as possible
  Syntax & Semantics and detailed decoder description are provided to make working on low-complexity operating point easier.
  Many interesting proposals are brought to JCT-VC, some of them also suitable for low-complexity operating point

## Slide 17: Conclusions
<number>
We believe TENTM is ideal also for working towards the high coding efficiency goal:
Back-to-basics design, low complexity and clean software
  TENTM encoder is 25x faster than JM17.0
    ~400-800 times faster than many high complexity proposals (rough estimate).
Majority of the tools brought to JCT-VC do not overlap with tools in TENTM
  TENTM is ideal to be used in collaborative phase to test various competing tools on a clean environment with good software
Syntax&Semantics document and TENTM software are provided
  Make it easier for others to understand TENTM and make further developments
  To make sure concrete technical work starts at this meeting