## Slide 1: Video coding technology proposal for MPEG-HVC/ITU-T EPVC
A.Ichigaya, K.Iguchi, Y.Shishikui
NHK
S.Sekiguchi, K.Sugimoto, A.Minezawa
Mitsubishi Electric Corporation
JCTVC-A122

## Slide 2: Outline
Codec overview
Proposed coding tools
Coding performance
Complexity analysis
Simulation software
Conclusion

## Slide 3: Overview of Proposed Codec
MB-based MC+Transform hybrid coding with
  MB size extension
  Adaptive transform including block-size extension and DST
  New intra prediction exploiting global spatial correlation
  Multi-level hierarchical motion partitions including simplified diagonal partition modes
  Adaptive PMV/Direct MV derivation
  Adaptive in-loop Wiener filter with extended AVC de-blocking
Non-normative remarks to obtain reported performance
  Single-pass RDO-Q
  EPZS based motion vector search
  No use of frame multi-pass coding

## Slide 4: MB size extension
Promising for coding performance enhancement
  Better R-D trade-off depending on source characteristics
    resolution, motion activity, texture smoothness, etc
  Relevant for video source having higher inter-sample correlation such as high-resolution video
  Essentially no complexity impact to normative process
◎

## Slide 5: Motion representation
Multi-layer hierarchical motion partitions
  Quad-tree based
  Simplified non-rectangular (“diagonal”) shapes
  Mixed intra/inter in a MB
  Hierarchical skip support
◎
Flexible motion representation for wide variety of video source classes with a single syntax

## Slide 6: Diagonal motion partitioning
Promising through literatures
  Around 8% gain with pixel-wise partitioning (too complex encoding)
  Decoding complexity impact: only on memory access
Issue: “Efficiency and Complexity” trade-off
  Flexible partitioning increases pattern representation bits and encoding complexity
Proposal: “Simplified” and “Block-aligned” shapes
  PMV derivation by shifting spatial neighboring positions depending on shape
◎

## Slide 7: Adaptive PMV derivation
Extends KTA’s Motion Vector Competition concept to exploit temporal correlation
1-bit signaling per motion partition to select spatial or temporal PMV candidate
◎
Contribute to reduction of motion bits especially becoming a burden in high-resolution video coding

## Slide 8: Improved direct mode
Adaptive direct MV derivation from spatial and temporal candidates
  Without signaling bit by SAD competition at both encoder and decoder
  Used also as B-Skip MV
Use of closest spatial neighboring MV, not outside a MB as AVC
  Consideration on MB size extension
Selective prediction generation at picture edge
  “Uni-directional pred.” when UMV observed at picture edge
  Avoid unreliable prediction with UMV
◎
Contribute to coding performance improvement for B-picture

## Slide 9: Generation of inter prediction
Essentially identical to AVC
  Semantics of slice (picture) type
  Q-pel accuracy MV representation
  Chroma MV derivation
  Multiple reference pictures and refIdx signaling
  MC interpolation filtering
Disabled weighted prediction for obtaining coding performance result

## Slide 10: Transform design
Adaptive block-size 2D transform for luma inter residue
  Simple decision depending on motion partition size
Coding mode dependent transform for luma intra residue
  intra4x4, intra8x8  4x4, 8x8
  Intra16x16  16x16 DCT
Efficient signal power concentration depending on residual statistics
◎

## Slide 11: Intra prediction
New intra16x16 prediction modes
  Global planer prediction
  Iterative adjustment prediction
  Replacing DC/Planer modes
Re-use AVC on
  Luma intra4x4, intra8x8, intra16x16(horizontal, vertical modes)
Modification to AVC on
  16x16 DCT for intra16x16 residue
  Intra8x8 coding to chroma

## Slide 12: Global planer prediction
Assumes that pixel values of neighboring samples and current block samples fit on a plane surface.
The surface is calculated from neighboring samples using the LMS method.
Suitable for area with gradation texture
Value of pixel

## Slide 13: Iterative adjustment prediction
Estimates pixel values of current block to be natural extension of neighboring area in an iterative manner
- set initial values for current block
- reduce discontinuity between block and neighboring area
- keep the neighboring sample values as originally constructed values
Suitable for area with global ac fluctuation
Current
block
Set an initial value
Constructed
neighboring
samples
DCT
Replace with zero
IDCT
Replace with original
constructed neighboring samples
n
n
32
16
16
Process block
16
16
Prediction block

## Slide 14: Adaptive DCT/DST Transform for chroma
Chroma is transformed by DCT or DST adaptively.
DST is suitable for compression of low correlation signals.
The complexity is as same as DCT.
The 8x8 Integer DST is defined as below:

## Slide 15: Quantization/Scanning
Conceptually identical to AVC
Notes
  16x16 DCT does not use decomposition into “core” + “scale” matrices, and zig-zag scanning is used
  Scaling process is not modified for chroma DST, and modified zig-zag scanning is used.
Non-normative settings for obtaining reported coding performance
  Single-pass RDO-Q USED
  Hierarchical QP offsets USED
  Q-matrix function NOT USED

## Slide 16: Entropy Coding
CABAC with modifications to support MB size extension syntax
  Quad-tree based CBP representation
  Unification of symbol representation of intra16x16 mode with other intra modes
  Skip mode at sub-partition levels
◎

## Slide 17: In-loop filtering
Extended AVC de-blocking filter
  Consideration on 16x16 transform block and mixed intra/inter blocks
  Strength derivation and actual filtering process identical to AVC
Adaptive Wiener filter
  Enhancement to KTA BALF tool
  Quality improvement of decoded picture and inter-prediction reference
◎

## Slide 18: Enhanced BALF
Applies up to two Wiener filters per video component adaptively
  Optimising two Wiener filters together with the adaptive indication flags
Significant coding gain observed,
at penalty of picture-level repetitive filter design and local adaptation process
◎
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Coding Performance Summary
Constraint Set1
  Hierarchical B structure identical to Alpha anchor
  Around 1dB luma BD-PSNR gain for class A/B/C at higher compression condition
Constraint Set2
  IPPP structure with hierarchical P style QP offsets
  Relative to Beta anchor
    Around 1dB luma BD-PSNR gain for class B/E at higher compression condition
  Relative to Gamma anchor
    Around 2dB luma BD-PSNR gain for class B/E at higher compression condition

## Slide 20: Class A/B, CS1 vs. Alpha anchor
Sequence | BD low |  | BD high | 
 | Bitrate Δ | PSNR Δ | Bitrate Δ | PSNR Δ
Traffic | -25.45 | 1.08 | -22.62 | 0.84
PeopleOnStreet | -16.91 | 0.95 | -13.93 | 0.76
average | -21.18 | 1.02 | -18.28 | 0.80
Sequence | BD low |  | BD high | 
 | Bitrate Δ | PSNR Δ | Bitrate Δ | PSNR Δ
Kimono | -32.25 | 1.37 | -29.93 | 1.10
ParkScene | -21.20 | 0.86 | -16.86 | 0.65
Cactus | -24.58 | 0.87 | -23.29 | 0.69
BasketballDrive | -28.05 | 1.05 | -25.47 | 0.80
BQTerrace | -32.88 | 0.69 | -32.76 | 0.53
average | -27.79 | 0.97 | -25.66 | 0.75

## Slide 21: Class B/E, CS2 vs. Beta anchor
Sequence | BD low |  | BD high | 
 | Bitrate Δ | PSNR Δ | Bitrate Δ | PSNR Δ
Kimono | -33.85 | 1.53 | -32.59 | 1.31
ParkScene | -15.48 | 0.60 | -12.47 | 0.46
Cactus | -18.70 | 0.65 | -17.45 | 0.53
BasketballDrive | -30.28 | 1.21 | -28.37 | 0.98
BQTerrace | -27.24 | 0.63 | -25.03 | 0.47
average | -25.11 | 0.92 | -23.18 | 0.75
Sequence | BD low |  | BD high | 
 | Bitrate Δ | PSNR Δ | Bitrate Δ | PSNR Δ
Vidyo1 | -27.66 | 1.40 | -27.29 | 1.12
Vidyo3 | -20.37 | 1.00 | -20.37 | 0.84
Vidyo4 | -20.74 | 0.98 | -19.63 | 0.72
average | -22.93 | 1.13 | -22.43 | 0.89

## Slide 22: Class B/E, CS2 vs. Gamma anchor
Sequence | BD low |  | BD high | 
 | Bitrate Δ | PSNR Δ | Bitrate Δ | PSNR Δ
Kimono | -49.11 | 2.52 | -49.17 | 2.28
ParkScene | -37.00 | 1.65 | -33.12 | 1.43
Cactus | -40.72 | 1.65 | -38.79 | 1.45
BasketballDrive | -45.78 | 2.16 | -43.91 | 1.79
BQTerrace | -55.99 | 1.89 | -51.19 | 1.43
average | -45.72 | 1.98 | -43.24 | 1.67
Sequence | BD low |  | BD high | 
 | Bitrate Δ | PSNR Δ | Bitrate Δ | PSNR Δ
Vidyo1 | -44.39 | 2.60 | -45.39 | 2.17
Vidyo3 | -40.54 | 2.32 | -39.80 | 1.98
Vidyo4 | -40.99 | 2.26 | -42.65 | 1.89
average | -41.98 | 2.39 | -42.61 | 2.01

## Slide 23: Example of R-D performance

## Slide 24: Complexity in Encoding Process
Similar degree of encoding speed to JM anchor observed
  Reported performance results were obtained
    at around 2x encoding time than anchor with current functional algorithm simulator
    without using frame-level multi-pass coding
    same memory size as anchor
Complexity notice
  Computations for MB-level RDO decision due to increased number of motion partitions and prediction/coding modes
  Total memory requirement strongly depends on implementation, and can be expected via conventional codec implementation
◎

## Slide 25: Mode decision in I-picture
16x16 conventional MB size
All prediction modes and MB coding modes are determined by RDO
Chroma
  intra8x8 coding with adaptive DCT/DST
  Separate decision on pred. mode and transform basis type from luma process

## Slide 26: Mode decision in P/B-pictures
MB size: 64x64(class A/B) or 32x32(class C/D/E)
Motion estimation
  EPZS based
  ME cost: sum of SADs of all color components and motion bits
Mode and transform block-size/basis type
  jointly determined by RDO per each motion partition
Intra mode
  evaluated at partition having 16x16 block size, after finding the best MV and inter mode
◎

## Slide 27: Complexity in Decoding (Normative) Process
Could be within a few times complexity relative to AVC High Profile
Computational complexity factors
  In-loop Wiener filtering
  New intra predictions (less impact for inter pictures)
  SAD computation for adaptive direct MV derivation
Additional memory usage
  Intermediate storage for adaptive Wiener filter process
Additional memory bandwidth
  SAD computation for adaptive direct MV derivation
  Frame memory access during in-loop Wiener filtering

## Slide 28: Other characteristics
Random access & Delay characteristics
  Same degree as existing MPEG/ITU-T H.26x Standards by using conventional GOP structure
Error resilience
  Same degree as AVC in terms of context adaptive coding architecture
  Slice structure is possible as usual
Extensibility
  Supports of 4:4:4 coding, scalability, multi-view coding are equivalently possible as done in AVC extensions
Parallel processing
  Conventional approaches possible (Slice partitioning, MB-level pipeline process flow)
  In-loop Wiener filter requires more consideration
◎

## Slide 29: On simulation software
Pure standard C-language based code
  Clean implementation of extended MB size support
  No use of CPU dependent instructions
Multi-platform
  Windows (VisualStudio, gcc/cygwin)
  Linux (gcc)
  Mac OS X (gcc)
  Any UNIX workstations (gcc)
64bit operating system assumed
Modularized extensible design
  existing software modules in JM/KTA has been re-using without changing the code too much
◎

## Slide 30: Remarks
MB-based hybrid coding is still preferable for practical codec implementations
  Especially for next-generation UHDTV H/W codec up to 8Kx4K
MB size extension and in-loop Wiener filter tool should be considered as “starting point” of reference model
  has been verified by explorations in MPEG CfE / VCEG KTA study
  Significant coding gain achieved
Core experiments should consider:
  More performance enhancements with additional tools
  Further studies on performance-complexity trade-off
  Performance improvement for higher resolution video sources
Our codec simulator offers clean and extensible platform for future collaborative standardization work

## Slide 31: Summary of Proposed Tools
Entropy
Coding
MC
ME
－
Transform
Q
IQ
IT
Coding Control
Loop
Filter
Block
Division
Intra Pred
＋
Intra Pred
Memory
Frame
Memory
MV
Enhanced BALF
Multi-layer hierarchical
motion partition
Advanced
PMV
derivation
Adaptive block-size transform
& Adaptive DCT/DST
MB Size
Extension
New Intra Pred
modes
Video
Input
Bitstream
Improved direct mode
Simplified diagonal
motion partitions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: Summary of Proposed Tools
Category | Proposed Tool
MB size | Explicit MB size signaling
Transform | Adaptive block-size transform Adaptive DCT/DST
Entropy Coding | Advanced PMV derivation
Loop Filter | Enhanced BALF
Intra Prediction | Global planer prediction Iterative adjustment prediction
Motion representation | Multi-level hierarchical motion partitioning diagonal partition shapes Improved direct mode

## Slide 33: Conclusion
A new video coding algorithm for MPEG-HVC/ITU-T EPVC presented
  Up to 1dB Luma PSNR gain relative to Alpha/Beta anchor
  Up to 2dB Luma PSNR gain relative to Gamma anchor
  Could be within a few times decoder complexity to AVC HP
Recommendations
  To adopt the proposed coding algorithm framework into reference model, given the observed performance for higher resolution video
  To consider Super Hi-Vision source for further studies
    To be proposed by JCTVC-A023