## Slide 1: JCTVC-A123 NCTU CfP Proposal Parametric Overlapped Block Motion Compensation (POBMC)
National Chiao Tung University (NCTU)
Wen-Hsiao Peng, Yi-Wen Chen, Tse-Wei Wang, et al.
<number>
Notes: <number>

## Slide 2: Summary
Block-based hybrid codec based on KTA 2.4
  Enable EAIF, RDOQ, QALF, EMB, MDDT
  Incorporate POBMC, TMP-Skip
Compression performance
  22.04% saving, 0.90dB gain over Alpha
  21.93% saving, 0.91dB gain over Beta
  41.46% saving, 1.98dB gain over Gamma
<number>
Notes: <number>

## Slide 3: Summary
Complexity analysis
  Encoding time 2-100 hrs/case
  Decoding time w. YUV output
    (Ours : Alpha = 58 : 1)(Ours : Beta : Gamma= 75 : 1 : 1)
  Decoding time w/o YUV output
    (Ours : Alpha = 86 : 1)(Ours : Beta : Gamma= 128 : 1 : 0.9)
Highlighted aspects
  Multi-hypothesis motion compensation
  Error resilience, memory bandwidth
<number>
Notes: <number>

## Slide 4: Overlapped Block Motion Comp.
Prediction based on MVs of neighboring blocks
Weight vector varies with relative pixel position
   By symmetry, only 36 weight vectors!
<number>
LMMSE Estimate
Notes: <number>

## Slide 5: Problem
Weight vector depends on absolute pixel pos.
   Different pixels, different weight vectors
How to obtain? How to keep?
<number>
Notes: <number>

## Slide 6: Parametric Solution
To give a closed-form formula for weight vector
Signal Model & Assumption
  Block MV approximates motion at block center
  Motion difference follows normal distribution
<number>
Notes: <number>

## Slide 7: Parametric Solution
Under mild conditions
Interpretation
The optimal weight associated
with a block MV is inversely
proportional to the squared
distance from its block center
to the predicted pixel
<number>
Notes: <number>

## Slide 8: Extension to Bi-Prediction
Generate predictors using prediction modes of neighboring partitions
<number>
16
B1
B2
B3
B4
Notes: <number>

## Slide 9: Extension to Bi-Prediction
Combine resulting predictors using POBMC
<number>
Forward
Backward
Current Frame
S .
Notes: <number>

## Slide 10: POBMC Highlights
Multi-hypothesis motion compensation
  Improve prediction efficiency, error resilience
  Alleviate blocking artifacts
   Incur moderate increase in memory accesses
   Require to buffer motion information
Spatially varying weight vector
 Increase computational complexity
<number>
Notes: <number>

## Slide 11: Mode Decision
#1 & #2 iterations w/o AIF
#3 & #4 iterations w. AIF
Remark:
Segmentation decision and
motion search are carried
out based on BMC
<number>
Iter #1 MD
w/o POBMC
Iter #2 MD
with POBMC
EAIF
Iter #4 MD
with POBMC
DBF & ALF
AIF Decision
Iter #3 MD
w/o POBMC
Notes: <number>

## Slide 12: Compression Performance vs. Alpha
min/max/avg. | Y BD-rate(%) | Y BD-SNR(dB) | U BD-SNR(dB) | V BD-SNR(dB)
Class A | 14/23/19 | 0.79/0.99/0.88 | 0.19/1.51/0.86 | -1.99/-0.36/-1.17
Class B | 14/28/24 | 0.55/1.21/0.78 | -0..09/1.36/0.21 | -0.12/2.06/0.38
Class C | 21/25/23 | 0.95/1.24/1.08 | -0.28/0.21/-0.02 | -0.28/0.42/0.05
Class D | 13/31/19 | 0.69/1.28/0.88 | -0.38/0.22/-0.05 | -0.12/0.15/0.04
Overall | 13/31/22 | 0.55/1.28/0.90 | -0.38/1.51/0.17 | -1.99/2.06/-0.01

## Slide 13: Compression Performance vs. Beta
min/max/avg. | Y BD-rate(%) | Y BD-SNR(dB) | U BD-SNR(dB) | V BD-SNR(dB)
Class B | 15/35/28 | 0.56/1.58/0.96 | -0.35/-0.04/-0.21 | -0.50/-0.02/-0.24
Class C | 13/21/18 | 0.52/1.12/0.82 | -0.45/-0.09/-0.26 | -0.59/0.11/-0.29
Class D | 6/17/11 | 0.25/0.91/0.52 | -0.75/-0.05/-0.38 | -0.67/-0.01/-0.34
Class E | 27/36/32 | 1.19/1.87/1.46 | -0.15/0.63/0.15 | -0.87/0.27/-0.17
Overall | 6/36/22 | 0.25/1.87/0.91 | -0.75/0.63/-0.20 | -0.87/0.27/-0.26

## Slide 14: Compression Performance vs. Gamma
min/max/avg. | Y BD-rate(%) | Y BD-SNR(dB) | U BD-SNR(dB) | V BD-SNR(dB)
Class B | 35/59/46 | 1.53/2.57/1.95 | 0.25/0.49/0.29 | 0.07/0.71/0.36
Class C | 28/43/37 | 1.26/2.26/1.82 | 0.05/0.69/0.31 | 0.03/0.97/0.31
Class D | 19/55/34 | 1.05/2.40/1.67 | -0.12/0.42/0.14 | 0.02/0.39/0.25
Class E | 45/52/49 | 2.33/3.07/2.64 | 0.54/1.50/0.90 | 0.08/0.97/0.69
Overall | 19/59/41 | 1.05/30.7/1.98 | -0.12/1.50/0.37 | 0.02/0.97/0.38

## Slide 15: Complexity Analysis
Decoding Time Ratio | Decoding w/o Output |  | Decoding with Output | 
 | Constraint set 1 | Constraint set 2 | Constraint set 1 | Constraint set 2
Class A | 59.9 | N/A | 120.4 | N/A
Class B | 36.6 | 68.2 | 64.0 | 121.3
Class C | 46.2 | 66.7 | 87.9 | 145.5
Class D | 91.2 | 142.0 | 94.1 | 144.2
Class E | N/A | 24.8 | N/A | 107.3
Avg. | 58.5 | 75.4 | 86.2 | 128.2
Encoding Time (h:m:s) | Constraint set 1 | Constraint set 2
Class A | 36:36:51 | N/A
Class B | 54:47:51 | 66:32:58
Class C | 11:26:33 | 13:42:49
Class D | 3:42:2 | 4:33:0
Class E | N/A | 32:47:33
Avg. | 26:38:20 | 29:24:5

## Slide 16: Q & A
<number>
Notes: <number>