## Slide 1: Samsung and BBC response to Call for Proposals on Video Compression Technology
Ken McCann (Samsung)
Thomas Davies (BBC)
Notes: <number>

## Slide 2: Overview
Introduction
Algorithm Description
  Unit Definition
  Motion Representation
  Intra-frame Prediction
  Spatial Transforms
  In-loop Filtering
  Entropy Coding
Compression Performance
Complexity Analysis
Conclusions
Notes: <number>

## Slide 3: Introduction: Samsung/BBC Coding Framework
This presentation covers
  JCTVC-A124: Samsung Response to CfP
  JCTVC-A125: BBC response to CfP
The Samsung/BBC coding framework provides the ability to trade off complexity and compression efficiency
In our responses to the CfP we demonstrate two key operating points
  A125: low-complexity operating point, with comparable complexity to H.264/AVC but better compression efficiency
    Average efficiency about 30% better than Alpha and Beta anchors
    Decoding time about 0.6 to1.3 times that of JM17.0
  A124: high-performance operating point, giving even higher compression efficiency with a moderate increase in complexity over H.264/AVC
    Average efficiency about 40% better than Alpha and Beta anchors
    Decoding time about 0.9 to 2.4 times that of JM17.0
Notes: <number>

## Slide 4: Introduction: Key Features
Flexible block structure to support arbitrary min & max unit sizes
  Coding Unit (CU)
  Prediction Unit (PU)
  Transform Unit (TU)
Consistent syntax representation, independent of size
Asymmetric motion partitions
Greater than ¼ pixel motion accuracy with new interpolation filter
Large integer transforms up to 64x64
New rotational transform
New motion vector prediction method
New in-loop filtering methods
New intra-coding prediction methods
New entropy coding with explicit scan order signaling
Notes: <number>

## Slide 5: Introduction: Building Blocks in Decoder

## Slide 6: Unit Definition: Coding Unit (CU)
CU is the basic processing block
  Used for quad-tree based segmentation of regions
  Plays a similar role to macroblock
  Can take various sizes
    Always power of 2 size
    Always square shape
Range of allowed sizes specified in Sequence Parameter Set
  Largest CU (LCU)
  Maximum hierarchical depth
  Easily adapted for various applications
Recursive structure with split flag
  Single 2Nx2N or four NxN
LCU size = 128 (N=64), maximum hierarchical depth = 5

## Slide 7: Unit Definition: Benefits of CU structure
Supports large CU size
  Virtually no limit to maximum size
  Maximum of 128x128 used in CfP submissions
Flexible structure
  Can be optimized for content, device or application
Size-independent syntax
  Each CU has an identical syntax regardless of its size
  Reduces complexity of parsing
Notes: <number>

## Slide 8: Unit Definition: Prediction Unit (PU)
Prediction Unit (PU) is the basic unit for prediction
  Largest allowed PU size is equal to the CU size
  Other allowed PU sizes depend on prediction type
    Includes asymmetric splitting options for inter-prediction
Example of 128x128 CU
  Skip: PU = 128x128
  Intra: PU = 128x128 or 64x64
  Inter: PU = 128x128, 128x64, 64x128, 64x64, 128x32, 128x96, 32x128 or 96x128
Asymmetric splitting

## Slide 9: Unit Definition: Transform Unit (TU)
Transform Unit (TU) is the basic unit for transform and quantization
  May exceed size of PU, but not CU
Only two TU options are allowed, signalled by transform unit size flag
  Transform unit size flag = 0  2Nx2N - same as CU
  Transform unit size flag = 1  square units of smaller size
    NxN when PU splitting is symmetric
    N/2xN/2 when PU splitting is asymmetric

## Slide 10: Unit Definition: Relationship of CU, PU and TU

## Slide 11: Motion: Asymmetric Motion Partition (AMP)
Asymmetric motion partition (AMP)
  Describes various object motions efficiently without further splitting
  Computationally efficient compared to non-rectangular partitions
    Motion estimation, motion compensation, transform, etc.
PU types for AMP
2NxnU
2NxnD
nRx2N
nLx2N
  Examples of use of AMP (from RaceHorses in Class C)
Note: Not included in A125

## Slide 12: Motion: Advanced Motion Vector Prediction (AMVP)
Advanced Motion Vector Prediction (AMVP)
  Extension of motion vector competition techniques
Explicit motion vector predictor signaling
  New candidate motion vectors (motion vector candidates = {median(a’, b’, c'), a’, b’, c’, temporal predictor})
  Three spatial motion vectors (a’, b’, c’)
    The first available one for each group (inter mode & same ref. idx)
    Groups are the above group {a0, a1,…, ana}, the left group {b0, b1,…, bnb } and the corner {c,d,e}
  Median motion vector of three spatial motion vectors
  Temporal motion predictor using one colocated motion vector
Signaling overhead is minimized
  Candidate order is adapted according to PU splitting
  Unnecessary or duplicated motion vectors are removed
a0
a1
ana
b0
b1
bnb
c
d
e

## Slide 13: Motion: Improved Skip and Direct modes
Improved Skip and Direct provide intermediate complexity modes
  Skip and direct modes are enabled for both P and B slices
    Differentiated only by whether texture information is sent or not
    The motion of skip and direct modes is derived by AMVP
  The motion vector prediction information is sent
    AMVP index information is sent to determine motion predictor
  There are three kinds of direct mode in B slice
    Two uni-directional direct modes and a bi-directional direct mode

## Slide 14: Motion: DCT-based interpolation filter (DIF)
DIF provides an elegant method of high-accuracy interpolation
  Direct fractional pixel generation replaces Wiener + bi-linear combination
    Only one filtering is used to generate pixels at any accuracy
    Mathematically, it is a forward DCT followed by inverse DCT with shifted argument of basis functions
    Supports any accuracy & filter length
  Implemented as a multiplication-free spatial domain filter
merged

## Slide 15: Motion: High Accuracy Motion (HAM)
High Accuracy Motion (HAM) provides
  Higher motion accuracy than ¼ pel
Proposal uses a refinement representation
  Motion vector (lower accuracy, e.g. ¼ pel) + refinement (0, -1, +1)
    1 bit overhead when refinement not used
      Smaller overhead to always 1/8 design
      No negative gain sequences
    Prediction is used only for lower accuracy MV
      To prevent randomness of MVD
      Smaller MVD magnitude
Current design uses 1/12 pel accuracy
  More compact coverage than 1/8 pel
Note: Not included in A125

## Slide 16: Intra: Arbitrary Direction Intra (ADI)
Arbitrary Direction Intra (ADI) provides improved directional prediction
  Prediction of any direction is defined by the delta value (dx, dy) from current pixel to the corresponding reference pixel: Y[x, y] = Y[x-dx, y-dy]
  Left down pixels are possible reference pixels
  Filtering of boundary reconstructed pixels before prediction
Number of prediction modes dependent on PU size
  Up to 33 prediction modes
Prediction generation with arbitrary direction
PU size | Number of modes
4x4 | 9
8x8 | 9
16x16 | 33
32x32 | 33
64x64 | 5
128x128 | 5

## Slide 17: Intra: Multi-Parameter Intra (MPI)
Multi-Parameter Intra (MPI) provides more natural prediction patterns
  Uses a 4-point filter for each pixel inside the predicted block
Note: Not included in A125
pred’[x,y] = (pred[x,y]+pred[x-1,y]+ pred[x,y-1]+ pred[x,y+1] +2 ) >>2
Notes: <number>

## Slide 18: Intra: Color Component Correlation Prediction (CCCP)
CCCP improves chroma intra prediction by using information inferred from reconstructed luma samples
  Chroma intra prediction based on segmentation map from luma samples
  Capable of generating complex object shapes
Note: Not included in A125
Original Chroma signal
Prediction of H.264/AVC
Prediction of proposed method (CCCP replace DC mode)

## Slide 19: Intra: Pixel based template matching (PTM)
Pixel based template matching (PTM) improves intra prediction in regions with repeated regular patterns
  L-shaped search region, including already predicted samples in template
Want to predict PR
  Use T0, T1, T2 as template of size 6x6
    Total 27 points are searched
  Previously predicted pixels are reused
  as candidate and template
  Choose pixel C if it gives min. SAD
Note: Not included in A125

## Slide 20
Combined Intra Prediction (CIP) improves other prediction methods by allowing pixel-by-pixel adaptation
In A125, ADI predictions are combined with a local mean within a block
Forward prediction using the local mean is open-loop
  any noise is damped by the combination factors and more than compensated by a better, adaptive prediction
Note: Not included in A124
Intra: Combined Intra Prediction (CIP)

## Slide 21: Transform: Large Transform
The proposal extends transform to larger sizes
  16x16, 32x32 and 64x64
Minimising complexity is important in large transform design
  Chen’s fast DCT has been chosen for this proposal
  Reduced implementation complexity due to the regular butterfly design
  Approximation of values from sinusoidal functions into dyadic rationals
    Can be implemented using additions and shifts only

## Slide 22: Transform: Rotational Transform (ROT)
The Rotational Transform (ROT) provides a way to rotate DCT basis
  Designed as 2nd tranform after DCT: can be applied with any transforms
  Similar to directional transform, but simpler approach
Implementation cost is minimized in this proposal by
  Allowing only four possible rotation angles
  Excluding areas outside of the 8x8 low frequency area – advantages from transform domain processing
Note: Not included in A125

## Slide 23: Transform: Logical transform (LOT)
The Logical Transform (LOT) allows the input residual size to be bigger than the maximum physical transform size
  Roughly equivalent to taking only low-frequency components of DCT
  Beneficial in coding smooth regions
  Wavelet transform is followed by down-sampling and conventional transform
    only LL-band signals are transformed by spatial transform
Note: Not included in A125
LL band
(32x32)
Coefficients
(32x32)
Large coding unit (128x128)
Physical Transform
(32x32)
2nd level
Wavelet transform

## Slide 24: Loop Filtering: Overview of In-loop filtering
The in-loop filter in A124 is a combination of several spatial processes
The in-loop filter in A125 is only the Deblocking filter
  - Same filters and boundary strength decision as H.264/AVC
Deblocking
filter
Blocking artifact
Edge correction
Reduce MSE
PDF matching
Range adjustment
Blocking artifact

## Slide 25: Loop Filtering: CU-synchronized ALF
CU-synchronized Adaptive Loop Filter (ALF) further reduces distortion
  On/off partition reuses CU boundaries - no need to transmit partition info.
    Much simpler to estimate in encoder-side
    Multi-level merging of CU boundary is supported
    CU-synchronized ALF process can be implemented in decoder-side
Note: Not included in A125
Initial stage
After first merging
After second merging
CU boundary
If best RD cost
On/off signal is sent for each partition

## Slide 26: Loop Filtering: Extreme correction (EXC)
Extreme correction (EXC) is useful to compensate distortion for specific pixel class, e.g. object edge
  Extreme type is determined by comparison of current pixel value with upper, lower, left and right neighbors (for non-boundary pixels)
  Location of points to be corrected are determined by decoder
  Correction values are calculated for 6 types of extreme points as mean error among the frame
Note: Not included in A125
Extreme type derivation
for value of pixel P using
4 neighbours
C
U
L
R
D

## Slide 27: Loop Filtering: Band Correction (BDC)
Band Correction (BDC) allows the correction of systematic errors, related to specific ranges of pixel values
  Conceptually similar to PDF matching process between two signals
  Band may be defined by the p most significant bits of pixel value
  Integer correction values for each band are determined while coding
  Correction values for each band are coded in slice header
Note: Not included in A125
Band number | 0 | 1 | … | 15
Reconstructed pixel value band | 0 - 255 | 256 - 511 | … | 3840 - 4095
Correction value | 6 | -4 | … | 8
Example: Band derivation by 4 most significant bits for 12-bit depth of pixel values and correction values (PeopleOnStreet 1st frame).

## Slide 28: Loop Filtering: Content Adaptive Dynamic Range (CADR)
Content Adaptive Dynamic Range (CADR) gives improved accuracy for internal calculations by exploiting known limits to luma samples
  Without requiring increased bit depth – useful for bit-depth limited H/W
For example, clipped BT.709 luma samples lie in the range [16, 235]
  CADR mapping expands dynamic range to [0,255]
Note: Not included in A125
sample dynamic range
enlarged dynamic range
16
235
255
0

## Slide 29: Entropy Coding: SBAC
The proposal uses Syntax-based context-adaptive binary arithmetic coding (SBAC)
  Coding engine is based on JPEG Annex D
  Coding performance appears to be slightly better than H.264/AVC’s CABAC
  Overall architecture is similar to CABAC, but the details of each step are different

## Slide 30: Entropy Coding: Adaptive Coefficient Scanning (ACS)
Adaptive Coefficient Scanning (ACS) improves the coding performance when using large transform blocks
Allows scanning pattern to be selected by encoder:
  Conventional zig-zag
  Horizontal scan
  Vertical scan
Only signalled when there are non-DC coefficients
zig-zag scan
horizontal scan
vertical scan

## Slide 31: Compression Perfomance (A125)
Average bit-saving 31.95% for CS1 and 29.97% for CS2
  Best classes: Class B@CS1 and Class E@CS2
  Worst class: Class D@CS2
  Best sequence: BQTerrace@CS2 (50.55%)
  Worst sequence: RaceHorses@CS2 (13.31%)
 | Class A | Class B | Class C | Class D | Class E | Average
CS1 | 27.24 | 36.85 | 33.04 | 27.07 |  | 31.95
CS2 |  | 35.06 | 26.19 | 22.23 | 36.85 | 29.97

## Slide 32: Compression Perfomance (A124)
Average bit-saving 39.49% for CS1 and 39.48% for CS2
  Best class: Class E@CS2
  Worst class: Class D@CS2
  Best sequence: BQTerrace@CS2 (60.62%)
  Worst sequence: RaceHorses@CS2 (21.59%)
 | Class A | Class B | Class C | Class D | Class E | Average
CS1 | 35.21 | 43.29 | 39.94 | 36.45 |  | 39.49
CS2 |  | 43.66 | 35.58 | 32.16 | 47.48 | 39.48

## Slide 33: Complexity Analysis (A125)
Decoding time using PC with fast SATA drive
  Average decoding time about 1.3 times that of JM17.0
Decoding time using PC with SCSI drive
  Average decoding time about 0.6 times that of JM17.0
JM17.0 | Class A | Class B | Class C | Class D | Class E | Average
CS1 | x1.26 | x0.94 | x1.05 | x1.38 |  | x1.16
CS2 |  | x1.14 | x1.32 | x1.58 | x1.35 | x1.35
JM17.0 | Class A | Class B | Class C | Class D | Class E | Average
CS1 | X0.30 | X0.31 | X0.53 | X1.13 |  | X0.57
CS2 |  | X0.32 | X0.49 | X1.21 | X0.39 | X0.60

## Slide 34: Complexity Analysis (A124)
Decoding time using PC with fast SATA drive
  Average decoding time about 2.4 times that of JM17.0
Decoding time using PC with SCSI drive
  Average decoding time about 0.9 times that of JM17.0
JM17.0 | Class A | Class B | Class C | Class D | Class E | Average
CS1 | X0.64 | X0.61 | X0.79 | X1.45 |  | X0.87
CS2 |  | X0.62 | X0.85 | x1.51 | X0.48 | X0.87
JM17.0 | Class A | Class B | Class C | Class D | Class E | Average
CS1 | x3.01 | x2.26 | x1.93 | x2.45 |  | x2.41
CS2 |  | x2.67 | x2.20 | x2.63 | x1.64 | x2.29

## Slide 35: Further improvements after submission (A124)
Average bit-saving is now 41.58% for CS1
  2.09% better than in submitted proposal
Class | Sequence | Submitted | Improved | Delta
A | Traffic PeopleOnStreet | 40.59 29.84 | 42.99 31.20 | 2.40 1.36
B | Kimono ParkScene Cactus BasketballDrive BQTerrace | 44.42 32.96 40.78 44.21 54.06 | 45.80 36.09 43.28 45.11 55.96 | 1.37 3.13 2.49 0.90 1.90
C | BasketballDrill BQMall PartyScene RaceHorses | 43.09 39.69 41.13 35.86 | 44.56 41.94 43.36 37.11 | 1.47 2.25 2.23 1.25
D | BasketballPass BQSquare BlowingBubbles RaceHorses | 30.55 54.19 33.97 27.08 | 33.45 56.92 36.95 28.95 | 2.90 2.73 2.98 1.86
Class | Submitted | Improved | Delta
A | 35.21 | 37.09 | 1.88
B | 43.29 | 45.25 | 1.96
C | 39.94 | 41.74 | 1.80
D | 36.45 | 39.07 | 2.62
ALL | 39.49 | 41.58 | 2.09
Skip & direct mode using HAM
New deblocking filter design
Bi-directional prediction refinement
Newly added tools

## Slide 36: Conclusions
The Samsung/BBC coding framework has been described in some detail
In our responses to the CfP we demonstrated two key operating points
  A low-complexity operating point, with comparable complexity to H.264/AVC and better compression efficiency
    Average efficiency about 30% better than Alpha and Beta anchors
    Decoding time about 0.6 to 1.3 times that of JM17.0
  A high-performance operating point, giving even higher compression efficiency with a moderate increase in complexity over H.264/AVC
    Average efficiency about 40% better than Alpha and Beta anchors
    Decoding time about 0.9 to 2.4 times that of JM17.0
The Samsung/BBC coding framework should be considered to be a strong candidate for the Test Model that will be used as the basis of the Core Experiments in the next phase of HVC standardization