## Slide 1: AHG7: MCTS Context information SEI Message
N. Ouedraogo, J. Taquet, F. Denoual, F. Mazé
28/03/2017

## Slide 2: Problem statement
Context
  temporal motion constrained tile sets (MCTS) SEI message allows to signal independently decodable tile sets
    When mc_all_tiles_exact_sample_value_match_flag=1
    Or when mc_exact_sample_value_match_flag[ i ] =1
Problem
  The current motion constrained tile sets (MCTS) SEI messages do not guarantee that a tile set will always reconstruct correctly in a different decoding context
    E.g., when it is decoded with a different neighborhood than during its encoding
    Particularly if we do not want to deactivate all encoder optimization for MCTS
  Depending on encoder choices and potential neighborhood tile sets at decoding time, the reconstruction may not always be correct
1/7

## Slide 3: Example of scenarios
mcts_00
Video 0
extraction
encoding
mcts_00
mcts_01
mcts_02
mcts_03
decoding
Video 0
combination
mcts_00
mcts_11
mcts_12
mcts_03
mcts_00
mcts_01
mcts_02
mcts_03
mcts_10
mcts_11
mcts_12
mcts_13
Quality 0
encoding
Quality 1
encoding
combination
Video 0
Video 1
mcts_00
mcts_01
mcts_02
mcts_03
mcts_10
mcts_11
mcts_12
mcts_13
encoding
encoding
decoding
Scenario 1: Extract one or more tiles from a single stream
Scenario 2: Combined tiles encoded with different quality
Scenario 3: Combine and shuffle tiles possibly from different streams
mcts_01
mcts_10
mcts_03
mcts_12
decoding
decoding ok
2/7

## Slide 4: Issue with motion prediction from border extension
3/7
mcts_00
mcts_02
mcts_03
mcts_01
Frame border extension
mcts_01
Frame border extension
mcts_10
mcts_12
mcts_03
mcts_01
Frame border extension
Frame border extension
mcts_10
mcts_12
mcts_03
mcts_01
extraction
decoding
mcts_00
mcts_02
mcts_03
mcts_01
Frame border extension
mcts_10
mcts_12
mcts_13
mcts_11
Frame border extension
combination
decoding
decoding
X
combination
mcts_00
mcts_02
mcts_03
mcts_01
Frame border extension
mcts_10
mcts_12
mcts_13
mcts_11
Frame border extension

## Slide 5: Issue with temporal motion predictors (1/2)
4/7
mcts_00
mcts_02
mcts_03
mcts_01
Temporal motion
predictor list derivation
List 1
bottom right is available
in co-located block
mcts_00
Temporal motion
predictor list derivation
List 2
bottom right
is not available in co-located block
Select a Motion Vector predictor
The derivation process
is constrained so that selected
predictor is the same in both lists
Encoder derivation process when temporal motion predictor from outside tile for MCTS tile sets
MV Predictor

## Slide 6: Issue with temporal motion predictors (2/2)
mcts_10
mcts_12
mcts_03
mcts_01
Temporal motion
predictor list derivation
List 3
Decode MV P
mcts_00
mcts_02
mcts_03
mcts_01
Temporal motion
predictor list derivation
List 1
Temporal motion
predictor list derivation
List 2
mcts_00
Decode MV P
Decode MV P
X
Decoder derivation process depending on combination of MCTS
5/7
MV Predictor
MV Predictor
MV Predictor

## Slide 7: Other encoder choices that could be signaled
MCTS and slice encapsulation
  MCTS is independently accessible if all the coding tree units of the tile set are contained in one or more slice AND this one or more slice contains only coding tree units of this tile set
  We may also signal when one or more slice may include coding unit of tile that do not pertain to the tile set
  Thus the tile set extraction process would be informed to remove bytes corresponding to coding tree units not belonging to this tile set
Loop filter across MCTS
  We may signal to the tile set extraction process when inter-prediction may use or not sample from the margin modified by loop filters around the tile boundaries
  If samples from this margin are used for inter-prediction, the tile set extraction process shall not use a tile setup for which the tile set is decoded with other tile sets different from the tile sets at encoding
6/7

## Slide 8: Proposal: mcts_context_info SEI message
New SEI message
  To signal more information on the encoding context of MCTS
    specifies inter prediction constraints and slice encapsulation
Advantages
  decoder and application using a tile set are informed on encoder choices
  decoder and application can deduce which scenarios of use are possible with a given tile set
7/7
mcts_context_info( payloadSize ) { | Descriptor
num_mcts_context_in_minus1 | ue(v)
for( i = 0; i <= num_mcts_context_minus1; i++ ) { | 
mcts_context_id [i ] | ue ( v )
mcts_slice_encapsulated_flag [ i ] | u(1)
mcts_motion_vectors_over_pic_boundaries [ i ] | u(1)
if ( loop_filter_across_tiles_enabled_flag ) { | 
mcts_exclude_loop_filter_margin[ i ] | u (1)
} | 
mcts_temporal_motion_vector_predictor_flag [ i ] | u(1)
} | 

## Slide 9: Thank you for your attention.

## Slide 10: Backup slides

## Slide 11: Detailed syntax
D.3.45 MCTS context information SEI message syntax
The motion-constrained tile sets context information SEI message indicates context information for motion-constrained tile sets. In particular, it specifies the number of slices used for motion-constrained tile sets and inter prediction constraints.
Let a set of pictures associatedPicSet be the pictures from the access unit containing the motion-constrained context information SEI message, inclusive, up to but not including the first of any of the following in decoding order:
– The next access unit, in decoding order, that contains a temporal motion-constrained tile sets SEI message
– The next IRAP picture with NoRaslOutputFlag equal to 1, in decoding order.
– The next IRAP access unit, in decoding order, with NoClrasOutputFlag equal to 1.
The scope of the motion-constrained tile set context information SEI message is the set of pictures associatedPicSet.
When a motion-constrained tile set context information SEI message is present for any picture in associatedPicSet, a temporal motion-constrained tile set SEI message shall be present for the first picture of associatedPicSet in decoding order and may also be present for other pictures of associatedPicSet. The mcts_context_id[ ] values of the motion-constrained tile sets context information SEI message shall have a corresponding equal mcts_id[] value in the associated temporal motion-constrained tile set context SEI message with either mc_all_tiles_exact_sample_value_match_flag or mc_exact_sample_value_match_flag equal to 1.
The motion-constrained tile set context information SEI message shall not be present for any picture in associatedPicSet when tiles_enabled_flag is equal to 0 for any PPS that is active for any picture in associatedPicSet.
The motion-constrained tile set context information SEI message shall not be present for any picture in associatedPicSet unless every PPS that is active for any picture in associatedPicSet has the same values of the syntax elements num_tile_columns_minus1, num_tile_rows_minus1, uniform_spacing_flag, column_width_minus1[ i ], and row_height_minus1[ i ].
NOTE 1 – This constraint is similar to the constraint associated with tiles_fixed_structure_flag equal to 1, and it may be desirable for tiles_fixed_structure_flag to be equal to 1 when the motion-constrained tile sets context information SEI message is present (although this is not required).
When more than one motion-constrained tile sets context information SEI message is present for the pictures of associatedPicSet, they shall contain identical content.
The number of temporal motion-constrained tile sets SEI messages in each access unit shall not exceed 5.

## Slide 12: Detailed syntax
num_mcts_context_minus1 plus 1 indicates the number of context information specified in the motion constrained tile sets context information SEI message. The value of num_mcts_context_minus1 shall be in the range of 0 to 232 – 2, inclusive.
mcts_context_id [ i ] identifies the i-th tile set with mcts_id equal to mcts_context_id [ i ] associated to the i-th context information set. The value of mcts_context_id[ i ] shall be in the range of 0 to 232 − 2, inclusive.
mcts_context_info( payloadSize ) { | Descriptor
num_mcts_context_in_minus1 | ue(v)
for( i = 0; i <= num_mcts_context_minus1; i++ ) { | 
mcts_context_id [i ] | ue ( v )
mcts_slice_encapsulated_flag [ i ] | u(1)
mcts_motion_vectors_over_pic_boundaries [ i ] | u(1)
if ( loop_filter_across_tiles_enabled_flag ) { | 
mcts_exclude_loop_filter_margin[ i ] | u (1)
} | 
mcts_temporal_motion_vector_predictor_flag [ i ] | u(1)
} | 

## Slide 13: Detailed syntax
mcts_slice_encapsulated_flag [ i ] equal to 1 specifies that all the coding tree units of the tile set with mcts_id equal to mcts_context_id [ i ] are contained in one or more slice. In addition, this one or more slice contains only coding tree units of the tile sets with mcts_id equal to mct_context_id [ i ]. Otherwise when equal to 0, the one or more slice may include coding unit of tile set with mcts_id different than mcts_context_id [ i ]
NOTE – When mcts_slice_encapsulated_flag [ i ] is equal to 0, the tile set extraction process may remove bytes corresponding to coding tree unit belonging to another tile set to obtain a NAL unit containing only data related to the tile set with mcts_id equal to mcts_context_id [ i ].
mcts_context_info( payloadSize ) { | Descriptor
num_mcts_context_in_minus1 | ue(v)
for( i = 0; i <= num_mcts_context_minus1; i++ ) { | 
mcts_context_id [i ] | ue ( v )
mcts_slice_encapsulated_flag [ i ] | u(1)
mcts_motion_vectors_over_pic_boundaries [ i ] | u(1)
if ( loop_filter_across_tiles_enabled_flag ) { | 
mcts_exclude_loop_filter_margin[ i ] | u (1)
} | 
mcts_temporal_motion_vector_predictor_flag [ i ] | u(1)
} | 

## Slide 14: Detailed syntax
mcts_motion_vectors_over_pic_boundaries [ i ] when equal to 0 indicates that no sample outside the picture boundaries and no sample at a fractional sample position for which the sample value is derived using one or more samples outside the picture boundaries is used for inter prediction of the i-th tile set with mcts_id equal to mcts_context_id [ i]. Otherwise when equal to 1 the inter prediction may use sample outside one picture boundary and sample at a fractional sample position for which the sample value is derived using one or more samples outside one picture boundary when the picture boundary is shared with the i-th tile set with mcts_id equal to mcts_context_id[ i ].
NOTE: When mcts_motion_vectors_over_pic_boundaries [ i ] is equal to 1, tile set extraction process shall not use a tile setup for which the tile set with mcts_id equal to mcts_context_id[i] is not sharing the same boundaries with the picture boundaries.
mcts_context_info( payloadSize ) { | Descriptor
num_mcts_context_in_minus1 | ue(v)
for( i = 0; i <= num_mcts_context_minus1; i++ ) { | 
mcts_context_id [i ] | ue ( v )
mcts_slice_encapsulated_flag [ i ] | u(1)
mcts_motion_vectors_over_pic_boundaries [ i ] | u(1)
if ( loop_filter_across_tiles_enabled_flag ) { | 
mcts_exclude_loop_filter_margin[ i ] | u (1)
} | 
mcts_temporal_motion_vector_predictor_flag [ i ] | u(1)
} | 

## Slide 15: Detailed syntax
mcts_exclude_loop_filter_margin[ i ] when equal to 1 indicates that no sample inside the margin around the tile boundaries which are modified by loop filters and no sample at a fractional sample position for which the sample value is derived using one or more samples from this margin is used for inter prediction of the i-th tile set with mcts_id eqal to mcts_context_id [ i ]. Otherwise when equal 0, the inter prediction may use sample within this margin.
NOTE: When mcts_exclude_loop_filter_margin[i] is equal to 0, tile set extraction process shall not use a tile setup for which the tile set with mcts_id equal to mcts_context_id[i] is decoded with other tile set different from the tile set at encoding.
mcts_context_info( payloadSize ) { | Descriptor
num_mcts_context_in_minus1 | ue(v)
for( i = 0; i <= num_mcts_context_minus1; i++ ) { | 
mcts_context_id [i ] | ue ( v )
mcts_slice_encapsulated_flag [ i ] | u(1)
mcts_motion_vectors_over_pic_boundaries [ i ] | u(1)
if ( loop_filter_across_tiles_enabled_flag ) { | 
mcts_exclude_loop_filter_margin[ i ] | u (1)
} | 
mcts_temporal_motion_vector_predictor_flag [ i ] | u(1)
} | 

## Slide 16: Detailed syntax
mcts_temporal_motion_vector_predictor_flag [ i ] when equal to 0 indicates that the candidates list generation process for temporal motion vector prediction is constrained such that the predictor selected in the list of candidates is never the bottom right motion vector when the bottom right motion vector of the collocated block is outside the i-th tile set with mcts_id equal to mcts_context_id [ i ]. Otherwise when equal to 1 indicates that the derivation process for temporal motion vector prediction is constrained such that the decoding of the motion predictor is the same when decoded with or without the i-th tile set with mcts_id equal to mcts_context_id [ i ].
NOTE: When mcts_temporal_motion_vector_predictor[ i ] is equal to 1, tile set extraction process shall not use a tile setup for which the tile set with mcts_id equal to mcts_context_id[i] is decoded with other tile sets different from the tile sets at the encoding.
mcts_context_info( payloadSize ) { | Descriptor
num_mcts_context_in_minus1 | ue(v)
for( i = 0; i <= num_mcts_context_minus1; i++ ) { | 
mcts_context_id [i ] | ue ( v )
mcts_slice_encapsulated_flag [ i ] | u(1)
mcts_motion_vectors_over_pic_boundaries [ i ] | u(1)
if ( loop_filter_across_tiles_enabled_flag ) { | 
mcts_exclude_loop_filter_margin[ i ] | u (1)
} | 
mcts_temporal_motion_vector_predictor_flag [ i ] | u(1)
} |