## Slide 1: JCTVC-AA0035: Omnidirectional projection indication SEI message geometry_type and projection_type changes
Jill Boyce

## Slide 2: Overview
  Propose to add functionality to the omnidirectional projection information SEI message in JCTVC-Z1005
  Add code values to the geometry_type and projection_type syntax elements
  Geometry_type: add value for cubical shape
  Projection_type: add values for cube map projection and rectilinear projection
  Change their semantics to clarify the distinction between a projection format used for coding a video sequence from the geometry used for rendering
  The “viewport mode” functionality proposed in JCTVC-Z0034 can also be provided with the proposed changes, without requiring any additional syntax

## Slide 3: Background: syntax in JCTVC-Z1005 No proposed change to syntax
omnidirectional_projection_indication( payloadSize ) { | Descriptor
omnidirectional_projection_indication_cancel_flag | u(1)
if( !omnidirectional_projection_indication_cancel_flag ) { | 
omnidirectional_projection_information_persistence_flag | u(1)
geometry_type | u(5)
sub_geometry_flag | u(1)
projection_type | u(8)
if( geometry_type = = 1 && sub_geometry_flag = = 1 && projection_type = = 1 ) { | 
yaw_center | i(16)
pitch_center | i(16)
roll_center | i(16)
yaw_range | u(16)
pitch_range | u(16)
} | 
} | 
} | 

## Slide 4: Why cube map?
Cube map has been proposed for tile-based streaming approaches using motion-constrained tile sets
  More consistent size relationship with rectilinear viewports than for equirectangular projection
Cubic rendering supported by modern GPUs
A particular cube map layout would need to be selected

## Slide 5: Distinction between projection format used for coding and rendering geometry
360Lib software calculations of PSNR-based metrics assume spherical rendering, even when cube map projection is used for coding
For some sequences, cube map projection format can be coded more efficiently than equirectangular projection format
Signaling projection format separate from recommended rendering geometry allows selection of best projection based on coding efficiency, or to support tile-based decoding approaches

## Slide 6: Cube map layout examples

## Slide 7: Example content in ERP and CMP

## Slide 8: Rectilinear viewport
Viewer selects viewport position via HMD orientation
360Lib software generates rectilinear viewport based upon spherical rendering
Using cubical rendering can cause discontinuities at face boundaries
Content creator can pre-compensate for this effect

## Slide 9: Viewport from cubical rendering may include 3 cube faces Bend of straight object, with angle at face edge

## Slide 10: Rectilinear viewport support
JCTVC-Z0034 proposed SEI message support for a “viewport mode” indicating the size and position of a rectilinear viewport that had been extracted from spherical video
  Position needed because of dynamically moving HMD and system latency
The JCTVC-Z1005 already provides indication of size and position of region of a sphere that the video represents
Adding a “rectilinear” code value to projection_type, accomplishes the proposed functionality, without any syntax change
  Size of region when rectilinear projection used limited to <180° in each dimension

## Slide 11: Viewport Mode
MANE-assisted distribution system can offload decoding compute resources from client and reduce network bandwidth by extracting a viewport based on the Head Mounted Display (HMD) position

## Slide 12: Region with yaw, pitch offset (from JCTVC-Z1005)

## Slide 13: Summary of syntax for proposed features
geometry_type | sub_geometry_flag | projection_type | description
0 (sphere) | 0 | 0 (ERP) | ERP content, rendered on a sphere, filling the entire sphere
0 (sphere) | 1 | 0 (ERP) | ERP content, rendered on a sphere, filling a portion of the sphere
0 (sphere) | 1 | 2 (rectilinear) | rectilinear region which had been extracted from a sphere (“viewport mode” from JCTVC-Z0034), rendered on a sphere, filling a portion of the sphere
1 (cube) | 0 | 1 (cube map) | cube map projection content, should be rendered on a cube
0 (sphere) | 0 | 1 (cube map) | cube map projection content, should be rendered on a sphere

## Slide 14: Conclusion
Proposed code values and semantics changes to the omnidirectional projection indication SEI message provide additional features, without syntax changes
  Add cube map projection and cubic rendering
  Differentiate between rendering geometry and coding projection
  Add rectilinear projection type