## Slide 1: JCTVC-AA0036r1: Omnidirectional recommended viewport SEI Message
Jill Boyce

## Slide 2: Overview
  SEI message is proposed for HEVC and AVC to indicate omnidirectional ROI
    Allows the encoder to indicate one or more “director’s views,” which are recommended rectangular viewports in a rectilinear projection from the coded spherical video
  MPEG OMAF AHG on ROI adopted signaling for this functionality to OMAF draft at Geneva meeting
  Previously proposed in JCTVC-Z0034, as “ROI Mode”
    Excerpt from Meeting Notes: “General support was expressed for this first proposed mode, as a distinct SEI message. It seems likely to be adopted at the next meeting, given adequate coordination and potential refinement.
    “
The r1 version of this document adds capability to send multiple recommended viewport regions with ids, and to add a roll center syntax element.

## Slide 3: ROI Mode
When viewing omnidirectional video, the viewer typically views only a small portion of the full 360º x 180º video at a given time.
  A viewer may miss the “most interesting” area of the video
  Content creator can recommend a region to view
  Viewer can follow the recommendation or override it
Syntax needed to indicate position and size of recommended region
  To indicate rectangular rectilinear region:
    Spherical center position (yaw, pitch, roll)
    Range of yaw and pitch angles of a rectangular region in a rectilinear projection of a sphere

## Slide 4: Related OMAF draft support
OMAF draft supports functionality to indicate a ROI
The region is bounded by two horizontal “great circles” and two vertical “great circles,” where a great circle is a diameter of the sphere
Corresponds to a rectangular region in a rectilinear viewport
Figure from Emmanuel Thomas on OMAF ROI AHG reflector

## Slide 5: Proposed SEI message syntax
omnidirectional_viewport( payloadSize ) { | Descriptor
omnidirectional_ viewport _id | u(3)
omnidirectional_ viewport _cancel_flag | u(1)
if( !omnidirectional_viewport_cancel_flag ) { | 
omnidirectional_viewport_persistence_flag | u(1)
omnidirectional_ viewport _cnt_minus1 | u(3)
for( i = 0; i <= omnidirectional_ cnt_minus1; i++ ) { | 
omnidirectional_viewport_yaw_center[ i ] | i(16)
omnidirectional_viewport_pitch_center[ i ] | i(16)
omnidirectional_viewport_roll_center[ i ] | i(16)
omnidirectional_viewport_yaw_range[ i ] | i(16)
omnidirectional_viewport_pitch_range[ i ] | i(16)
} | 
} | 
} | 

## Slide 6: Conclusion
Recommend to add an SEI message to indicate omnidirectional ROI
Align with OMAF draft functionality
While could perhaps be combined with the omnidirectional projection information SEI message, seems cleaner to keep separate
  May have different persistence conditions
    Desirable to allow this message to change on a per picture basis
  May wish to add or modify this SEI message after original encoding