## Slide 1: Industry Use Combinations
Yasser Syed, Chris Seeger, Chad Fogg, Lars Borg
Comcast/ NBCU, MovieLabs, Adobe

## Slide 2: Video Characterization Properties across Industries
Color Volume Parameters
Bitdepth
Chroma SubSampling
Full/ Narrow Scale
Display Reference Parameters
Others
Creation, Production, Distribution, Display

## Slide 3: MPEG Color Tags for HEVC and QuickTime
Chris Arley Seeger - Director, Advanced Content Production Technology
© 2016 NBCUniversal, LLC.
Color Volume | Color Primary (Logical) | Electro-Optical Transfer Function (EOTF)(Logical) | Color Representation | Minimum Bit Depth (bpc) | MPEG Color Primary Index Value | MPEG Transfer Function Index Value | MPEG Conversion Matrix Index Value | AVC/HEVC Codec Tiers | Additional Use Case for Production-level wrappers
Narrow Dynamic Range, Standard Color Gamut | BT.709-6 | BT.709-6 | Y’Cb’Cr’ NCL | 8 | 1 | 1 | 1 | MPEG2 MAIN 8-bit | Apple QuickTime™ Wrapper NCLC Color Tags using MPEG Tags (in Orange) and MXF Image Descriptors from ST.2067:21:2016 and prior standards
 | BT.709-6 | BT.709-6 | R’G’B’ 4:4:4 | 8 | 1 | 1 | 0 | AVC High 4:4:4 8-14 bits | 
 |  |  |  |  |  |  |  | HEVC Main 8-bit | 
HD/UHD/8K, Narrow Dynamic Range and Wide Color Gamut | BT.2020-2 | BT.709-6 | Y’Cb’Cr’ NCL | 10 | 9 | 1 | 9 | HEVC Main10 and Main12 | 
 |  |  | R’G’B’ 4:4:4 |  |  |  | 0 | HEVC Main 4:4:4 16 and Main 4:4:4 Intra | 
HD/UHD/8K, High Dynamic Range and Wide Color Gamut |  | PQ (ST.2084 / BT. 2100) | Y’Cb’Cr’ NCL |  |  | 16 | 9 | HEVC Main10 and Main12 | 
 |  | HLG / BT.2100 | Y’CbCr |  |  | 18 | 9 |  | 
 |  | PQ (ST.2084 / BT. 2100) | ICtCp |  |  | 16 | 14 |  | 
 |  | HLG / BT.2100 | ICtCp |  |  | 18 |  |  | 
 |  | PQ (ST.2084 / BT. 2100) | R’G’B’ 4:4:4 |  |  | 16 | 0 | HEVC Main 4:4:4 16 and Main 4:4:4 Intra | 
 |  | HLG / BT.2100 | R’G’B’ 4:4:4 |  |  | 18 | 0 | HEVC Main 4:4:4 16 and Main 4:4:4 Intra | 
Items that have ITALICIZED text are MPEG2/AVC/HEVC Codec Tiers in common use
HEVC 12/16 bit tiers are not typically used today.
ICtCp is not standardized for the MXF container yet
BT.2100 may supersede ST 2084 as it indicates PQ EOTF and OETF
BBC/NHK prefers referencing BT 2100 as the definitive reference for HLG
BT.1886 = EOTF for flat panel displays used in HDTV studio production as defined by ITU

## Slide 4: SMPTE 2067-21:2016 Defining Color Tags within MXF
Chris Arley Seeger - Director, Advanced Content Production Technology
© 2016 NBCUniversal, LLC.
Color Volume | Color Primary (Logical) | Transfer Function (Logical) | Color Representation | Minimum Bit Depth (bpc) | Color Primaries | Opto-Electronic Transfer Characteristics (OETF) | Coding Equations (Matrix Conversions)
SDR/BT.709-6 [COLOR 3] | BT.709-6 | ITU-R BT.709-6 | Y’Cb’Cr’ NCL | 8 | 06.0E.2B.34.04.01.01.06.04.01.01.01.03.03.00.00 | 06.0E.2B.34.04.01.01.01.04.01.01.01.01.02.00.00 | 06.0E.2B.34.04.01.01.01.04.01.01.01.02.02.00.00
HLG HDR-SDR [COLOR 3] |  | HLG / 2100 | Y’Cb’Cr’ NCL | 10 |  | 06.0E.2B.34.04.01.01.0D.04.01.01.01.01.0B.00.00 | 
SDR/WCG [COLOR 5] | BT.2020-2 | ITU-R BT.709-6 | Y’Cb’Cr’ NCL | 10 | 06.0E.2B.34.04.01.01.0D.04.01.01.01.03.04.00.00 | 06.0E.2B.34.04.01.01.0E.04.01.01.01.01.09.00.00 | 06.0e.2b.34.04.01.01.0d.04.01.01.01.02.06.00.00
HDR/WCG [COLOR 7] |  | PQ (ST.2084 / BT. 2100) | Y’Cb’Cr’ NCL |  |  | 06.0E.2B.34.04.01.01.0D.04.01.01.01.01.0A.00.00 | 
 |  | HLG / 2100 | Y’Cb’Cr’ NCL |  |  | 06.0E.2B.34.04.01.01.0D.04.01.01.01.01.0B.00.00 | 

## Slide 5: SMPTE 2067-21:2016 Defining Mastering Display Color Volume in MXF
Chris Arley Seeger - Director, Advanced Content Production Technology
© 2016 NBCUniversal, LLC.
Mastering Display Primaries | 12 | 060e2b34.01 01010e.0420 0401.010100 00 | Display Primaries metadata as specified in ST 2086
Mastering Display White Point Chromaticity | 4 | 060e2b34.01 01010e.0420 0401.010200 00 | Chromaticity of White Point metadata as specified in ST 2086
Mastering Display Maximum Luminance | 4 | 060e2b34.01 01010e.0420 0401.010300 00 | Maximum Display Mastering Luminance metadata as specified in ST 2086
Mastering Display Minimum Luminance | 4 | 060e2b34.01 01010e.0420 0401.010400 00 | Minimum Display Mastering Luminance metadata as specified in ST 2086
USEFUL EXAMPLES FOR COMMON WORKFLOWS |  |  |  | 
Description | Mastering Display Primaries (x,y) for {R}, {G}, {B} | Mastering Display White Point Chromaticity {x,y} | Mastering Display Maximum Luminance (10000*cd/m2) | Mastering Display Minimum Luminance (0.0001*cd/m2)
709-Gamma_2.4, D65, 1000nit | { 32000, 16500 } { 15000, 30000 } { 7500, 3000 } | { 15635, 16450 } (D65) | 10000000 (1000 cd/m2) | 500 (0.05 cd/m2 for LCD/LED)
709-Gamma_2.4, D65, 4000nit | { 32000, 16500 } { 15000, 30000 } { 7500, 3000 } | { 15635, 16450 } (D65) | 40000000 (4000 cd/m2) | 500 (0.05 cd/m2 for LCD/LED)
BT.2020, D65, 1000nit | { 35400, 14600 } { 8500, 39850 } { 6550, 2300 } | { 15635, 16450 } (D65) | 10000000 (1000 cd/m2) | 5 (0.0005 cd/m2 for OLED)
P3, D65, 1000nit | { 34000, 16000 } { 13250, 34500 } { 7500, 3000 } | { 15635, 16450 } (D65) | 10000000 (1000 cd/m2) | 5 (0.0005 cd/m2 for OLED)

## Slide 6: Tools
Tools Presently Operates in only parts of workflow
Parameter used is specific to workflow
With HDR, Production/ Distribution/ Display parameters are blurring (e.g LUTs)
  Live Production, Studio Production, File Based Workflows, Encoding Workflows, Graphics, Overlays
Need to Characterize Video Parameters to pass through each point and as they change through different carriage mediums
Otherwise tools make improper assumptions and can lead to Content processing mistakes

## Slide 7: Approaches
Create a Relational Table ( Different Coding Points in Different Mediums)
Document some of the Common Industry in-use Combinations of parameters (combination of code points?)

## Slide 8: Examples

## Slide 9: Examples of Common Combinations Colour Volume
Value | Colour Primaries | Transfer Functions | Matrix Coefficients | BitDepth | Chroma SubSampling | Full/ Narrow Scale
7 | 9 | 16 | 9 | 10 | 4:2:0 | NS
8 | 9 | 18 | 9 | 10 | 4:2:0 | NS
9 | 9 | 16 | 14 | 10 | 4:2:0 | NS
10 | 9 | 18 | 14 | 10 | 4:2:0 | NS
11 | 9 | 16 | 0 | 10 | 4:2:0 | NS
12 | 9 | 18 | 0 | 10 | 4:2:0 | NS
13 | 9 | 16 | 9 | 10 | 4:2:0 | FS
14 | 9 | 16 | 9 | 10 | 4:2:0 | FS
15 | 9 | 16 | 14 | 10 | 4:2:0 | FS
16 | 9 | 18 | 14 | 10 | 4:2:0 | FS
17 | 9 | 16 | 0 | 10 | 4:2:0 | FS
18 | 9 | 18 | 0 | 10 | 4:2:0 | FS
Value | Colour Primaries | Transfer Functions | Matrix Coefficients | BitDepth | Chroma SubSampling | Full/ Narrow Scale
5 | 9 | 1 | 9 | 10 | 4:2:0 | NS
6 | 9 | 1 | 0 | 10 | 4:2:0 | NS
Value | Colour Primaries | Transfer Functions | Matrix Coefficients | BitDepth | Chroma SubSampling | Full/ Narrow Scale
1 | 1 | 1 | 1 | 8 | 4:2:0 | FS
2 | 1 | 1 | 0 | 8 | 4:2:0 | NS
3 | 1 | 1 | 1 | 8 | 4:2:0 | FS
4 | 1 | 1 | 0 | 8 | 4:2:0 | NS
SD/HD- SDR Combinations
SD/HD- SDR/WCG Combinations
SD/HD- HDR Combinations

## Slide 10: Examples of Common Combinations Display Reference
Value | MDPrimaries | MDWhitePoint | MDMax Luminance | MDMin Luminance
1 | 709Gamma2.4 | D65 | 100 | CRT
Value | MDPrimaries | MDWhitePoint | MDMax Luminance | MDMin Luminance
2 | P3 | D65 | 100 | CRT
3 | BT2020 | D65 | 100 | CRT
Value | MDPrimaries | MDWhitePoint | MDMax Luminance | MDMin Luminance
4 | P3 | D65 | 1000 | LCD
5 | BT2020 | D65 | 1000 | LCD
6 | P3 | D65 | 4000 | LCD
7 | BT2020 | D65 | 4000 | LCD
8 | P3 | D65 | 1000 | LED
9 | BT2020 | D65 | 1000 | LED
10 | P3 | D65 | 4000 | LED
11 | BT2020 | D65 | 4000 | LED
SD/HD- SDR Combinations
SD/HD- SDR/WCG Combinations
SD/HD- HDR Combinations

## Slide 11: Camera Logs
Converts Light Levels in Camera Sensors to Digital Values (e.g. how to fit in 10 bits)
  Eventual Coding Point?
Examples are SLOG3, CLOG3
Archiving is an issue here
No- Standardization, but may have some movement in SMPTE
Needed so Right LUTS are applied for PQ/ HLG etc

## Slide 12: Next Steps?
Wait Wait Wait … while people are building tools
Put something into a Technical Report document (Relational/ Combinations)
  Example
  Tables
  Describing a set of Industry in use combinations is useful
  Technical Report Document is a good candidate to put something in.

## Slide 13: Reference
ISO/IEC 23001-8:2016(E): Part 8 Coding-independent code points
SMPTE 2067-21:2016 Application #2E: Extends 2067-20 Application #2 with MXF support for BT.2020, ST.2084 HDR Transfer Functions, ST.2086 HDR Mastering Display Metadata
Apple QuickTime™ Video Color Management in AV Foundation
Apple ProRes™ SMPTE RDD Draft for MXF
Chris Arley Seeger - Director, Advanced Content Production Technology
© 2016 NBCUniversal, LLC.