## Slide 1
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University, Taiwan
Centralized Texture-Depth Packing
SEI Message for HEVC and AVC
(Revisions of JCTVC-AA1008)

## Slide 2: Contents
Revisions of SEI Message Syntax in JCTVC-AA1008
Centralized Texture-Depth Packing Formats
New Color Depth Packing in RGB Subpixels
Experimental Results
Conclusions
Progress of Adoption Plan (if necessary)

## Slide 3: Centralized Texture-Depth Packing SEI Message Syntax

## Slide 4: Old CTDP SEI Syntax (JCTVC-AA1008)
centralized_texture_depth_packing( payloadSize ) { | Descriptor
centralized_texture_depth_packing_cancel_flag | u(1)
if( ! centralized_texture_depth_packing_cancel_flag ) { | 
ctdp_packing_type | u(3)
large_depth_type | u(1)
baseline_dist_flag | u(1)
focal_length_flag | u(1)
z_near_flag | u(1)
z_far_flag | u(1)
d_min_flag | u(1)
d_max_flag | u(1)
depth_representation_type | ue(v)
if( baseline_dist_flag ) | 
view_syn_rep_info_element( BdistanceSign, BdistanceExp, BdistanceMantissa, BdistanceManLen ) | 
if( focal_length_flag ) | 
view_syn_rep_info_element( FlengthSign, FlengthExp, FlengthMantissa, FlengthManLen ) | 
if( z_near_flag ) | 
view_syn_rep_info_element( ZNearSign, ZNearExp, ZNearMantissa, ZNearManLen ) | 
if( z_far_flag ) | 
view_syn_rep_info_element ( ZFarSign, ZFarExp, ZFarMantissa, ZFarManLen ) | 
if( d_min_flag ) | 
view_syn_rep_info_element ( DMinSign, DMinExp, DMinMantissa, DMinManLen ) | 
if( d_max_flag ) | 
view_syn_rep_info_element ( DMaxSign, DMaxExp, DMaxMantissa, DMaxManLen ) | 
if( depth_representation_type = = 3 ) { | 
depth_nonlinear_representation_num_minus1 | ue(v)
for( i = 1; i <= depth_nonlinear_representation_num_minus1 + 1; i++ ) | 
depth_nonlinear_representation_model[ i ] | 
centralized_texture_depth_packing_persistence_flag | u(1)
} | 
} | 
} | 

## Slide 5: New CTDP SEI Syntax (JCTVC-AC0027)
centralized_texture_depth_packing( payloadSize ) { | Descriptor
centralized_texture_depth_packing_cancel_flag | u(1)
if( ! centralized_texture_depth_packing_cancel_flag ) { | 
ctdp_packing_type | u(3)
color_packing_type | u(1)
baseline_dist_flag | u(1)
focal_length_flag | u(1)
z_near_flag | u(1)
z_far_flag | u(1)
d_min_flag | u(1)
d_max_flag | u(1)
depth_representation_type | ue(v)
if( baseline_dist_flag ) | 
view_syn_rep_info_element( BdistanceSign, BdistanceExp, BdistanceMantissa, BdistanceManLen ) | 
if( focal_length_flag ) | 
view_syn_rep_info_element( FlengthSign, FlengthExp, FlengthMantissa, FlengthManLen ) | 
if( z_near_flag ) | 
view_syn_rep_info_element( ZNearSign, ZNearExp, ZNearMantissa, ZNearManLen ) | 
if( z_far_flag ) | 
view_syn_rep_info_element ( ZFarSign, ZFarExp, ZFarMantissa, ZFarManLen ) | 
if( d_min_flag ) | 
view_syn_rep_info_element ( DMinSign, DMinExp, DMinMantissa, DMinManLen ) | 
if( d_max_flag ) | 
view_syn_rep_info_element ( DMaxSign, DMaxExp, DMaxMantissa, DMaxManLen ) | 
if( depth_representation_type = = 3 ) { | 
depth_nonlinear_representation_num_minus1 | ue(v)
for( i = 1; i <= depth_nonlinear_representation_num_minus1 + 1; i++ ) | 
depth_nonlinear_representation_model[ i ] | 
centralized_texture_depth_packing_persistence_flag | u(1)
} | 
} | 
} | 

## Slide 6: ctdp_packing_type
CTDP-TB
CTDP-LR
Value | Interpretation
0 | Indicates the frame of the CTDP-TB type with an arrangement of subsample color depth top (SCDT), related texture (RT), and subsample color depth bottom (SCDB) regions from top to bottom, as illustrated in Figure D‑X1.
1 | Indicates the frame of the CTDP-LR type with an arrangement of subsample color depth left (SCDL), related texture (RT), and subsample color depth right (SCDR) regions from left to right, as illustrated in Figure D‑X2.
Remove large_depth_size and fix depth size for each packing type
(Depth:1/9, Texure:8/9)
(Depth:1/12, Texture:11/12)

## Slide 7
color_packing_type equal to 1 indicates the depth map is packed into the colored depth map in YCbCr color components.
color_packing_type equal to 0 indicates the depth map is packed into the colored depth map in RGB color components.
When ctdp_packing_type is not equal to 0 or 1, color_packing_type is ignored and reserved for future use by ITU-T | ISO/IEC.
color_packing_type

## Slide 8: Centralized Texture-Depth Packing (CTDP) Formats

## Slide 9: CTDP- Top and Bottom (TB) Packing Procedure
Vertical Splitting
& Flipping
Spatial Subsample in
Vertical Direction
Vertical Subsample or
Original Texture Frame
Combination
H
H
Gray Depth to Color Depth
Vertical Packing
HHD
HST
HRT
HHD
HHD
HHD
2HHD
6HHD
w
w
w
w
w
w
w
w

## Slide 10: CTDP Left and Right (LR) Packing Procedure
Horizontal Splitting
& Flipping
Spatial Subsample in
Horizontal Direction
Horizontal Subsample or
Original Texture Frame
Combination
W
W
Gray Depth to Color Depth
Horizontal Packing
2WHD
WHD
WRT
WHD
WRT
WHD
WHD
6WHD
H
H
H
H
H
H
H
H

## Slide 11: CTDP Formats for HD Video (1920x1080)
CTDP-TB Format :
60
960
1920
60
1080

## Slide 12: CTDP Formats for HD Video (1920x1080)
1760
80
80
1080
CTDP-LR Format :
1920

## Slide 13: Nonstandard Resolution CTDP Packing
HD: 1920 x 1088
1920
Depth Deleting and Texture Reserving (DDTR) Method:
1088
1080
Delete upper 4
depth/texture lines
Delete lower 4
depth/texture lines
1920
960
60
60
1088
Padding upper
4 texture lines
Padding lower
4 texture lines
60
60
968
Advantages: 1) keep original resolution; 2) no texture deletion, 3) fixed packing computation
Disadvantage: depth deletion but could be obtained by extrapolation

## Slide 14: Experimental Results (1920x1088)
PSNR (dB) | Original CTDP without DDTR | Revised CTDP with DDTR
Texture | 42.9519 | 42.9405
Depth | 51.0192 | 50.7053*
*Note: The top and bottom depth lines are repeatedly extended for 4 rows in this simulations. A good extrapolation algorithm could further improve the depth performance!
Up-sampling computation | Original CTDP without DDTR | Revised CTDP with DDTR
Texture | 968:1088 (varied) | 8:9 (fixed)
Depth | 360:1088 (varied) | 1:3 (Fixed)
Computation Involvement for CTDP-TB Format:
Packing Performance (Uncoded):

## Slide 15
CTDP Depacking for ctdp_packing_type =0

## Slide 16
CTDP Depacking for ctdp_packing_type =1

## Slide 17: Revisions of Figures and Subscript Position Indexing

## Slide 18: Positioning of Color Depth to Gray Depth

## Slide 19: Colored Depth to Depth Depacking for YCbCr 4:2:0
For each 4 color pixels, in YCbCr 4:2:0, 6 Color Components {Yi,j, Yi,j+1, Yi+1,j, Yi+1,j+1, Cbi,j, and Cri,j) can be depacked to 6 correct depth pixels {D3i,j, D3i+1,j+1, D3i+4, j, D3i+5, j+1, D3i+2,j, D3i+3, j+1} for ctdp_packing type =0 and {Di,3j, Di+1,3j+1, Di,3 j+4, Di+1, 3j+5, Di,3j+2, Di+1,3j+} for ctdp_packing type =1.

## Slide 20: Linear Mapping of Y Component
In PCM approach, four Y components are linearly mapped to four selected depth values.
0
Y
D
16
235
255
255
235
Slope=0.8588
Y= [16, 235]
D= [0, 255]
Y = 0.8588 * D + 16
D = 1.1644 (Y – 16)
D = (19078* (Y – 16) + 213)/214

## Slide 21: Cb/Cr to Depth Value Conversion
In piece-wise DPCM approach, Cb/Cr component is mapped to the residual of the selected depth values with the prediction, which is the average of D1 and D2.
Cb/Cr=[16, 240]
DD =[-255, 255]
Cb, Cr
DD
16
240
255
255
235
-255
0
128
5
-5
1/Slope’=2.3364
Slope’=1
133
123
1/Slope’=2.3364

## Slide 22: Color Depth Values to Depth Values Mapping ctdp_packing_type=0, color_packing_type=1
D3i,j = (19078* ((Yi, j − 16) + 213) / 214, (D-X9)
D3i+1,j+1 = (19078 * (Yi, j+1 − 16) + 213) / 214, (D-X10)
D3i+4,j = (19078 * (Y (i+1, j) − 16) + 213) / 214, (D-X11)
D3i+5, j+1 = (19078 * (Yi+1, j+1 − 16) + 213) / 214, (D-X12)
D3i+2,j = f(Cbi,j, D3i, j, D3i+4,j), (D-X13)
D3i+3, j+1)= f(Cri,j, D3i+1,j+1, D3i+5, j+1) (D-X14)
Linear Mapping for Y components in PCM Approach:
Piecewise Linear Mapping for Cb/Cr components in DPCM Approach:

## Slide 23: Indirect Color Depacking Method: RGB Adjustment in Packing Side

## Slide 24: Traditional RGB to YUV Transform (Vertical Color Packing - Based on 4 color pixels )
R1
G1
B1
R3
G3
B3
R2
G2
B2
R4
G4
B4
RGB/YUV
Transform
Y1
U1
V1
Y3
U3
V3
Y2
U2
V2
Y4
U4
V4
i = 1, 2, 3, 4
Y1
U1
V1
Y3
U1
V1
Y2
U1
V1
Y4
U1
V1
Only R1, G1, B1 can be correctly depacked from
Y1, U1, V1 without any adjustments!
How to effectively use information of Y2, Y3, Y4 becomes a mathematical problem!

## Slide 25: Adjusted RGB to YUV Transform (Vertical Color Packing - Based on 4 color pixels )
i = 1, 2, 3, 4
Y1
U1
V1
Y3
U1
V1
Y2
U1
V1
Y4
U1
V1
Yi could give one degree freedom, which could be adjusted in the packing side to make one of {Ri, Gi, Bi} be correctly depacked in the depacking side!
For example, if we choose Gi be correctly depacked as
Gi = G’i = 1.1644(Yi-16)-0.3917 (U1-128)-0.8130 (V1-128);
Substituting U1 and V1 in terms of R1, G1, and B1 to (3), we can adjust Yi to Y’i
(1)
(2)
(3)
= 0.8588 (G2+0.2290R1-0.4130G1+0.1140B1)+16.
(4)
Since
, we adjust RGB to R’G’B’ as
Gi+0.2990R1-0.4130G1+0.1140B1
(5)

## Slide 26: Color Depth Values to Depth Values Mapping ctdp_packing_type=0, color_packing_type=0
, (D-X23)
In the Packing Side:
1st RGB set:
2st RGB set:
Gi,j+1+0.2990Ri,j-0.4130Ri+1,j+1+0.1140Bi,j
3rd RGB set:
4th RGB set:
Gi+1,j+0.2990Ri,j-0.4130Ri+1,j+1+0.1140Bi,j.
Bi+1,j+1 + 0.2990Ri,j+0.5870Ri+1,j+1-0.8860Bi,j.

## Slide 27: Color Depth Values to Depth Values Mapping ctdp_packing_type=0, color_packing_type=0
In the Depacking Side:

## Slide 28: Depth Parameters Related to this CTDP SEI Syntax (Copied from 3D-HEVC)

## Slide 33: Depth Parameter Related Flags
baseline_dist_flag equal to 0 specifies that the syntax elements specifying the baseline distance are not present in the syntax structure. baseline_dist_flag equal to 1 specifies that the syntax elements specifying the baseline distance value are present in the syntax structure.
focal_length_flag equal to 0 specifies that the syntax elements specifying the focal length are not present in the syntax structure. focal_length_pixel_flag equal to 1 specifies that the syntax elements specifying the focal length value are present in the syntax structure.
z_near_flag equal to 0 specifies that the syntax elements specifying the nearest depth value are not present in the syntax structure. z_near_flag equal to 1 specifies that the syntax elements specifying the nearest depth value are present in the syntax structure.
z_far_flag equal to 0 specifies that the syntax elements specifying the farthest depth value are not present in the syntax structure. z_far_flag equal to 1 specifies that the syntax elements specifying the farthest depth value are present in the syntax structure.
d_min_flag equal to 0 specifies that the syntax elements specifying the minimum disparity value are not present in the syntax structure. d_min_flag equal to 1 specifies that the syntax elements specifying the minimum disparity value are present in the syntax structure.
d_max_flag equal to 0 specifies that the syntax elements specifying the maximum disparity value are not present in the syntax structure. d_max_flag equal to 1 specifies that the syntax elements specifying the maximum disparity value are present in the syntax structure.

## Slide 34: depth_representation_type
Value | Interpretation
0 | Each decoded luma sample value of an auxiliary picture represents an inverse of Z value that is uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the luma sample value equal to 0 represents the inverse of ZFar (specified below). When z_near_flag is equal to 1, the luma sample value equal to maxVal represents the inverse of ZNear (specified below).
1 | Each decoded luma sample value of an auxiliary picture represents disparity that is uniformly quantized into the range of 0 to maxVal, inclusive. When d_min_flag is equal to 1, the luma sample value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the luma sample value equal to maxVal represents DMax (specified below).
2 | Each decoded luma sample value of an auxiliary picture represents a Z value uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the luma sample value equal to 0 corresponds to ZFar (specified below). When z_near_flag is equal to 1, the luma sample value equal to maxVal represents ZNear (specified below).
3 | Each decoded luma sample value of an auxiliary picture represents a nonlinearly mapped disparity, normalized in range from 0 to maxVal, as specified by depth_nonlinear_representation_num_minus1 and depth_nonlinear_representation_model[i].When d_min_flag is equal to 1, the luma sample value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the luma sample value equal to maxVal represents DMax (specified below).
Other values | Reserved for future use
The variable maxVal is set equal to ( 1 << ( 8 + bit_depth_luma_minus8 ) ) − 1, where bit_depth_luma_minus8 is the value included in or inferred for the active SPS of the layer with nuh_layer_id equal to targetLayerId.
depth_representation_type specifies the representation definition of decoded luma samples of auxiliary pictures. In the table, disparity specifies the horizontal displacement between two texture views and Z value specifies the distance from a camera.

## Slide 35: View synthesis representation information element syntax
The syntax structure specifies the value of an element in the view synthesis representation information SEI message.
The syntax structure sets the values of the OutSign, OutExp, OutMantissa and OutManLen variables that represent a floating-point value. When the syntax structure is included in another syntax structure, the variable names OutSign, OutExp, OutMantissa and OutManLen are to be interpreted as being replaced by the variable names used when the syntax structure is included.
da_sign_flag equal to 0 indicates that the sign of the floating-point value is positive. da_sign_flag equal to 1 indicates that the sign is negative. The variable OutSign is set equal to da_sign_flag.
da_exponent specifies the exponent of the floating-point value. The value of da_exponent shall be in the range of 0 to 27 − 2, inclusive. The value 27 − 1 is reserved for future use by ITU-T | ISO/IEC. Decoders shall treat the value 27 − 1 as indicating an unspecified value. The variable OutExp is set equal to da_exponent.
da_mantissa_len_minus1 plus 1 specifies the number of bits in the da_mantissa syntax element. The value of da_mantissa_len_minus1 shall be in the range of 0 to 31, inclusive. The variable OutManLen is set equal to da_mantissa_len_minus1 + 1.
da_mantissa specifies the mantissa of the floating-point value. The variable OutMantissa is set equal to da_mantissa.
view_syn_rep_info_element( OutSign, OutExp, OutMantissa, OutManLen ) { | Descriptor
da_sign_flag | u(1)
da_exponent | u(7)
da_mantissa_len_minus1 | u(5)
da_mantissa | u(v)
} | 

## Slide 36: Association between depth parameter variables and syntax elements
x | s | e | n | v
Bdistance | BdistanceSign | BdistanceExp | BdistanceMantissa | BdistanceManLen
Flength | FlengthSign | FlengthExp | FlengthMantissa | FlengthManLen
ZNear | ZNearSign | ZNearExp | ZNearMantissa | ZNearManLen
ZFar | ZFarSign | ZFarExp | ZFarMantissa | ZFarManLen
DMax | DMaxSign | DMaxExp | DMaxMantissa | DMaxManLen
DMin | DMinSign | DMinExp | DMinMantissa | DMinManLen
The variables in the x column of table are derived from the respective variables in the s, e, n and v columns as follows:
– If the value of e is in the range of 0 to 127, exclusive, x is set equal to ( −1 )s* 2e - 31 * ( 1 + n ÷ 2v ).
– Otherwise (e is equal to 0), x is set equal to ( −1 )s * 2−( 30 + v ) * n.
The DMin and DMax values, when present, are specified in units of a luma sample width of the coded picture.
The units for the ZNear and ZFar, when present, are identical but unspecified.
When depth_representation_type is equal to 0 or 2, the disparity D can further be obtained from the value of Z, Bdistance, and Flength, where D = Bdistance × Flength ÷ Z

## Slide 37: Other Syntax Elements
depth_nonlinear_representation_num_minus1 plus 2 specifies the number of piecewise linear segments for mapping of depth values to a scale that is uniformly quantized in terms of disparity.
depth_nonlinear_representation_model[ i ] for i ranging from 0 to depth_nonlinear_representation_num_minus1 + 2, inclusive, specify the piecewise linear segments for mapping of decoded luma sample values of an auxiliary picture to a scale that is uniformly quantized in terms of disparity. The values of depth_nonlinear_representation_model[0] and depth_nonlinear_representation_model[ depth_nonlinear_representation_num_minus1 + 2 ] are both inferred to be equal to 0.
centralized_texture_depth_packing_persistence_flag specifies the persistence of the centralized texture-depth packing arrangement SEI message.
centralized_texture-depth_packing_persistence_flag equal to 0 specifies that the centralized texture-depth packing arrangement SEI message applies to the current decoded frame only.
centralized_texture-depth_packing_persistence_flag equal to 1 specifies that the centralized texture-depth packing arrangement SEI message persists in output order until any of the following conditions are true:
– A new CVS begins.
– The bitstream ends.
– A frame in an access unit containing a centralized texture-depth packing SEI message with the same

## Slide 38: Conclusions

## Slide 39: Conclusions
In this document, the CTDP formats have been reduced to 2 formats (CTDP-TB and CTDP-LR), which will help to simplify realization of the system.
In this document, we added a new colored depth packing method, called adjusted RGB method, which allows the CTDP packing and depacking in RGB domain..
In this document, the figures have been revised to clearly explain the details.
In Taiwan, the CTDP formats have been tested in HYA Company to deliver the 3D video and AR/VR services in CATV systems. Official services and media release with a grand opening will be in November.

## Slide 40: Performance Evaluations for YCbCr and Adjusted RGB Color Packing Methods
1. Uncompressed CTDP Performance (Compare to Ground True Values) 2. HEVC-Coded CTDP Performance (Compare to 3D-HEVC Results)

## Slide 41
Sequences | Clipped Resolution | Frames | 1 View | Synthesized View
Undo Dancer | 1920×1080 | 250 | 3 | 4
Shark | 1920×1080 | 300 | 5 | 7
Computer Generated Test Sequences

## Slide 42: Experimental Settings
Uncoded and Coded HD Computer Generated Videos:
ratios of depth region :
CTDP TB: Depth:1/9, Texture: 8/9
CTDP LR: Depth: 1/12, Texture: 11/12
HEVC-CTDP Coding Parameters:
encoding mode: All Intra, Low delay, Random access
QP: 27,32,37,42
ctdp_packing_type: CTDP-TB and CTDP-LR
image resizing: Lancos 4
  depth resizing: bicubic

## Slide 43
CTDP depacked texture, depth, and synthesized view are compared to ground truth ones
Uncoded CTDP Performances
of YCbCr and RGB Color Packing Methods

## Slide 44
Objective Performances of Uncoded CTDP Formats
CTDP-TB: ctdp_packing_type = 0
CTDP-LR: ctdp_packing_type = 1
Results | Depacked Texture and Depth |  |  |  |  |  | Synthesized Virtual View Generated by VSRS |  | 
 | Depacked Texture |  |  | Depacked Depth |  |  |  |  | 
 | Emu. YCbCr | Direct RGB | Adj. RGB | Emu. YCbCr | Direct RGB | Adj. RGB | Emu. YCbCr | Direct RGB | Adj. RGB
PSNR | 46.1485 | 47.0919 |  | 44.1021 | 40.8486 | 44.6246 | 38.8875 | 37.1904 | 38.0283
SSIM | 0.9938 | 0.9938 |  | 0.9918 | 0.9890 | 0.9943 | 0.9867 | 0.9737 | 0.9754
Results | Depacked Texture and Depth |  |  |  |  |  | Synthesized Virtual View Generated by VSRS |  | 
 | Depacked Texture |  |  | Depacked Depth |  |  |  |  | 
 | Emu. YCbCr | Direct RGB | Adj. RGB | Emu. YCbCr | Direct RGB | Adj. RGB | Emu. YCbCr | Direct RGB | Adj. RGB
PSNR | 49.2137 | 49.2443 |  | 39.8881 | 35.9820 | 40.4315 | 38.2884 | 36.0823 | 37.4933
SSIM | 0.9958 | 0.9955 |  | 0.9873 | 0.9802 | 0.9905 | 0.9882 | 0.9737 | 0.9768

## Slide 45
Subjective Performances of Uncoded CTDP Formats
Depacked Depth of Original RGB Color Packing

## Slide 46
Subjective Performances of Uncoded CTDP Formats
Depacked Depth of Adjusted RGB Color Packing

## Slide 47
Subjective Performances of Uncoded CTDP Formats
Snythesized Virtual View of Original RGB Color Packing

## Slide 48
Subjective Performances of Uncoded CTDP Formats
Synthesized View of Adjusted RGB Color Packing

## Slide 49
HEVC-coded CTDP Performances
of YCbCr and RGB Color Packing Methods
CTDP-HEVC decoded and depacked texture, depth, and synthesized view are compared to 3D-HEVC decoded ones

## Slide 50
HEVC-coded CTDP-TB Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  |  | Depacked Depth |  |  | Virtual View by VSRS |  | 
 | Emu. YUV | Direct RGB | Adj. RGB | Emu. YUV | Direct RGB | Adj. RGB | Emu. YUV | Direct RGB | Adj. RGB
ra | 13.6254 | 9.6406 | 11.8079 | -30.6426 | -40.8299 | -41.9352 | 25.7829 | 27.0899 | 28.5642
ldp | 8.2266 | 4.6375 | 7.0231 | -53.8872 | -62.9424 | -61.2222 | 13.9024 | 16.1361 | 16.9534
ai | 6.8931 | 3.9400 | 5.4887 | -19.7578 | -20.9339 | -30.0731 | 29.2954 | 35.9331 | 34.6573
ave | 9.5817 | 6.0727 | 8.1065 | -34.7625 | -41.5687 | -44.4102 | 22.9936 | 26.3864 | 26.7250
Coding Modes | Depacked Texture |  |  | Depacked Depth |  |  | Virtual View by VSRS |  | 
 | Emu. YUV | Direct RGB | Adj. RGB | Emu. YUV | Direct RGB | Adj. RGB | Emu. YUV | Direct RGB | Adj. RGB
ra | -0.4247 | -0.3044 | -0.3737 | 1.3941 | 1.7552 | 2.1227 | -0.6789 | -0.7336 | -0.7511
ldp | -0.2707 | -0.1585 | -0.2344 | 3.6932 | 5.0084 | 4.4448 | -0.4051 | -0.4917 | -0.4940
ai | -0.2557 | -0.1489 | -0.2088 | 0.8799 | 0.5620 | 1.5138 | -0.8694 | -1.0608 | -1.0012
ave | -0.3170 | -0.2039 | -0.2723 | 1.9902 | 2.4419 | 2.6937 | -0.6511 | -0.7620 | -0.7487

## Slide 51
HEVC-coded CTDP-LR Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  |  | Depacked Depth |  |  | Virtual View by VSRS |  | 
 | Emu. YUV | Direct RGB | Adj. RGB | Emu. YUV | Direct RGB | Adj. RGB | Emu. YUV | Direct RGB | Adj. RGB
ra | 11.7019 | 7.9095 | 10.3264 | 26.5047 | 16.5991 | 6.3530 | 67.8342 | 61.9436 | 64.9970
ldp | 6.9614 | 3.4178 | 5.9485 | -30.2637 | -36.2061 | -40.3581 | 42.2946 | 39.2266 | 40.5865
ai | 3.7328 | 0.9848 | 2.8620 | 27.8123 | 30.3497 | 11.1768 | 69.7477 | 73.1888 | 68.4575
ave | 7.4653 | 4.1040 | 6.3790 | 8.0178 | 3.5809 | -7.6094 | 59.9588 | 58.1196 | 58.0137
Coding Modes | Depacked Texture |  |  | Depacked Depth |  |  | Virtual View by VSRS |  | 
 | Emu. YUV | Direct RGB | Adj. RGB | Emu. YUV | Direct RGB | Adj. RGB | Emu. YUV | Direct RGB | Adj. RGB
ra | -0.3560 | -0.2415 | -0.3184 | -1.0712 | -1.2349 | -0.3254 | -1.3992 | -1.3615 | -1.3630
ldp | -0.2231 | -0.1122 | -0.1935 | 1.3046 | 0.9894 | 2.0469 | -1.0077 | -0.9979 | -0.9781
ai | -0.1370 | -0.0344 | -0.1072 | -1.6007 | -2.4781 | -0.8882 | -1.6165 | -1.7321 | -1.6039
ave | -0.2387 | -0.1293 | -0.2064 | -0.4558 | -0.9079 | 0.2778 | -1.3411 | -1.3638 | -1.3150

## Slide 52
Subjective Performances of Coded CTDP Formats
Depacked Depth of Original RGB Color Packing
(QP=27)

## Slide 53
Subjective Performances of Coded CTDP Formats
Depacked Depth of Adjusted RGB Color Packing
(QP=27)

## Slide 54
Subjective Performances of Coded CTDP Formats
Synthesized Virtual View of Original RGB Color Packing
(QP=27)

## Slide 55
Subjective Performances of Coded CTDP Formats
Synthesized View of Adjusted RGB Color Packing
(QP=27)

## Slide 56: Adoption Plan in Taiwan
Hsin Yeong An (HYA) Cable TV Company
Public Television Services

## Slide 57
Depth Extraction from VR Contents

## Slide 58: Adoption Test Plan
The National Cheng Kung University and the Hsin Yeong An (HYA) Cable TV Company have signed Memorandum of Understanding (MOU) to adopt the CTDP formats to delivering 3D TV programs in HYA Broadcasting Systems. The test and adoption plan is divided into five stages and designed as:
1. Jan. 15, 2017: Complete MOU signing (completed)
2. Mar. 15, 2017: Propose and confirm the test and adoption detailed plans (completed)
3. Dec. 15, 2017: Test of downloaded 3D AR/VR Video CTDP services with computer clients (in Testing)
4. Aug. 15, 2018: Deliver 3D AR/VR Video CATV services in a remote server and set-top-box with CTDP separate module.
5. Aug.15, 2019: Deliver 3D AR/VR Video CATV services through Set-top-Boxes with Integrated CTDP depacking module (open to all users and charged 3D TV services)

## Slide 59: Test Plan for Headend (New with AR/VR)

## Slide 60
Interactive
Devices
2D
Display
Naked-eyes
3D Display
CTDP
Depacking
VLSI
Digital
Set Top Box
DIBR View Synthesizer
VLSI
Uncompressed
SbS 3D Display
RB-glasses
3D
2D TV Programs
Traditional
SbS 3D
Packing
SbS 3D Display
User 3D Effective Adjustment
Combined
Multiview
Two Views
Mixed RB 2-view
video
CTDP Packing Format
2 Views
Selection
RB 2-view
Mixing
Interactive
Inform
Wireless Unit
Wireless Unit
Reception of AR/VR 3D CTDP Programs