## Slide 1: ST 2086 update for 2018
JCTVC-AE0026 (version 2)

## Slide 2: ST 2086 status: https://kws.smpte.org/higherlogic/ws/public/projects
10E Revision of ST 2086 Mastering Display Color Volume Metadata Supporting High Luminance and Wide Color Gamut Images
Description
A revision of ST 2086 is necessary to address issues reported since publication.
Progress Report
In publication queue
Project Type
SMPTE Engineering Project (ANSI)
Project Overview
Problem to be solved: ST 2086 currently does not provide value ranges for the metadata items. Guidance is needed for other standards to specify encoding. ST 2086 currently does not provide encoding precision for the metadata items. Guidance is needed for other standards to specify encoding. TC 10E received a liaison from DVB reporting the need for signaling the use of PLUGE in live broadcast production work. ST 2086 needs to provide recommendation to indicate the use cases of PLUGE or permit DVB to define ditto. ST 2086 currently does not permit metadata item values to signal unknown values. For example, the CTA 861.3 and CTA 861-G set aside the chromaticity coordinate of (0.0, 0.0), maximum luminance 0 nit and minimum luminance of 0.0 nit to signal the corresponding value as unknown. Normative reference CIE 15:2004 is no longer available. It should be replaced with ISO 11664-3/CIE S 013-3/E
Project scope:: Add recommendation of value ranges for all metadata items Add recommendation of minimum precisions for all metadata items Add recommendation of setting aside a value range for each metadata item for application specific coding Add recommendation or option for signaling unknown values. Update normative reference CIE 15:2004 to ISO 11664-3/CIE S 014-3/E
Specific tasks:: Create a proposed revision of ST 2086 to address the issues described in the Project Scope.
Form of output:: Revision
Progress
Start: 2017-06-08| Complete: 2018-04-01 (est.)

## Slide 3: History of Mastering Display Color Volume
Studios initiated SMPTE ST 2086 to convey approved color volume. May be very different from implied volume of signal container, such as XYZ/YDzDx or vast BT.2100/2020 gamut.
SMPTE ST 2086: 2014 (first edition) elements were defined only as real-signal values.
  No quantization or syntax guidance other than “the metadata value shall be a number with four decimal places” for display primaries and white point, and “the metadata value shall be a number with up to four significant digits and up to two decimal places” for max/min luminance.
  JCT therefore chose real units of 0.00002 (1/50000) for display primaries & white point, and 0.0001 cd/m^2 units for both max & min display master luminance.
During 2014 Valencia meeting review of (JCTVC-Q0086), HEVC editors determined extra any precision and range in MDCV SEI msg. would not be harmful, and can be ignored.
In 2015, CTA 861.3 copied MDCV SEI msg. payload, but quantized HDMI max. lum. to 16-bits, in 1 cd/m^2 units, to save bytes in new Dynamic Range and Mastering InfoFrame. Also limited min. lum. to 0 to 6.5535 nits.
  Precision and range tailored for realistic measures of modern displays.
  This unit step precision of 1 cd/m^2 not reflected back in SMPTE ST 2086 until 2018.
ST 2086:2018 adds common HDMI HDR practice: 0=“unspecified” for any element.
ST 2086:2018 took the opportunity to define nominal ranges of elements.
ST 2086:2018 is final: https://kws.smpte.org/higherlogic/ws/public/projects

## Slide 4: Current MDCV SEI syntax (HEVC 2018 edition)
mastering_display_colour_volume( payloadSize ) { | Descriptor
for( c = 0; c < 3; c++ ) { | 
display_primaries_x[ c ] | u(16)
display_primaries_y[ c ] | u(16)
} | 
white_point_x | u(16)
white_point_y | u(16)
max_display_mastering_luminance | u(32)
min_display_mastering_luminance | u(32)
} | 
    D.2.28 Mastering display colour volume SEI message syntax

## Slide 5: Current MDCV SEI semantics (HEVC 2018 edition)
D.3.28 Mastering display colour volume SEI message semantics
This SEI message identifies the colour volume (the colour primaries, white point and luminance range) of a display considered to be the mastering display for the associated video content – e.g., the colour volume of a display that was used for viewing while authoring the video content. The described mastering display is a three-colour additive display system that has been configured to use the indicated mastering colour volume.
This SEI message does not specify the measurement methodologies and procedures used for determining the indicated values or any description of the mastering environment. It also does not provide information on colour transformations that would be appropriate to preserve creative intent on displays with colour volumes different from that of the described mastering display.
The information conveyed in this SEI message is intended to be adequate for purposes corresponding to the use of SMPTE ST 2086 (2014).
When a mastering display colour volume SEI message is present for any picture of a CLVS of a particular layer, a mastering display colour volume SEI message shall be present for the first picture of the CLVS. The mastering display colour volume SEI message persists for the current layer in decoding order from the current picture until the end of the CLVS. All mastering display colour volume SEI messages that apply to the same CLVS shall have the same content.
display_primaries_x[ c ] and display_primaries_y[ c ] specify the normalized x and y chromaticity coordinates, respectively, of the colour primary component c of the mastering display, according to the CIE 1931 definition of x and y as specified in ISO 11664-1 (see also ISO 11664-3 and CIE 15), in increments of 0.00002. For describing mastering displays that use red, green, and blue colour primaries, it is suggested that index value c equal to 0 should correspond to the green primary, c equal to 1 should correspond to the blue primary and c equal to 2 should correspond to the red colour primary (see also Annex E and Table E.3). The values of display_primaries_x[ c ] and display_primaries_y[ c ] shall be in the range of 0 to 50 000, inclusive.
white_point_x and white_point_y specify the normalized x and y chromaticity coordinates, respectively, of the white point of the mastering display, according to the CIE 1931 definition of x and y as specified in ISO 11664-1 (see also ISO 11664-3 and CIE 15), in normalized increments of 0.00002. The values of white_point_x and white_point_y shall be in the range of 0 to 50 000.
max_display_mastering_luminance and min_display_mastering_luminance specify the nominal maximum and minimum display luminance, respectively, of the mastering display in units of 0.0001 candelas per square metre. min_display_mastering_luminance shall be less than max_display_mastering_luminance.
At minimum luminance, the mastering display is considered to have the same nominal chromaticity as the white point.

## Slide 6: JCTVC-AE0026: Proposal
Add sentences:
  Greater precision can by conveyed in this SEI message for some elements than is required by the 2018 revision of SMPTE ST 2086. The extra precision can be ignored by devices or may be removed during the repacking and relaying of the metadata to downstream devices. A value of 0 of any element within this SEI message can indicate that the corresponding quantity is unspecified or unknown.
Add NOTES to existing MDCV SEI message semantics informing readers of new nominal ST 2086:2018 ranges.
  NOTE: ST 2086:2018 defines the precision of xy chromaticy coordinates with four decimal places, thus this SEI message provides 5 times as much precision. ST 2086:2018 also states that x coordinates shall be in the decimal range [0.0001, 0.7400] and y coordinates shall be in the decimal range [0.0001, 0.8400].
  NOTE: SMPTE ST 2086:2018 states that maximum display mastering luminance shall be a multiple of 1 candela per square meter, thus this SEI message syntax has 1000 times as much precision for this element.
  NOTE: SMPTE ST 2086:2018 states that a value in the range [5, 10000] candelas per square meter indicates the nominal maximum display luminance.
  SMPTE ST 2086:2018 states that a value in the range [0.0001, 5.0000] candelas per square meter indicates the nominal minimum display luminance.
Remove the following sentence, since it conflicts with the use of 0 value to indicate “unknown”:
  max_display_mastering_luminance and min_display_mastering_luminance specify the nominal maximum and minimum display luminance, respectively, of the mastering display in units of 0.0001 candelas per square metre. min_display_mastering_luminance shall be less than max_display_mastering_luminance.

## Slide 7: What firmware developers do for SEI  HDMI
HDMI_display_primaries_{x,y}[c] = SEI_display_primaries_{x,y}[c]
HDMI_white_point_{x,y} = SEI_white_point{x,y}
HDMI_max_display_mastering_luminance = SEI_max_display_mastering_luminance / 10000 [Note: ‘/’ is the truncating divide as per HEVC § 5.2]
HDMI_min_display_mastering_luminance = (SEI_min_display_mastering_luminance > 65535) ? 0 : (SEI_min_display_mastering_luminance & 0xFFFF )
SEI_* are the syntax elements in mastering_display_colour_volume() SEI message (payloadType 137) in AVC and HEVC bitstreams.
HDMI_* are the conterpart syntax elements in CTA 861-G (static metadata type 1) Dynamic Range and Mastering InfoFrame.
The 6 elements of HDMI_display_primaries_{x,y}[c] are packed into data bytes 3 through 14 of the InfoFrame and have the same 0.00002 units (1/50000) as their SEI msg. counterparts.
The 2 elements of HDMI_white_point _{x,y} are packed into data bytes 15 through 18 and have the same 0.00002 units (1/50000) as their counterparts in AVC, HEVC.
HDMI_max_display_mastering_luminance occupies data byte 19 and 20
HDMI_min_display_mastering_luminance occupies data byte 21 and 22.
MaxCLL is packed into bytes 23 and 24, while MaxFALL is in bytes 25 and 26 and has the same units as the HEVC Content Light Level SEI message.
EOTF (HLG, PQ, etc.) is carried in the InfoFrame byte 1.

## Slide 8: Note: Additional HDMI rule
MovieLabs CTO Jim Helman added the following rule to CTA 861 so that any order of display_primary elements in the InfoFrame can be mapped to the correct respective R,G,B primary (CTA did not specify order in the first publication, in 861.3):
  “The correspondence between Red, Green and Blue color primaries and indices 0, 1, or 2 is determined by the following relationship:
  The Red color primary corresponds to the index of the largest display_primaries_x[] value.
  The Green color primary corresponds to the index of the largest display_primaries_y[] value.
  The Blue color primary corresponds to the index with neither the largest display_primaries_y[] value nor the largest display_primaries_x[] value.”
MDCV SEI message explicitly defines g,b,r order due to historical ISO/IEC | ITU-T use of channel 0 to carry Green or Luma samples in respective RGB (matrix_coef=0) or YCbCr (matrix_coef=1, etc.) modes.
x
y