## Slide 1
Presenter : Jar-Ferr Yang
JCTVC-AG0023: Centralized Texture-Depth Packing SEI Message for HEVC and AVC
(Revisions of JCTVC-AA1008)
Institute of Computer and Communication Engineering,
Department of Electrical Engineering,
National Cheng Kung University, Tainan, Taiwan

## Slide 2: Contents
CTDP SEI Message Syntax
CTDP Formats: Interpretation of ctdp_packing_type
Colored Depth Depacking
Depth Parameters Related Syntax
Experimental Results with Texture-based Upsampling
Conclusions

## Slide 3: Centralized Texture-Depth Packing SEI Message Syntax

## Slide 4: CTDP SEI Syntax in JCTVC-AE0022 (New)
centralized_texture_depth_packing( payloadSize ) { | Descriptor
centralized_texture_depth_packing_cancel_flag | u(1)
if( ! centralized_texture_depth_packing_cancel_flag ) { | 
ctdp_packing_type | u(3)
baseline_dist_flag | u(1)
focal_length_flag | u(1)
z_near_flag | u(1)
z_far_flag | u(1)
d_min_flag | u(1)
d_max_flag | u(1)
depth_representation_type | ue(v)
if( baseline_dist_flag ) | 
view_syn_rep_info_element( BdistanceSign, BdistanceExp, BdistanceMantissa, BdistanceManLen ) | 
if( focal_length_flag ) | 
view_syn_rep_info_element( FlengthSign, FlengthExp, FlengthMantissa, FlengthManLen ) | 
if( z_near_flag ) | 
view_syn_rep_info_element( ZNearSign, ZNearExp, ZNearMantissa, ZNearManLen ) | 
if( z_far_flag ) | 
view_syn_rep_info_element ( ZFarSign, ZFarExp, ZFarMantissa, ZFarManLen ) | 
if( d_min_flag ) | 
view_syn_rep_info_element ( DMinSign, DMinExp, DMinMantissa, DMinManLen ) | 
if( d_max_flag ) | 
view_syn_rep_info_element ( DMaxSign, DMaxExp, DMaxMantissa, DMaxManLen ) | 
if( depth_representation_type = = 3 ) { | 
depth_nonlinear_representation_num_minus1 | ue(v)
for( i = 1; i <= depth_nonlinear_representation_num_minus1 + 1; i++ ) | 
depth_nonlinear_representation_model[ i ] | 
centralized_texture_depth_packing_persistence_flag | u(1)
} | 
} | 
} | 

## Slide 5: Centralized Texture-Depth Packing (CTDP) Formats : ctdp_packing_type

## Slide 6: ctdp_packing_type
CTDP-TB
CTDP-LR
Value | Interpretation
0 | Indicates the frame of the CTDP-TB type with an arrangement of top color depth (CDT), texture (T), and bottom color depth (CDB) regions from top to bottom, as illustrated in Figure D‑X1.
1 | Indicates the frame of the CTDP-LR type with an arrangement of left color depth (CDL), texture (T), and right color depth (CDR) regions from left to right, as illustrated in Figure D‑X2.
(Depth:1/9, Texure:8/9)
(Depth:1/12, Texture:11/12)

## Slide 7: CTDP-TB Format Packing Procedure
Vertical Depth Packing
to YCbCr Components
Spatial Subsample in
Vertical Direction
Vertical Subsample or
Original Texture Frame
Vertical
Combination
H
H
HT
HT
HD
HD
6HD
w
w
w
HD
HD
w
w
w
w
2HD
Vertical Splitting
& Flipping

## Slide 8: CTDP-TB Format for HD Video (1920x1080)
CTDP-TB Format :
60
960
1920
60
1080
HD=(1080/36)*2=60
HT=1080-2*60=960

## Slide 9
CTDP Depacking for ctdp_packing_type =0
Arrangement of the CTDP-TB frame and its depacking steps (ctdp_packing type = 0):

## Slide 10: CTDP-LR Format Packing Procedure
Spatial Subsample in
Horizontal Direction
Horizontal Subsample or
Original Texture Frame
Combination
W
W
WD
WT
WD
WT
H
H
6*WD
H
WD
WD
H
H
H
H
Horizontal Splitting
& Flipping
Horizontal Depth Packing
to YCbCr Components
2*WD
H

## Slide 11: CTDP-LR Format for HD Video (1920x1080)
CTDP-LR Format :
1760
80
80
1080
1920
WD=(1920/48)*2=80
WT=1920-2*80=1760

## Slide 12
CTDP Depacking for ctdp_packing_type =1
Arrangement of the CTDP-LR frame and its depacking steps (ctdp_packing type = 1):

## Slide 13: CTDP-LR Format Depacking Procedure
Horizontal Upsample to
Original Texture Frame
Horizontal Splitting
W
W
WT
H
H
6*WD
H
WD
WD
H
H
H
WD
WD
WT
H
Horizontal Flipping
& Merging
YCbCr Components To
Depth Horizontal Depacking
2*WD
H
Spatial Upsample in
Horizontal Direction

## Slide 14: Colored Depth Pixels Packing and Depacking by Using YCbCr Components

## Slide 15: Positions of Depth & Color Depth Pixels in YCbCr
CTDP-TB type RGB subpixels arranged in 3 consecutive vertical depth pixels
CTDP-TB type RGB subpixels arranged in 3 consecutive horizontal depth pixels
Concept of Color Depth Packing:
1 color depth pixel in YCbCr components can carry 3 depth pixels;
4 color depth pixels in YCbCr components can carry 12 depth pixels.

## Slide 16: Y Component Mapping to Depth Value
0
Y
D
16
235
255
255
235
Slope=0.8588
Y= [16, 235]
D= [0, 255]
Y = 0.8588 * D + 16
D = 1.1644 (Y – 16)
D = (19078* (Y – 16) + 213)/214
In PCM approach, the depth value D is depacked from Y component, which is linearly mapped to;
JCTVC-AA1008
maxValue=255
JCTVC-AA1008

## Slide 17: PCM: Y Component Mapping to Depth Value
In PCM approach, the depth value D=g(Y) is depacked from Y component, which is linearly mapped to;
D =g(Y) = (214 * (Y − 16)*maxValue / (maxValue-36) + 213) / 214
where
maxValue =(1<<(8+bit_depth_luma_minus8))−1

## Slide 18: Cb/Cr to Depth Value Conversion ( )
In DPCM approach, Cb/Cr component is mapped to the residual of the selected depth values with the prediction, which is the average of D and E.
Cb/Cr=[16, 240]
DD =[-255, 255]
Cb, Cr
DD
16
240
255
255
235
-255
0
128
5
-5
1/Slope’=2.3364
Slope’=1
133
123
1/Slope’=2.3364
JCTVC-AA1008：
maxValue=255
JCTVC-AA1008

## Slide 19: DPCM: C Component Mapping to Depth Value
In DPCM approach, the depacked depth value D= f(C, D1, D2) is equal to Prediction = (D1 + D2)/2 plus Depth Residual Value, which is retrieved from chroma component C by piecewise-linearly mapping as

## Slide 20: CTDP-TB Depth Positions for YCbCr 4:2:0
6 YCbCr components
ctdp_packing_type = 0
D3i,j
D3i+1,j
D3i+2,j
D3i+3,j
D3i+4,j
D3i+5,j
D3i,j+1
D3i+1,j+1
Ci,j+1
Ci+1,j+1
Ci,j
Ci+1,j
4 color
pixels
6 depth pixels
D3i+2,j+1
D3i+3,j+1
D3i+4,j+1
D3i+5,j+1
Yi,j
Cbi,j
Cri,j
Yi+1,j
Cbi,j
Cri,j
Yi,j+1
Yi+1.j+1
Cbi,j
Cri,j
Cbi,j
Cri,j
i = 0, 2, 4…, (2*HD-2) and j = 0, 2, 4…, (W-2)
Color Depth Packing for YCbCr 4:2:0:
4 color depth pixels in 6 YCbCr components can carry 6 depth pixels.
D3i, j = g(Yi, j), (D-X7)
D3i+1, j+1 = g(Yi, j+1), (D-X8)
D3i+4, j = g(Yi+1, j), (D-X9)
D3i+5, j+1 = g(Yi+1, j+1). (D-X10)
D3i+2,j = f(Cbi,j, D3i,j, D3i+4,j), (D-X11)
D3i+3,j+1= f(Cri,j,D3i+1,j+1,D3i+5, j+1), (D-X12)

## Slide 21: CTDP-LR Depth Positions for YCbCr 4:2:0
Ci,j+1
Ci+1,j+1
Ci,j
Ci+1,j
4 color
pixels
Color Depth Packing for YCbCr 4:2:0:
4 color depth pixels in 6 YCbCr components can carry 6 depth pixels.
Di,3j = g(Yi,j), (D-X13)
Di+1,3j+1 = g(Yi+1, j), (D-X14)
Di, 3j+4 = g(Yi, j+1), (D-X15)
Di+1, 3j+5 = g(Yi+1, j+1), (D-X16)
Di, 3j+2 = f(Cbi, j, Di, 3j, Di, 3j+4), (D-X17)
Di+1,3j+3= f(Cri,j,Di+1,3j+1,Di+1,3j+5), (D-X18)
ctdp_packing_type = 1
Yi+1,j
6 YCbCr components
Di,3j
Di,3j+2
Di,3j+4
Di,3j+1
Di.3j+3
6 depth pixels
Yi,j
Cbi,j
Cri,j
Yi,j+1
Cbi,j
Cbi,j
Cbi,j
Yi+1.j+1
Cri,j
Cri,j
Cri,j
Di.3j+5
Di+1,3j
Di+1,3j+2
Di+1,3j+4
Di+1,3j+1
Di+1,3j+3
Di+1,3j+5
i = 0, 2, 4…, (H-2) and j = 0, 2, 4…, (2*WD-2)

## Slide 22: CTDP-TB Depth Positions for YCbCr 4:2:2
Color Depth Packing for YCbCr 4:2:2:
4 color depth pixels in 6 YCbCr components can carry 6 depth pixels.
8 YCbCr components
ctdp_packing_type = 0
Ci,j+1
Ci+1,j+1
Ci,j
Ci+1,j
4 color
pixels
8 depth pixels
i = 0, 2, 4…, (2*HD-2) and j = 0, 2, 4…, (W-2)
D3i, j = g(Yi, j), (D-X7)
D3i+1, j+1 = g(Yi, j+1), (D-X8)
D3i+4, j = g(Yi+1, j), (D-X9)
D3i+5, j+1 = g(Yi+1, j+1). (D-X10)
D3i,j+1=f(Cbi,j, D3i,j, D3i+1,j+1), (D-X19)
D3i+2,j = f(Cri, j, D3i,j, D3i+4, j) (D-X20)
D3i+3,j+1=f(Cbi+1,j,D3i+1,j,D3i+5,j+1), (D-X21)
D3i+5,j=f(Cri+1,j,D3i+1,j+1,D3i+5,j+1) (D-X22)
Yi,j
Cbi,j
Cri,j
Yi+1,j
Cbi+1,j
Cri+1,j
Yi,j+1
Yi+1.j+1
Cbi+1,j
Cri+1,j
D3i,j
D3i+1,j
D3i+2,j
D3i+3,j
D3i+4,j
D3i+5,j
D3i,j+1
D3i+1,j+1
D3i+2,j+1
D3i+3,j+1
D3i+4,j+1
D3i+5,j+1
Cbi,j
Cri,j

## Slide 23: CTDP-LR Depth Positions for YCbCr 4:2:2
Color Depth Packing for YCbCr 4:2:2:
4 color depth pixels in 8 YCbCr components can carry 8 depth pixels.
Ci,j+1
Ci+1,j+1
Ci,j
Ci+1,j
4 color
pixels
Di,3j = g(Yi,j), (D-X13)
Di+1,3j+1 = g(Yi+1, j), (D-X14)
Di, 3j+4 = g(Yi, j+1), (D-X15)
Di+1, 3j+5 = g(Yi+1, j+1), (D-X16)
Di+1,3j= f(Cbi,j,Di,3j,Di+1,3j+1), (D-X23)
Di,3j+2 = f(Cri, j, Di,3j, Di, 3j+4), (D-X24)
Di+1,3j= f(Cbi+1,j, Di,3j, Di+1,3j+1), (D-X25)
Di+1,3j+3= f(Cri+1,j,Di+1,3j+1,Di+1,3j+5) (D-X26)
ctdp_packing_type = 1
i = 0, 2, 4…, (H-2) and j = 0, 2, 4…, (2*WD-2)
Yi+1,j
8 YCbCr components
Di,3j
Di,3j+2
Di,3j+4
Di,3j+1
Di.3j+3
8 depth pixels
Yi,j
Cbi,j
Cri,j
Yi,j+1
Cbi+1,j
Cbi,j
Cbi+1,j
Yi+1.j+1
Cri,j
Cri+1,j
Cri+1,j
Di.3j+5
Di+1,3j
Di+1,3j+2
Di+1,3j+4
Di+1,3j+1
Di+1,3j+3
Di+1,3j+5

## Slide 24: Relationship of Depacked Depth and Texture
ctdp_packing_type=0 and H is divisible to 36

## Slide 25: Relationship of Depacked Depth and Texture
ctdp_packing_type=1 and W is divisible to 48

## Slide 26: Depth Parameters Related Syntax (Transferred and Revised from 3D-HEVC)

## Slide 27: Depth Parameter Related Flags
baseline_dist_flag equal to 0 specifies that the syntax elements specifying the baseline distance are not present in the syntax structure. baseline_dist_flag equal to 1 specifies that the syntax elements specifying the baseline distance value are present in the syntax structure.
focal_length_flag equal to 0 specifies that the syntax elements specifying the focal length are not present in the syntax structure. focal_length_pixel_flag equal to 1 specifies that the syntax elements specifying the focal length value are present in the syntax structure.
z_near_flag equal to 0 specifies that the syntax elements specifying the nearest depth value are not present in the syntax structure. z_near_flag equal to 1 specifies that the syntax elements specifying the nearest depth value are present in the syntax structure.
z_far_flag equal to 0 specifies that the syntax elements specifying the farthest depth value are not present in the syntax structure. z_far_flag equal to 1 specifies that the syntax elements specifying the farthest depth value are present in the syntax structure.
d_min_flag equal to 0 specifies that the syntax elements specifying the minimum disparity value are not present in the syntax structure. d_min_flag equal to 1 specifies that the syntax elements specifying the minimum disparity value are present in the syntax structure.
d_max_flag equal to 0 specifies that the syntax elements specifying the maximum disparity value are not present in the syntax structure. d_max_flag equal to 1 specifies that the syntax elements specifying the maximum disparity value are present in the syntax structure.

## Slide 28: depth_representation_type
Value | Interpretation
0 | Each recovered depth value represents an inverse of Z value that is uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the recovered depth value equal to 0 represents the inverse of ZFar (specified below). When z_near_flag is equal to 1, the recovered depth value equal to maxVal represents the inverse of ZNear (specified below).
1 | Each recovered depth value represents disparity that is uniformly quantized into the range of 0 to maxVal, inclusive. When d_min_flag is equal to 1, the recovered depth value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the recovered depth value equal to maxVal represents DMax (specified below).
2 | Each recovered depth value represents a Z value uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the recovered depth value equal to 0 corresponds to ZFar (specified below). When z_near_flag is equal to 1, the recovered depth value equal to maxVal represents ZNear (specified below).
3 | Each recovered depth value represents a nonlinearly mapped disparity, normalized in range from 0 to maxVal, as specified by depth_nonlinear_representation_num_minus1 and depth_nonlinear_representation_model[i]. When d_min_flag is equal to 1, the recovered depth value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the recovered depth value equal to maxVal represents DMax (specified below).
Other values | Reserved for future use
The variable maxVal is set equal to ( 1 << ( 8 + bit_depth_luma_minus8 ) ) − 1, where bit_depth_luma_minus8 is the value included in or inferred for the active SPS of the layer with nuh_layer_id equal to targetLayerId.
depth_representation_type specifies the representation definition of the recovered depth values as specified in Table D-X3. In Table D-X3, disparity specifies the horizontal displacement between two texture views and Z value specifies the distance from a camera.

## Slide 29: depth_representation_type versus disparity
depth_representation_type = 1:
di,j = ( / maxVal) * DMax – DMin) + DMin. (D-X71)
depth_representation_type = 0:
Zi,j = 1 / {( / maxVal) * (1/ZNear – 1/ZFar) – 1/ZFar}. (D-X72)
depth_representation_type = 2:
Zi,j = ( / maxVal) * (ZFar – ZNear)– ZNear. (D-X73)
depth_representation_type = 0 or 2:
di,j = Bdistance * Flength ÷ Zi,j (D-X74)

## Slide 30: Representation information element syntax
The syntax structure specifies the value of an element in the view synthesis representation information SEI message.
The syntax structure sets the values of the OutSign, OutExp, OutMantissa and OutManLen variables that represent a floating-point value. When the syntax structure is included in another syntax structure, the variable names OutSign, OutExp, OutMantissa and OutManLen are to be interpreted as being replaced by the variable names used when the syntax structure is included.
da_sign_flag equal to 0 indicates that the sign of the floating-point value is positive. da_sign_flag equal to 1 indicates that the sign is negative. The variable OutSign is set equal to da_sign_flag.
da_exponent specifies the exponent of the floating-point value. The value of da_exponent shall be in the range of 0 to 27 − 2, inclusive. The value 27 − 1 is reserved for future use by ITU-T | ISO/IEC. Decoders shall treat the value 27 − 1 as indicating an unspecified value. The variable OutExp is set equal to da_exponent.
da_mantissa_len_minus1 plus 1 specifies the number of bits in the da_mantissa syntax element. The value of da_mantissa_len_minus1 shall be in the range of 0 to 31, inclusive. The variable OutManLen is set equal to da_mantissa_len_minus1 + 1.
da_mantissa specifies the mantissa of the floating-point value. The variable OutMantissa is set equal to da_mantissa.
view_syn_rep_info_element( OutSign, OutExp, OutMantissa, OutManLen ) { | Descriptor
da_sign_flag | u(1)
da_exponent | u(7)
da_mantissa_len_minus1 | u(5)
da_mantissa | u(v)
} | 

## Slide 31: Depth parameter variables and syntax elements
x | s | e | n | v
Bdistance | BdistanceSign | BdistanceExp | BdistanceMantissa | BdistanceManLen
Flength | FlengthSign | FlengthExp | FlengthMantissa | FlengthManLen
ZNear | ZNearSign | ZNearExp | ZNearMantissa | ZNearManLen
ZFar | ZFarSign | ZFarExp | ZFarMantissa | ZFarManLen
DMax | DMaxSign | DMaxExp | DMaxMantissa | DMaxManLen
DMin | DMinSign | DMinExp | DMinMantissa | DMinManLen
The variables in the x column of table are derived from the respective variables in the s, e, n and v columns as follows:
– If the value of e is in the range of 0 to 127, exclusive, x is set equal to ( −1 )s* 2e - 31 * ( 1 + n ÷ 2v ).
– Otherwise (e is equal to 0), x is set equal to ( −1 )s * 2−( 30 + v ) * n.
The DMin and DMax values, when present, are specified in units of a luma sample width of the coded picture.
The units for the ZNear and ZFar, when present, are identical but unspecified.
When depth_representation_type is equal to 0 or 2, the disparity D can further be obtained from the value of Z, Bdistance, and Flength, where D = Bdistance × Flength ÷ Z

## Slide 32: Other Syntax Elements
depth_nonlinear_representation_num_minus1 plus 2 specifies the number of piecewise linear segments for mapping of depth values to a scale that is uniformly quantized in terms of disparity.
depth_nonlinear_representation_model[ i ] for i ranging from 0 to depth_nonlinear_representation_num_minus1 + 2, inclusive, specify the piecewise linear segments for mapping of the recovered depth values to a scale that is uniformly quantized in terms of disparity. The values of depth_nonlinear_representation_model[0] and depth_nonlinear_representation_model[ depth_nonlinear_representation_num_minus1 + 2 ] are both inferred to be equal to 0.
centralized_texture_depth_packing_persistence_flag specifies the persistence of the centralized texture-depth packing arrangement SEI message.
centralized_texture-depth_packing_persistence_flag equal to 0 specifies that the centralized texture-depth packing arrangement SEI message applies to the current decoded frame only.
centralized_texture-depth_packing_persistence_flag equal to 1 specifies that the centralized texture-depth packing arrangement SEI message persists in output order until any of the following conditions are true:
– A new CVS begins.
– The bitstream ends.
– A frame in an access unit containing a centralized texture-depth packing SEI message with the same

## Slide 33: Experimental Results with Texture-based Upsampling

## Slide 34: CTDP-LR Format Depacking Procedure
Horizontal Upsample to
Original Texture Frame
Horizontal Splitting
W
WT
H
6*WD
H
WD
WD
H
H
H
WD
WD
WT
H
Horizontal Flipping
& Merging
YCbCr Components To
Depth Horizontal Depacking
2*WD
H
Spatial Upsample in
Horizontal Direction
W
H
Hierarchical Evolution Weighted Upsampling
W
H
Hierarchical Evolution Weighted Upsampling

## Slide 35: Texture-based Depth Upsampling (TDU)
Create a Reliable Index Map
At the center pixel p, we open an 5x5 window to search maximum depth value (Dmax) and minimum depth value (Dmin) if the difference of the maximum and minimum values are less than a threshold t, we will set it as reliable depth pixel as
Rp, Reliable Index Map
Reliable Index Map:
Remove depth values as undecided values for unreliable Index pixels

## Slide 36: Iterative TDU Process
Iterative TDU Process
Depth map with
Undecided pixels
N is the normalization factor.
Rq is reliable index. If neighborhood pixel q is reliable, Rq =1, else Rq =0.
d is depth candidate from neighborhood pixels
1st iterative depth map
2nd iterative depth map

## Slide 37
Sequences | Clipped Resolution | Frames | 1 View | Synthesized View
Undo Dancer | 1920×1080 | 250 | 3 | 4
Shark | 1920×1080 | 300 | 5 | 7
Computer Generated Test Sequences

## Slide 38: Experimental Settings
Uncoded and Coded HD Computer Generated Videos:
ratios of depth region :
CTDP LR: Depth: 1/12, Texture: 11/12
HEVC-CTDP Coding Parameters:
encoding mode: All Intra, Low delay, Random access
QP: 27,32,37,42
ctdp_packing_type: CTDP-LR
image resizing: Lancos 4
depth resizing: bicubic (with TDU/without TDU)

## Slide 39
CTDP depacked texture, depth, and synthesized view are compared to ground truth ones
Uncoded CTDP Performances
of YCbCr Color Packing Method

## Slide 40
Performances of Uncoded CTDP-LR Formats
CTDP-LR: ctdp_packing_type = 1
Performances | Depacked Texture and Depth |  |  |  |  |  | Synthesized Virtual View Generated by VSRS |  | 
 | Depacked Texture |  |  | Depacked Depth |  |  |  |  | 
 | Direct RGB | Direct YCbCr | Direct YCbCr+ | Direct RGB | Direct YCbCr | Direct YCbCr+ | Direct RGB | Direct YCbCr | Direct YCbCr+
PSNR | 49.2443 | 49.2137 | 50.2522 | 35.9820 | 39.8881 | 40.5137 | 36.0823 | 38.2884 | 39.1031
SSIM | 0.9955 | 0.9958 | 0.9963 | 0.9802 | 0.9873 | 0.9886 | 0.9737 | 0.9882 | 0.9879
Direct YCbCr: Direct YCbCr colour depth packing method;
Direct YCbCr+: Direct YCbCr colour depth packing method with TDU method.

## Slide 41
Depacked Depth from Uncoded CTDP-LR Format
Depacked Depth for Direct RGB Colour Packing (YCbCr 4:2:0)

## Slide 42
Depacked Depth of Direct YCbCr Colour Depth (YCbCr 4:2:0)
Depacked Depth from Uncoded CTDP-LR Format

## Slide 43
Depacked Depth from Uncoded CTDP-LR Format
Depacked Depth of Direct YCbCr with TDU Method (YCbCr 4:2:0)

## Slide 44
Uncompressed Subjective Results (Fin Area)
(a) Direct RGB Method (b) Direct YCbCr Method (c) Direct YCbCr+TDU Method

## Slide 45
HEVC-coded CTDP Performances
of YCbCr Color Packing Methods
CTDP-HEVC decoded and depacked texture, depth, and VSRS synthesized view are compared to those by 3D-HEVC decoded ones

## Slide 46
HEVC-coded CTDP-LR Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  |  | Depacked Depth |  |  | Virtual View by VSRS |  | 
 | Direct RGB | Direct YCbCr | Direct YCbCr+ | Direct RGB | Direct YCbCr | Direct YCbCr+ | Direct RGB | Direct YCbCr | Direct YCbCr+
ra | 7.9095 | 11.7019 | 10.0607 | 16.5991 | 26.5047 | 22.3624 | 61.9436 | 67.8342 | 58.9028
ldp | 3.4178 | 6.9614 | 5.8712 | -36.2061 | -30.2637 | -30.9079 | 39.226 | 42.2946 | 35.7900
ai | 0.9848 | 3.7328 | 2.5841 | 30.3497 | 27.8123 | 27.3386 | 73.1888 | 69.7477 | 60.3423
ave | 4.1040 | 7.4653 | 6.1720 | 3.5809 | 8.0178 | 6.2644 | 58.119 | 59.9588 | 51.6783
Coding Modes | Depacked Texture |  |  | Depacked Depth |  |  | Virtual View by VSRS |  | 
 | Direct RGB | Direct YCbCr | Direct YCbCr+ | Direct RGB | Direct YCbCr | Direct YCbCr+ | Direct RGB | Direct YCbCr | Direct YCbCr+
ra | -0.2415 | -0.3560 | -0.3090 | -1.2349 | -1.0712 | -0.9416 | -1.3615 | -1.3992 | -1.2734
ldp | -0.1122 | -0.2231 | -0.1901 | 0.9894 | 1.3046 | 1.3853 | -0.9979 | -1.0077 | -0.8752
ai | -0.0344 | -0.1370 | -0.0954 | -2.4781 | -1.6007 | -1.5509 | -1.732 | -1.6165 | -1.4785
ave | -0.1293 | -0.2387 | -0.1981 | -0.9079 | -0.4558 | -0.3691 | -1.3638 | -1.3411 | -1.2090
Direct YCbCr: Direct YCbCr colour depth packing method;
Direct YCbCr+: Direct YCbCr colour depth packing method with TDU method.

## Slide 47
Depacked Depth of Direct RGB Color Packing (YCbCr 4:2:0)
Depacked Depth of Coded CTDP-LR Format
(QP=27)

## Slide 48
Depacked Depth of Direct YCbCr Color Packing (YCbCr 4:2:0)
Depacked Depth of Coded CTDP-LR Format
(QP=27)

## Slide 49
Depacked Depth of Direct YCbCr Packing with TDU Method (YUV4:2:0)
Depacked Depth of Coded CTDP-LR Format
(QP=27)

## Slide 50
Compressed Subjective Results (Fin Area)
(a) Direct RGB Method (b) Direct YUV Method (c) Direct YUV+TDU Method

## Slide 51: Conclusions

## Slide 52: Conclusions
This document is a revision of Output Document JCTVC-AA1008 by keeping YCbCr colour packing method and removing irrelevant parts. .
The revision covers the cases of general depth values with 8 bits or more by checking “bit_depth_luma_minus8” and “bit_depth_chroma_minus8”.
To improve the packing performance, we optionally suggest a texture-based upsampling method, which can further reduce about 8.3% bitrate or improve 0.24dB in average.
In Taiwan, the CTDP formats in assigned RGB coulor packing method have been adopted in HYA Company to deliver the 3D video and AR/VR services in CATV systems. The direct YCbCr color packing method will be redesigned with 4K OTT platform currently.

## Slide 53
Thanks for your attentions !