## Slide 1: Coding efficiency test on large block size transforms in HEVC
Minhua Zhou (zhou@ti.com) Texas Instruments Inc., USA
JVTVC-B028

## Slide 2: Large block size transforms
Large block size 16x16, 32x32, 64x64 transforms proposed in TMuC
Large block size transforms have serious area impact
Coding efficiency and complexity trade-off should be carefully studied
Coding efficiency test results are presented

## Slide 3: Test Conditions
Software: striped-down version of A124 reference software
Number of frames: only the first 121 frames are used
Coding settings: followed the ones in Alpha.bat; Beta.bat (CU sizes, GOP structures, QPs)
I-frame only coding mode is also tested

## Slide 4: Test Results (I+B+P and I+P modes)
 | BD-rate difference (%) (up to 32x32 transform size vs. up to 64x64 transform size) |  |  | BD-rate difference (%) (up to 16x16 transform size vs. up to 64x64 transform size) |  | 
Alpha settings (IBP) | Average | Min | Max | Average | Min | Max
Class A | -0.12 | -0.01 | -0.17 | -0.38 | -0.06 | -0.71
Class B | -0.56 | 0.00 | -0.90 | -2.74 | -0.26 | -5.82
Class C | -0.12 | 0.02 | -0.35 | -0.92 | -0.22 | -2.42
Class D | 0.06 | 0.15 | 0.02 | -0.49 | 0.00 | -0.81
All | -0.21 |  |  | -1.34 |  | 
Beta settings (IP) | Average | Min | Max | Average | Min | Max
Class B | -0.66 | 0.03 | -1.56 | -3.18 | -0.09 | -6.06
Class C | -0.31 | -0.05 | -1.05 | -1.33 | -0.32 | -3.42
Class D | 0.01 | 0.09 | -0.09 | -0.33 | 0.03 | -0.73
Class E | -0.63 | -0.49 | -0.77 | -2.55 | -2.15 | -2.82
All | -0.40 |  |  | -1.89 |  | 
Table 1. Experimental results for I+B+P (Alpha) and I+P (Beta) coding

## Slide 5: Test Results (I-frame only)
 | BD-rate difference (%) (up to 32x32 transform size vs. up to 64x64 transform size) |  |  | BD-rate difference (%) (up to 16x16 transform size vs. up to 64x64 transform size) |  | 
Alpha settings (I-only) | Average | Min | Max | Average | Min | Max
Class A | 0.04 | 0.06 | -0.02 | -0.11 | -0.04 | -0.19
Class B | -0.59 | -0.02 | -1.52 | -2.81 | -0.39 | -8.77
Class C | -0.05 | 0.03 | -0.23 | -0.41 | -0.03 | -1.32
Class D | -0.02 | 0.00 | -0.07 | -0.17 | 0.01 | -0.52
All | -0.21 |  |  | -1.10 |  | 
Beta settings (I-only) | Average | Min | Max | Average | Min | Max
Class B | -0.66 | -0.03 | -1.79 | -2.92 | -0.39 | -9.11
Class C | -0.05 | 0.02 | -0.23 | -0.41 | -0.02 | -1.32
Class D | -0.01 | 0.00 | -0.06 | -0.16 | 0.03 | -0.52
Class E | -0.36 | -0.21 | -0.62 | -1.60 | -1.18 | -2.35
All | -0.29 |  |  | -1.36 |  | 

## Slide 6: Observations
On average the gain provided by the large size transforms (32x32 and 64x64) is around 1 ~ 2%.
However, the larger gain is observed in 1080p (Class B) sequences, in which an average gain around 3% (peak 6 – 9 %) was measured.
The additional gain by adding 64x64 transform on the top of 32x32 transform is very limited.
The large size transform is more effective in the cases where the inter-prediction is less effective.