## Slide 1: JCTVC-B035: Improved Quantization for HEVC
<number>
July 23, 2010
Dake He, Xiang Yu, En-hui Yang
Research in Motion Ltd., Canada
Notes: <number>

## Slide 2: Outline
<number>
Background
  Scalar quantization
  Minimizing distortion design
  Minimizing RD cost design
Related work
  Adaptive rounding
  Soft decision quantization/RDOQ
  Adaptive quantization table
Proposed design
Results
Notes: <number>

## Slide 3: Background
<number>
Uniform scalar quantizer given by a step size q:
    Quantization: u = floor ( c / q + δ ) Partition
    De-Quantization: cˆ = u ∙ q Reconstuction
q
0
3q
2q
(1- δ)∙q
(2- δ)∙q
(3- δ)∙q
(4- δ)∙q
Notes: <number>

## Slide 4: Background
<number>
Generic scalar quantizer designing rules for minimizing distortion (Lloyd-max algorithm)
    The nearest neighbor rule
    The centroid rule
q2
q1
q3
q4
A1
A2
A3
Notes: <number>

## Slide 5: Background
<number>
Generic scalar quantizer designing rules for minimizing RD cost
Min d( c – c^ ) +λ r(u) + λ r({qi})
{Ai}: mapping from c to u
{qi}: mapping from u to c^
Optimize with respects to partitions and reconstruction levels.
q1
0
q2
q3
q4
Notes: <number>

## Slide 6: Related work
<number>
Adaptive rounding
Uniform reconstruction levels given as {0, q, 2q, …}
u = floor ( c / q + δ )
q
0
3q
2q
(1- δ)∙q
(2- δ)∙q
(3- δ)∙q
(4- δ)∙q
Notes: <number>

## Slide 7: Related work
<number>
Soft decision quantization / RDOQ
Min d( c – c^ ) +λ r(u) + λ r(q)
{Ai}: dynamic programming or simplified search
{qi}: Given by {0, q, 2q, …}
Optimize with respects to partitions, but reconstruction levels are still given as {0, q, 2q, …}.
q
0
2q
3q
4q
Notes: <number>

## Slide 8: Related work
<number>
Adaptive quantization table/multiple quantizers
Uniform partitions;
Uniform reconstruction levels {0, q(1), 2q(1), …}.
Q1: u = floor ( c / q(1) + δ )
Q2: u = floor ( c / q(2) + δ )
Uniform partitions;
Uniform reconstruction levels {0, q(2), 2q(2), …}.
Notes: <number>

## Slide 9: Proposed design
<number>
Adaptive reconstruction levels for decoding
cˆ = 0, |u|=0
q1, |u|=1
q2, |u|=2
q3, |u|=3
…
cˆ = 0, |u|=0
q1, |u|=1
q2, |u|=2
u∙q, |u|>=3
q1
0
q2
q3
u=0
u=1
u=2
u=3
q1
0
q2
3q
u=0
u=1
u=2
u=3
4q
u∙q
u=4
u=5
u>3
q4
q5
Notes: <number>

## Slide 10: Proposed design
<number>
Encoding with adaptive reconstruction levels
  It works with multiple quantizers.
  Slice/CU level uniform quantization to collect {q1, q2 , q} for each quantizer.
  At block level, apply RDOQ with given {q1, q2 , q}
  Update {q1, q2 , q} based on the RDOQ outputs of {u}.
q1
0
q2
3q
u∙q
u>3
Notes: <number>

## Slide 11: Results: Bqsquare (416x240)
<number>
 | RDOQ |  | Proposed | 
QP | BitRate | PSNR | BitRate | PSNR
27 | 1517.4 | 35.0678 | 1202.72 | 34.4577
30 | 767.22 | 32.7269 | 576.48 | 32.2734
33 | 342 | 30.7754 | 267.38 | 30.5076
35 | 213 | 29.6 | 168.92 | 29.4006
BD-PSNR gain = 0.27dB BD-Rate saving = -9.9%
Notes: <number>

## Slide 12: Results: Racehorse (416x240)
<number>
 | RDOQ |  | Proposed | 
 | BitRate | PSNR | BitRate | PSNR
25 | 2646.78 | 37.5987 | 2298.92 | 36.9167
27 | 2029.68 | 36.0814 | 1761.02 | 35.4345
30 | 1342.02 | 33.9161 | 1146.74 | 33.3172
33 | 846.18 | 31.7994 | 731.06 | 31.3323
BD-PSNR gain = 0.14dB
BD-Rate saving = -2.8%
Notes: <number>

## Slide 13: Results: BQmall (832x480)
<number>
 | RDOQ |  | Proposed | 
QP | Bitrate | PSNR | Bitrate | PSNR
27 | 1868.1 | 37.0705 | 1507.4 | 36.706
30 | 1162.86 | 35.2954 | 959.72 | 34.9904
33 | 736.8 | 33.4943 | 612.92 | 33.2406
35 | 553.8 | 32.2512 | 458.6 | 32.0072
BD-PSNR gain = 0.46dB
BD-Rate saving = -11.1%
Notes: <number>

## Slide 14: Results: Basketball (832x480)
<number>
 | RDOQ |  | Proposed | 
QP | Bitrate | PSNR | Bitrate | PSNR
27 | 1726.75 | 37.3502 | 1475.25 | 37.128
30 | 1086.45 | 35.7271 | 937.65 | 35.5418
33 | 694 | 34.2392 | 609.8 | 34.0664
35 | 511.4 | 33.2043 | 453.65 | 33.0434
BD-PSNR gain = 0.29 dB
BD-Rate saving = -8.3%
Notes: <number>

## Slide 15: Results: PartyScene (832x480)
<number>
 | RDOQ |  | Proposed | 
QP | Bitrate | PSNR | Bitrate | PSNR
27 | 6112.35 | 35.0492 | 5078.7 | 34.61
30 | 3691.3 | 32.764 | 3066.3 | 32.4034
33 | 2210.45 | 30.6462 | 1856.8 | 30.3863
35 | 1573.5 | 29.2505 | 1307.55 | 29.0118
BD-PSNR gain = 0.43dB
BD-Rate saving = -9.6%
Notes: <number>

## Slide 16: Results:
<number>
Sequence | BD-PSNR (dB) | BD-bitrate (%)
BQ-Square 240p | 0.27 | -9.9
Race-horse 240p | 0.14 | -2.8
Basketballpass 240p | 0.25 | -6.3
BlowingBubble 240p | 0.23 | -7.1
BQ-Mall 480p | 0.46 | -11.1
Basketball drill 480p | 0.29 | -8.3
PartyScene 480p | 0.43 | -9.8
Racehorse 480p | 0.07 | -1.9
Vidyo-1 720p | 0.30 | -12.2
Vidyo-3 720p | 0.21 | -9.1
Vidyo-4 720p | 0.31 | -14.6
Notes: <number>

## Slide 17
<number>
The proposed method minimizes the rate distortion coding cost with respect to the partitions and the reconstruction levels.
Recommend to be included in TMuC for further experiments.
Conclusion
q1
0
q2
3q
u∙q
u>3
Notes: <number>

## Slide 18
<number>
Notes: <number>

## Slide 19
<number>
1241 2260 1085 -2
217 212 61 -2
1.21 2.20 3.176 4.236 5.295 …
Notes: <number>

## Slide 20: HDQ+ARL
<number>
One pass
Uniform partition
Adaptive reconstruction levels
q1
0
q2
(1- δ)∙q
(2- δ)∙q
(3- δ)∙q
(4- δ)∙q
q3
Notes: <number>