## Slide 1: TE1: Huawei report on DMVD improvements
26/7/30
Sixin Lin, Mingyuan Yang, Jiantong Zhou, Jin Song, Dong Wang, Haitao Yang, Jiali Fu, Haoping Yu
Yue Wang, Li Zhang, Siwei Ma, Wen Gao
Huawei Technologies Co., Ltd. & Peking University
Notes: <number>

## Slide 2: Contents
Page <number>
Simplified DMVD(SDMVD)
Spatial Temporal Direct Mode (STDM)
Compression Performance
Complexity Analysis
Improved STDM in P Slice
Conclusion
Notes: <number>

## Slide 3: SDMVD-Block Diagram of DMVD
Page <number>
Build template for
current MB
Build Motion Vector
Candidate Set for
current MB
Template Matching
In ME
Predict Current Block
In MC
In Motion Estimation procedure, H.264
wiener filter or AIF filter is used to
interpolate reference template.
In Motion Compensation procedure, H.264
wiener filter or AIF filter is used to interpolate
reference block.
Notes: <number>

## Slide 4: SDMVD-Block diagram of SDMVD
Page <number>
Build template for
current MB
Build Motion Vector
Candidate Set for
current MB
Template Matching
In ME
Predict Current Block
In MC
In Motion Estimation procedure, Bilinear filter is
used to interpolate reference template.
In Motion Compensation procedure, H.264
wiener filter or AIF filter is used to interpolate
reference block.
Notes: <number>

## Slide 5: SDMVD
Page <number>
Bilinear Interpolation of SDMVD
h = (A + C + 1) / 2;
m = (B + D +1) / 2;
b = (A + B + 1) / 2;
s = (C + D + 1) / 2;
j = (b + s + 1) / 2;
a = (A + b +1 ) /2;
…………
Notes: <number>

## Slide 6: SDMVD-Complexity Analysis
Page <number>
Decoding time for CS1
Video Sequences | rwthDMVD | SDMVD
Class A | 614.86 | 252.92
Class B | 259.75 | 135.24
Class C | 55.43 | 27.50
Average | 245.74 | 114.80
Decoding time for CS2
Video Sequences | rwthDMVD | SDMVD
Class B | 421.19 | 182.90
Class C | 102.75 | 42.44
Average | 279.66 | 120.48
53%↓
57%↓
Notes: <number>

## Slide 7: SDMVD- Compression Performance Analysis
Page <number>
RD Performance for CS1 (ExtMB=1)
RD Performance for CS2 (ExtMB=1)
Video Sequences | rwthDMVD |  | SDMVD | 
 | BDPSNR | BDRATE | BDPSNR | BDRATE
 | [dB] | [%] | [dB] | [%]
Class B | 0.12 | -4.55 | 0.11 | -4.34
Class C | 0.13 | -3.11 | 0.13 | -3.11
Average | 0.12 | -3.91 | 0.12 | -3.80
Video Sequences | rwthDMVD |  | SDMVD | 
 | BDPSNR | BDRATE | BDPSNR | BDRATE
 | [dB] | [%] | [dB] | [%]
Class A | 0.16 | -3.64 | 0.15 | -3.4
Class B | 0.16 | -5.18 | 0.15 | -4.95
Class C | 0.12 | -2.93 | 0.12 | -2.93
Average | 0.14 | -4.08 | 0.14 | -3.93
SDMVD has equivalent
RD performance as rwthDMVD.
Notes: <number>

## Slide 8: STDM
Page <number>
STDM is proposed here which could exploit both spatial and temporal information and improve coding efficiency.
Notes: <number>

## Slide 9: STDM
Page <number>
1 Selection of the reference frames
2 Motion vector candidate set
Notes: <number>

## Slide 10: STDM
Page <number>
3 Derivation of motion vector pairs
4 Best motion vector pair calculation
Cost = SAD(MBforward, MBcorresponding)+lambda*SAD(Templateforward, Templatecurrent) +lambda*SAD(Templatecorresponding, Templatecunrent)
Assuming that the motion of objects is translational with constant speed, the corresponding motion vector is obtained by the following formula:
3 Derivation of motion vector pairs
Notes: <number>

## Slide 11: STDM in P Slice and B Slice
Page <number>
In P slice, AVC P_SKIP mode is replaced by STDM PSKIP in macroblock 32x32 level. DMVD P_SKIP and STDM P_SKIP mode are selected in macroblock 16x16 level. One flag is needed to indicate which specific method is chosen in P_SKIP mode.
In B Slice, AVC B_SKIP/B_DIRECT and STDM B_SKIP/B_DIRECT are used in macroblock 16x16 and 32x32 levels. One flag for B_SKIP/B_DIRECT mode is needed to indicate which specific method is chosen in B SKIP/DIRECE mode.
Notes: <number>

## Slide 12: Compression Performance
Page <number>
RD performance for CS1 relative to TE1 anchor (ExtMB=1)
Video Sequences | SDMVD_STDM |  | SDMVD_SSTDM | 
 | BDPSNR | BDRATE | BDPSNR | BDRATE
 | [dB] | [%] | [dB] | [%]
Class A | 0.25 | -5.68 | 0.25 | -5.75
Class B | 0.23 | -7.53 | 0.23 | -7.55
Class C | 0.17 | -4.05 | 0.17 | -4.11
Average | 0.21 | -5.93 | 0.21 | -5.97
RD performance for CS2 relative to TE1 anchor (ExtMB=1)
total gain :
about 6% bitrate ↓
0.2 dB PSNR↑
total gain :
about 4.7% bitrate ↓
0.15 dB PSNR↑
Video Sequences | SDMVD_STDM |  | SDMVD_SSTDM | 
 | BDPSNR | BDRATE | BDPSNR | BDRATE
 | [dB] | [%] | [dB] | [%]
Class B | 0.14 | -4.66 | 0.14 | -4.74
Class C | 0.15 | -3.99 | 0.15 | -4.07
Average | 0.15 | -4.75 | 0.15 | -4.74
Notes: <number>

## Slide 13: Complexity Performance
Page <number>
Decoding Time for CS1 relative to TE1 anchor
Decoding Time for CS2 relative to TE1 anchor
Video Sequences | Anchor | SDMVD_STDM | SDMVD_SSTDM
Class A | 124.07 | 289.72 | 257.42
Class B | 61.67 | 130.85 | 115.90
Class C | 11.21 | 26.90 | 24.23
Average | 54.67 | 121.93 | 108.30
Video Sequences | Anchor | SDMVD_STDM | SDMVD_SSTDM
Class B | 58.62 | 206.22 | 193.08
Class C | 11.32 | 43.88 | 41.99
Average | 37.60 | 134.07 | 125.93
In cs1 the decoding time of proposed SDMVD_SSTDM is 1 times slower than TE1 anchor
In cs2 the decoding time of proposed SDMVD_SSTDM is 2.35 times slower than TE1 anchor
Notes: <number>

## Slide 14: Improvement STDM in P Slice
Page <number>
We recently find out instead of using DMVD P_SKIP with STDM P_SKIP in P slice, using AVC P_SKIP and STDM P_SKIP can obtain better compression performance. Now AVC P_SKIP and STDM P_SKIP are used in macroblock 16x16 and 32x32 levels.
Notes: <number>

## Slide 15: Improved STDM in P slice
Page <number>
RD performance for CS1 relative to TE1 anchor (ExtMB=1)
RD performance for CS2 relative to TE1 anchor (ExtMB=1)
Video Sequences | SDMVD_STDM |  | SDMVD_SSTDM | 
 | BDPSNR | BDRATE | BDPSNR | BDRATE
 | [dB] | [%] | [dB] | [%]
Class A | 0.25 | -5.71 | 0.25 | -5.79
Class B | 0.23 | -7.51 | 0.23 | -7.56
Class C | 0.17 | -4.15 | 0.17 | -4.08
Average | (0.21)0.21 | (-5.93)-5.96 | (0.21)0.21 | (-5.97)-5.98
Video Sequences | SDMVD_STDM |  | SDMVD_SSTDM | 
 | BDPSNR | BDRATE | BDPSNR | BDRATE
 | [dB] | [%] | [dB] | [%]
Class B | 0.16 | -5.90 | 0.16 | -6.05
Class C | 0.15 | -3.67 | 0.15 | -3.73
Average | (0.15)0.15 | (-4.75)-4.91 | (0.15)0.16 | (-4.74)-5.02
Data in red color are data of old implementation
Notes: <number>

## Slide 16: Conclusion
Page <number>
  In this proposal we present the detailed description of our SDMVD and STDM together with the analysis of coding performance and complexity.
  Compared with TE1 anchor bitstreams, 6% of bitrate saving can be achieved in CS1 and 5% of bitrate saving in CS2.
Notes: <number>

## Slide 17
Page <number>
Thank you
www.huawei.com