## Slide 1: JCTVC-B038 Performance Improved Directional Transform Techniques for HEVC
Dong Wang
Huawei Technologies
July 2010
Notes: <number>

## Slide 2: Content
Directional Multiple Transform Technique (DMT)
  Overview
  Updated Techniques
  Experimental Results
  Analysis
Rate-Distortion Optimized Transform (RDOT)
  Overview
  Updated Techniques
  Experimental Results

## Slide 3: DMT – Technique Overview
Directional Transforms
  Multiple directional transforms are trained offline, according to the texture direction of the residual block.

## Slide 4: DMT – Technique Overview
Encoding Flow
  The trained directional transforms for 8 directions, together with DCT transforms are evaluated through RDO process, and the best transform is selected.

## Slide 5: DMT – Technique Overview
Syntax Description
  DCT/Directional Trasnform flag
  Directional Transform Index

## Slide 6: DMT – Updated Techniques
Temporal Predictive Coding
  Direction of the predictor block (DP) is closed correlated with the current residual block (DR).
  Predictive coding: Direction difference is encoded. diff = DP - DR
  CABAC: Fixed-length binarization is used.

## Slide 7: DMT – Experimental Results
Implementation
  The software is based on the KTA 2.6r1, and currently the it is only applied on the 8x8 transform block.
Test condition
  Based on VCEG-AJ10r1
  New KTA tools are switched off.
  Large MB is switched off. Note: the large MB includes the large transform and it is to be studied by the AhG, and therefore it is not switched on.
  CS1 and CS2, defined by CfP, are used.
  QP_I = are 22, 27, 32, 37. QP_P, QP_FirstBLayer, QP_SecondBLayer and QP_ThirdBLayer are QP_I+1, QP_I+2, QP_I+3 and QP_I+4, respectively.

## Slide 8: DMT – Experimental Results
RD performance
 | CS1 |  | CS2 | 
Sequence | BD-RATE(%) | BD-PSNR(dB) | BD-RATE(%) | BD-PSNR(dB)
Class A | -0.558 | 0.023 | -1.571 | 0.061
Class B | -1.060 | 0.026 | -2.300 | 0.062
Class C | -1.790 | 0.077 | -3.128 | 0.135
Class D | -1.113 | 0.050 | -2.205 | 0.101
Class E | N/A | N/A | -2.273 | 0.071
Average of all sequences: | -1.202 | 0.045 | -2.377 | 0.088

## Slide 9: DMT – Experimental Results
Analysis and future work
  The CS2 gain is about 2.5%, and is better that the result for CS1. Analysis: The current B frame implementation is the same as P frame. However since there are much less residuals in B frames, the implementation could be further optimized.
  The performance for class A sequences is worse than other sequences.
  The residuals are less significant that of the smaller sequences, and the better 8x8 transforms are not that helpful compared with smaller sequences. It is expected to bring better performance with the DMT technique.

## Slide 10: DMT – Experimental Results
Analysis and future work
  The current implementation is only applied on 8x8 transform blocks.
  The DMT for other transform sizes need to be implemented, especially when large block sizes are used.

## Slide 11: Content
Directional Multiple Transform Technique (DMT)
  Overview
  Updated Techniques
  Experimental Results
  Analysis
Rate-Distortion Optimized Transform (RDOT)
  Overview
  Updated Techniques
  Experimental Results

## Slide 12: RDOT – Technique Overview
RDOT
  MB layer flag indicates use of RDOT.
  Transform schemes of a residual block X for IP mode I, compared with MDDT.
F=Ci·X·Ri
F=C0i·X·R0i
F=C0i·X·R1i
F=CK-1i·X·RK-1i
T(X)
(a) MDDT
…
…
…
X
X
(b) Proposed RDOT
T(X)
Refer to: Xin Zhao, Li Zhang, Siwei Ma, Wen Gao, “Rate-Distortion Optimized Transform”,
ISO/IEC JTC1/SC29/WG11 MPEG, m16926, Xi’an, China, October 2009.

## Slide 13: RDOT – Experimental Results
Implementation
  The software is based on the KTA 2.6r1, and currently the it is only applied on all intra prediction modes.
Test condition
  Same as DMT test condition, except that All-Intra and CS1 test conditions are used.

## Slide 14: RDOT – Experimental Results
Performance compared with the anchor
 | All-intra |  | CS1 | 
Sequence | BD-RATE(%) | BD-PSNR(dB) | BD-RATE(%) | BD-PSNR(dB)
Class A | -8.76 | 0.481 | -3.32 | 0.137
Class B | -7.30 | 0.322 | -3.16 | 0.086
Class C | -6.73 | 0.453 | -3.10 | 0.134
Class D | -6.82 | 0.500 | -2.64 | 0.120
Class E | -9.65 | 0.539 | -4.73 | 0.157
Average of all sequences: | -7.62 | 0.449 | -3.03 | 0.115

## Slide 15: RDOT – Experimental Results
Complexity in terms of encoding and decoding time
  Note that the numbers represent the ratio of RDOT time to anchor time.
 | All-intra |  | CS1 | 
Sequence | Encoding | Decoding | Encoding | Decoding
Class A | 4.25 | 1.26 | 1.13 | 1.08
Class B | 4.99 | 1.29 | 1.08 | 1.07
Class C | 4.19 | 1.22 | 1.32 | 1.07
Class D | 4.80 | 1.23 | 1.02 | 1.09
Class E | 3.88 | 1.29 | 1.14 | 1.05
Average of all sequences: | 4.50 | 1.26 | 1.13 | 1.07

## Slide 16
Thank You
www.huawei.com
Notes: <number>