## Slide 1: New intra prediction using the correlation between pixels and lines
26/7/31
Changcai Lai, Yongbing Lin
Notes: <number>

## Slide 2
Agenda
Introduction
Algorithm description
Experimental results

## Slide 3: Introduction
Intra prediction in H.264/AVC uses the adjacent boundary pixels of reconstructed neighboring blocks to get the prediction of the entire coding block.
using the correlation between lines and pixels to shorten the distance of predicted pixel and its reference pixels (Dresden)
implemented RDOQ into the proposed intra prediction and fixed several bugs from Dresden meeting.

## Slide 4: Line-based intra prediction
Fig. 1. Directional prediction of 1x16 and 2x8 mode
1x16, 16x1, 2x8 and 8x2 modes are designed
For each mode, nine directional predictions are proposed
DCT of size 1x16, 16x1, 2x8 or 8x2 is applied

## Slide 5: Resample-based intra prediction
Three new MB partitions based on resampling are proposed
  A MB is decomposed into 4 blocks by down-sampling in the first level decomposition
  One of the down-sampled block is decomposed into 4 sub-blocks in the second level decomposition
Signal method: two new flags combined with the existing transform_size_8x8_flag

## Slide 6: Intra prediction and interpolation in RIP
Page <number>
Block I0 is encoded with traditional block-based intra prediction. 9 intra prediction modes
Block P1&P2 are predicted pixel-by-pixel with the reference of the block I0 by interpolation with 4-tap filter [-1 5 5 -1] horizontally and vertically, respectively.
Block P3 is predicted pixel-by-pixel with the reference of the block P1&P2 by averaging four neighboring pixels.
( I0 )
( P1 )
( P2 )
( P3 )

## Slide 7: Experimental conditions
Anchor: KTA2.6r1
CfP common test condition except that GOP structure is all intra pictures
H.264/AVC High Profile
RDO and RDOQ ON
5 QP points same as used in CfP anchor bit streams
The proposed technique is only applied to luminance component
All HEVC sequences with full length are tested

## Slide 8
Page <number>
Experimental
results
 | low-bitrate range |  | high-bitrate range | 
sequence | BD-bitrate | BD-PSNR | BD-bitrate | BD-PSNR
RaceHorses_416x240_30 | -2.80% | 0.17 | -2.83% | 0.21
BasketballPass_416x240_50 | -4.51% | 0.25 | -4.03% | 0.25
BlowingBubbles_416x240_50 | -3.21% | 0.20 | -3.22% | 0.24
BQSquare_416x240_60 | -3.25% | 0.24 | -2.95% | 0.25
Average QWVGA | -3.44% | 0.22 | -3.26% | 0.24
RaceHorses_832x480_30 | -3.71% | 0.17 | -3.53% | 0.19
BasketballDrill_832x480_50 | -7.14% | 0.32 | -7.06% | 0.32
PartyScene_832x480_50 | -4.78% | 0.22 | -4.27% | 0.24
BQMall_832x480_60 | -5.63% | 0.30 | -5.48% | 0.31
Average WVGA | -5.32% | 0.25 | -5.09% | 0.26
vidyo1_720p_60 | -7.16% | 0.40 | -7.60% | 0.42
vidyo3_720p_60 | -6.04% | 0.37 | -5.79% | 0.36
vidyo4_720p_60 | -6.44% | 0.33 | -6.33% | 0.33
Average 720P | -6.55% | 0.37 | -6.57% | 0.37
Kimono1_1920x1080_24 | -8.88% | 0.33 | -5.99% | 0.19
ParkScene_1920x1080_24 | -2.05% | 0.09 | -1.42% | 0.07
BasketballDrive_1920x1080_50 | -6.62% | 0.22 | -6.03% | 0.19
Cactus_1920x1080_50 | -4.79% | 0.19 | -4.08% | 0.16
BQTerrace_1920x1080_60 | -7.25% | 0.31 | -6.52% | 0.28
Average 1080P | -5.92% | 0.23 | -4.81% | 0.18
PeopleOnStreet_2560x1600_30_crop | -6.75% | 0.38 | -6.04% | 0.34
Traffic_2560x1600_30_crop | -4.54% | 0.25 | -3.94% | 0.22
Average 1600P | -5.65% | 0.31 | -4.99% | 0.28
Average | -5.31% | 0.26 | -4.84% | 0.25
All Bitrate Average | -5.07% 0.26 |  |  | 

## Slide 9
Notes: <number>