## Slide 1
TE3: Huawei & Hisilicon report on flexible motion partitioning coding
Xiaozhen Zheng
Haoping Yu
JCT-VC B041
Geneva, 21-28 July 2010

## Slide 2: Introduction
Investigation and improvement on the compression capability on flexible motion partitioning
Representation method for block with flexible motion partitioning
Coding of block partitioning parameters
Improved motion vector prediction for non-AVC MB partitioning

## Slide 3: Representation method for block with flexible motion partitioning
General idea
  Use two points to indicate the partitioning
  Code the position of two points
Use quad-tree design to signal partitioning
  P_L0_L0_16x8 / P_L0_L0_8x16: Horizontal / Vertical partitioning
  P_L0_16x16: Non-rectangular partitioning

## Slide 4
Horizontal / Vertical partitioning
  Use a parameter pos to indicate the size of rectangles
  pos = 0 : 16x8 / 8x16 partitioning
  pos != 0 : Asymmetric partitioning

## Slide 5
Non-rectangular partitioning
  A flag used to indicate the partitioning direction: left-down to right-up or left-up to right-down partitioning
  Parameter pos used to indicate the position of point A
  Parameter scale_factor used to indicate the position of point B (the length of BO)
    scale_factor = 0 : BO = AO
    scale_factor = 1 : BO = 0.5 x AO (22.5 degree partitioning)
    scale_factor = -1 : BO = 2 x AO (66.5 degree partitioning)

## Slide 6: Coding of block partitioning parameters
Predictive coding of position parameter pos
  Use left block (A) and up block (B)
  Form the predictive position parameter, and the difference is coded

## Slide 7: Improved motion vector prediction for non-AVC MB partitioning
Choose the neighboring blocks that has same object’s boundary as current macroblock
Horizontal partitioning: Check the left and up block’s partitioning mode sequentially

## Slide 8
Vertical partitioning: Check the up and left block’s partitioning mode sequentially

## Slide 9
Left-down to right-up partitioning: Check the left, up and up-right block’s partitioning mode

## Slide 10
Left-up to right-down partitioning: Check the left, up and up-left block’s partitioning mode

## Slide 11
If above conditions can not be satisfied, the traditional AVC median prediction is used

## Slide 12: Experiment
For horizontal / vertical partitioning case, the partitioning with the pos value +/-2, +/-4, +/-6 are tested
For non-rectangular partitioning case, +/-45, +/-22.5 and +/-66.5 degree partitioning with pos value 0 +/-4, +/-8 and +/-12 are tested
Class B, C, and D test sequences for constraint set 2 condition are chose for simulation
AIF, ALF and MDDT are turned on

## Slide 13: Experiment (continue)
ClassD |  | Bitrate Saving | ClassC | Bitrate Saving | ClassB | Bitrate Saving
BasketballPass | Low | 4.05% | BasketballDrill | 4.82% | BasketballDrive | 3.29%
 | High | 2.56% |  | 4.63% |  | 2.52%
BlowingBubbles | Low | 1.99% | BQMall | 6.39% | BQTerrace | 1.47%
 | High | 2.23% |  | 6.16% |  | 1.18%
BQSquare | Low | 4.97% | PartyScene | 3.65% | Cactus | 2.33%
 | High | 5.04% |  | 4.07% |  | 2.54%
RaceHorses | Low | 4.93% | RaceHorses | 7.00% | Kimono1 | 1.60%
 | High | 3.98% |  | 5.85% |  | 1.34%
 |  |  |  |  | ParkScene | 0.95%
 |  |  |  |  |  | 0.93%
Average | Low | 3.99% | Average | 5.47% | Average | 1.93%
 | High | 3.45% |  | 5.18% |  | 1.70%
Total Average for Class D, C and B: 3.48% |  |  |  |  |  | 

## Slide 14: Closing remarks
Preliminary research work revealed that the compression capability of flexible motion partitioning can be further improved
Suggest continuing TE to explore the potential improvement on inter-frame coding

## Slide 15
Thank you!
www.hisilicon.com