## Slide 1: Region-based adaptive interpolation filter
Region-based adaptive interpolation filter
Shohei Matsuo, Yukihiro Bandoh,
Seishi Takamura and Jozawa Hirohisa
NTT Cyber Space Laboratories
NTT Corporation, Japan
JCTVC-B051 (2nd JCTVC meeting: Geneva, CH, 21-28 July, 2010)

## Slide 2: Outline
Introduction
Basic idea
Algorithm of the proposal
Simulation results
Conclusion

## Slide 3: Introduction
Conventional interpolation filter
  Fixed interpolation: 6-tap filter of H.264
  Adaptive interpolation: 2D-AIF, SAIF
Proposal
  Enhancement of frame-based AIFs
  Optimizing filter coefficients on a region-by-region basis
Simulation results
  More effective than SAIF by about 0.6 points on average
    Average: SAIF: 5.0%, Proposal: 5.6%, Diff: 0.6
    Maximum: SAIF: 4.3%, Proposal: 6.6%, Diff: 2.3 (Cactus)

## Slide 4: Basic Idea
SAIF: Filter coefficients are optimized on a frame-by-frame basis
When an original image has multiple movements or each region of the image has different characteristics (motion, texture, etc.),
  Frame-based AIF is the best method?
Proposal: Region-Based AIF (RBAIF)
  Filter coefficients are optimized on a region-by-region basis
Conventional AIF
RBAIF


Region-A
Region-B
Filter
Set 1
Filter Set 1
Filter Set 2

## Slide 5: Expected Effect
Merit:
  Improvement of coding efficiency
    Prediction error energy reduction
  Adaptability
    Combined with conventional AIFs
Demerit:
  Increase of overhead
    Bits of additional filter coefficients
RBAIF would be effective:
  for high-resolution images
  at high bit-rates

## Slide 6: Algorithm (Current implementation)
Divide the frame into blocks of 4x4
Set a region number to each block
Calculate the coefficients and interpolate the image
Derive new MVs
End
Start
Encode the filter coefficents of each region
Derive MVs using H.264/AVC filter
Same calculation and interpolation method of SAIF
MV component
MV direction
Spatial coordinate

## Slide 7: Simulation
Conditions
  KTA 2.6r1, High Profile
  HEVC CfP sequences
  2 frames (GOP: IP)
  QP(I)=22, 27, 32, 37 / QP(P)=QP(I)+1
  Interpolation filter: SAIF (UseAdaptiveFilter=2)
    The other KTA tools were turned off
  Other parameters were same as the default of encoder.cfg
  Region-dividing mode: 12 (detailed in the next page)
Results
  BD-rate and BD-PSNR for the first P-frame

## Slide 8: Definition of region-dividing modes
Method |  | Definition |  |  | 
H.264/AVC |  | Fixed 6-tap filter |  |  | 
0 | Conventional | Frame-based conventional AIF |  |  | 
Proposed methods |  | Region-1 | Region-2 | Region-3 | Region-4
1 | Motion speed (1) | x<MVx<x | otherwise | N/A | N/A
2 | Motion speed (2) | y<MVy<y | otherwise | N/A | N/A
3 | Motion direction (1) | 1st or 3rd quadrant | 2nd or 4th quadrant | N/A | N/A
4 | Motion direction (2) | MVx > 0 | otherwise | N/A | N/A
5 | Motion direction (3) | MVy > 0 | otherwise | N/A | N/A
6 | Left/right | x < W/2 | otherwise | N/A | N/A
7 | Top/bottom | y < H/2 | otherwise | N/A | N/A
8 | Left/middle/right | x < W/3 | W/3 < x < 2W/3 | otherwise | N/A
9 | Top/middle/bottom | y < H/3 | H/3 < y < 2H/3 | otherwise | N/A
10 | Horizontally-quartered | x < W/4 | W/4 < x < W/2 | W/2 < x < 3W/4 | otherwise
11 | Vertically-quartered | y < H/4 | H/4 < y < H/2 | H/2 < y < 3H/4 | otherwise
12 | Quartered | x < W/2 && y < H/2 | W/2 < x && y < H/2 | x < W/2 && H/2 < y | otherwise

## Slide 9: BD-rate and BD-PSNR
Class | SAIF | RBAIF |  | Maximum 
A | 5.867 | 6.365 | 0.498 | Traffic: 0.786
B | 6.812 | 7.829 | 1.017 | Cactus: 2.306
C | 2.929 | 3.419 | 0.490 | PartyScene: 1.431
D | 4.356 | 4.448 | 0.092 | BQSquare: 0.570
E | 5.218 | 5.925 | 0.707 | Vidyo3: 2.059
All | 5.033 | 5.618 | 0.585 | 
Class | SAIF | RBAIF |  | Maximum 
A | 0.219 | 0.239 | 0.019 | Traffic: 0.029
B | 0.189 | 0.218 | 0.029 | Cactus: 0.054
C | 0.126 | 0.148 | 0.022 | PartyScene: 0.070
D | 0.177 | 0.180 | 0.003 | BQSquare: 0.023
E | 0.166 | 0.195 | 0.028 | Vidyo3: 0.067
All | 0.172 | 0.192 | 0.021 | 
BD-rate
BD-PSNR

## Slide 10: Conclusion
A region-based AIF was proposed
Simulation results showed
  Coding gain: about 0.6 points (SAIF: 5.0% RBAIF: 5.6%)
  Its performance depended on the region-dividing method
Future work
  Implementation for B pictures
  Investigation of more effective region-dividing methods
Suggestion
  The proposal can be combined with any xAIFs
  It should be incorporated into one of coding options for HEVC

## Slide 11
Thank you