## Slide 1: Proposed low complexity video encoder settings for HEVC
Minhua Zhou (zhou@ti.com) Texas Instruments Inc., USA
JVTVC-B054

## Slide 2: Low-Complexity Video Applications
Camera phones, camcorders, video surveillance and video conferencing applications have evolved into another major video market in recent years
Video codecs serving this market sector are highly cost sensitive
High coding efficiency at low encoder complexity is a key requirement

## Slide 3: Lessons Learned from Past
Coding tools behave differently at high- and low encoder environments, gains observed in the high complexity modes often do not apply in the low-complexity modes
Committee code cannot be used for driving chip architecture
Too many options/modes oftentimes do not help improve video quality in low encoder complexity environments, but increase chip design cost
“Deterministic” quality enhancement tools with no or little need of mode decision are preferred (e.g. CABAC, de-blocking filter)
Video quality could be better if low-complexity encoder requirements can be considered during the standardization
Time to market can be shortened if test data for low-complexity mode is readily available in the committee

## Slide 4: Challenges and Opportunities
Gains from “deterministic” tools such as entropy coding, in-loop de-blocking filter have been exhausted
Further quality gain heavily rely on more advanced design in inter-prediction, intra-prediction, adaptive block size transforms, etc.
Important to test advanced tools (modes) in both high-complexity and low-complexity environments
  Significant coding efficiency gain over MPEG4 AVC/H.264 for a wide range of video applications

## Slide 5: Design Considerations
On-chip memory size
  e.g. Search ranges, LCU sizes, transform sizes
Memory bandwidth
  e.g. Number of reference frames, search ranges
Throughput
  e.g. Transform size in intra prediction
Encoder processing power
  e.g. Motion estimation, intra prediction estimation, mode decisions

## Slide 6: Proposed low-complexity encoder settings (1)
Parameters | Settings | Remark
Maximum CU size | 64 x 64 | This will effectively increase the on-chip memory requirement by 8x compared to the current MPEG4 AVC/H.264 design, a very challenging goal.
Minimum PU size | 16 x 16 | Vector block size less than 8x8 is hard to support on the encoder side
Transform sizes | 8x8, 16x16, 32x32 | 4x4 and 2nd level 4x4 DC transform may have throughput issues at UHD due to dependency in intra prediction; 64x64 transform is too expensive
Transforms for intra | TBD | Transforms proposed for intra blocks need to be unified into a simpler design
Motion vector precision | ¼ pel | Low-complexity 1/8 pel vectors could be supported in the future
Search range | TBD | The search range is limited by on-chip memory size and available memory bandwidth
Slice type | I, P, B, HierP, HierB | 
Number of reference frames for P | 2 | In the DPB buffer there can be more than 2 reference frames, but for coding the current P frame the encoder choose up to 2 reference frames
Number of reference frames for B | 1 in each direction | In the DPB buffer there can be multiple reference frames, but for coding the current B frame the encoder choose the best reference frame in each direction
Reference picture re-ordering | Yes | 

## Slide 7: Proposed low-complexity encoder settings (2)
Parameters | Settings | Remark
LowDelayMode | 0 and 1 | Both low-delay and high-delay modes shall be supported
Weighted prediction | yes | 
IBDI | On ? | n bits increase, deterministic increase in complexity and coding efficiency; needs to determine value n based on complexity and coding efficiency trade-offs; memory bandwidth reduction needs to be considered.
Interpolation Filter | TBD | Small number of filter tap is preferred for saving memory bandwidth; needs to consider filter settings when IBDI is on
Entropy coding | CABAC | It can be replaced by v2v if the final design of v2v can provide intended throughput improvements
Deblocking filter | On | 
ALF | Off | Memory bandwidth concerns
RDOQ | Off | Complexity is too high for low-complexity encoder design
RDO | On, fast mode | simplified cost metrics instead of brute force R + λ*D. Currently this feature is not addressed in the reference software [2]
CU partitioning for PUs and TUs | Fast mode | Currently this feature is not addressed in the reference software [2]