## Slide 1: Sub-picture based raster scanning coding order for HEVC UHD video coding
Minhua Zhou (zhou@ti.com) Texas Instruments Inc., USA
JVTVC-B062

## Slide 2: Motivation
HEVC will support UHD (8K x 4K or even higher) video applications
Picture size increase goes much faster than DDR bandwidth and on-chip memory size increase that can be afford
  Increased constraints of memory bandwidth and on-chip memory
  New challenges for achieving high quality for UHD video coding
Provide a option of improving video quality under the constrained memory bandwidth and on-chip memory size budget

## Slide 3: Growing Window
Reference frame
Current frame
Where srY is vertical search range, N x N is MB size, picWidth is horizontal picture size
2*srY+N
2*srY+N
2*srY+N
Minimized memory bandwidth usage for ME & MC
Unlimited horizontal search range
Large on-chip memory required for buffering search window

## Slide 4: Sub-picture raster scanning order

## Slide 5: Memory size w/ sub-picture partitioning
srX | srY | N | K | picWidth | memSize (bytes) | On-chip memory size reduction (%) | Memory bandwidth increase (%)
256 | 256 | 64 | 1 | 7680 | 4423680 | 0 | 0
256 | 256 | 64 | 2 | 7680 | 2359296 | -46.67 | 6.67
256 | 256 | 64 | 3 | 7680 | 1671168 | -62.22 | 13.33
256 | 256 | 64 | 4 | 7680 | 1327104 | -70.00 | 20.00
256 | 256 | 64 | 5 | 7680 | 1120666 | -74.66 | 26.67
256 | 256 | 64 | 6 | 7680 | 983040 | -77.78 | 33.33

## Slide 6: Characteristics of sub-picture coding order
It is a more generic coding order, and can be signaled in SPS or PPS
Sub-pictures can belong to a same slice (different from FMO)
It is up to users for seeking balance between horizontal and vertical search range for given on-chip memory budget
Sub-pictures shall be aligned on LCU boundary and evenly divided along the horizontal direction
It might not be suited for ultra low–delay video applications
No quality loss expected (to be tested)