## Slide 1: TE1: Decoder-Side Motion Vector Derivation with Switchable Template Matching
Yu-Wen Huang, Ching-Yeh Chen, Chih-Wei Hsu, Jian-Liang Lin Yu-Pao Tsai, Jicheng An, and Shawmin Lei
JCTVC-B076
Copyright © MediaTek Inc. All rights reserved.
2nd JCT-VC Meeting in Geneva
21-28 July, 2010
Notes: <number>

## Slide 2: Outline
Introduction
Algorithm description
Compression performance
Complexity analysis
Conclusion
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 3: Decoder-side Motion Vector Derivation (DMVD)
Copyright © MediaTek Inc. All rights reserved.
<number>
Prior art
  RWTH Aachen University
    VCEG-AG16, VCEG-AH15, JVT-AA039, JVT-AA040, VCEG-AJ18, JCTVC-A112
    Template matching (TM) on both encoding and decoding sides
    Do not need to send any motion information (MI) including reference picture index or motion vector (MV)
    Multi-hypothesis prediction (MHP)
  MediaTek
    JCTVC-A109
    Support multiple coding unit (CU) sizes
    Support multiple prediction unit (PU) sizes for each DMVD CU
    Support B-pictures
  Many other proponents including Huawei, Intel, JVC, Leibniz Univ. Hannover, LGE, Peking Univ., Qualcomm, …
Notes: <number>

## Slide 4: What’s New in the This Proposal?
Two DMVD modes
  DMVD_DIRECT: TM is disabled
  DMVD_TM: TM is enabled
  For each DMVD CU, send a flag to select between DMVD_DIRECT and DMVD_TM
Two operating points
Copyright © MediaTek Inc. All rights reserved.
<number>
 | Low Complexity Operating Point | High Coding Efficiency Operating Point
DMVD_DIRECT Mode | On | On
DMVD_TM Mode | Off | On

## Slide 5: DMVD_DIRECT Mode vs DIRECT Mode
MHP is used in DMVD_DIRECT
Multiple modes in DMVD_DIRECT signaled by the encoder
DMVD_DIRECT uses different predicted MI
  Each PU of DMVD_DIRECT has its own sets of candidates
Spatial/temporal adaptation
  DMVD_DIRECT: switched at CU level
  DIRECT: switched at slice level
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 6: DMVD_DIRECT Mode
MHP derived from MI of neighboring CUs
  Multiple sets of spatial-temporal candidates
  Transmit a set index to decoders
  No TM
Four DMVD_DIRECT modes
  3 spatial direct modes:
    DMVD_DIRECT_S: spatial direct mode
    DMVD_DIRECT_L: left direct mode
    DMVD_DIRECT_U: upper direct mode
  1 temporal direct modes:
    DMVD_DIRECT_T: temporal direct mode
  These modes can be switched on the CU level.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 7: DMVD_DIRECT_ST Modes
P
e
a
f
d
b
c
U
L
T
R
D
Current CU
Co-located CU
Spatial
Temporal
Current PU
Copyright © MediaTek Inc. All rights reserved.
<number>
+ ( + + + )x1/8
= ( + )x1/4
Pa
Pb
P
Pc
Pd
Pe
Pf
+ ( + + + )x1/4
= x1/2
PT
P
PL
PR
PT
PU
Pc
denotes the prediction of current PU with MI of block c
Notes: <number>

## Slide 8: DMVD_DIRECT_LU Modes
Copyright © MediaTek Inc. All rights reserved.
<number>
P
e
a
f
d
b
c
Left
Upper
P
Current CU
Current CU
+ ( + )x1/4
= x1/2
Pa
P
Pe
Pf
+ ( + )x1/4
= x1/2
Pb
P
Pc
Pd
Current PU
Notes: <number>

## Slide 9: DMVD_TM vs A112 (RWTH Aachen Univ.)
Template boundary weighting in DMVD_TM
Adaptive template shape in DMVD_TM
Different search algorithm
  Different initial search candidates
  Distortion check to remove outliers in MHP after initial search
  Partial but joint refinement in DMVD_TM
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 10: Boundary Weighting for DMVD_TM
Sequence-level parameter
Conveyed in the PPS
  Give higher weights for distortion values of boundary pixels
  Use shift operation instead of multiplication
2-bit left shift used in all experiments
Copyright © MediaTek Inc. All rights reserved.
<number>
Current
PU
Template
Template
Template
Boundary pixels
Non-boundary pixels

## Slide 11: Template Shapes for DMVD_TM
CU-level adaptation
4 template shapes selected by a 2-bit flag
Provide higher TM accuracy for object boundaries
Reduces decoding complexity due to smaller templates
Copyright © MediaTek Inc. All rights reserved.
<number>
Current PU
TN
TN+1
TN+2
L-Shape Mode
T…
T…
T1
T…
T…
T2N+1
Current PU
TN+2
Upper Mode
T…
T…
T2N+1
Current PU
TN
Left Mode
T…
T…
T1
Current PU
T…
TN+1
T…
Corner Mode
TN/2+1
T3N/2+1

## Slide 12: Search Algorithm for DMVD_TM
Assume N-hypothesis prediction is used
Initial search
  Search the 11 candidates used in DMVD_DIRECT_ST
  Store the best N candidates with the smallest distortions
Distortion Check
  Replace the stored candidates having distortions larger than a threshold (coded in PPS) by the best candidate having the smallest distortion
MHP Refinement
  Refine N/2 stored candidates having the largest distortions with a 5-point cross pattern
  When 1 candidate is refined, the other N-1 are fixed.
  Joint optimization of N candidates
    Minimize the distortion between the current template and the N-hypothesis reference template
Initial Search
Distortion Check
MHP Refinement

## Slide 13: Miscellaneous Information about Our DMVD
Based on KTA2.6r1
Quarter pixel accuracy
Applied on 3 levels of CUs => 16x16, 32x32, 64x64
For each DMVD CU, residues can be skipped or coded by sending a flag
For each DMVD CU, the PU size is adaptive
  If skipped, the PU size is equal to the CU size
  If coded, the PU size is equal to the transform unit (TU) size
Copyright © MediaTek Inc. All rights reserved.
<number>
DMVD PU Sizes | 16x16 CU | 32x32 CU | 64x64 CU
Skipped | 16x16 | 32x32 | 64x64
Coded | 4x4, 8x8, 16x16 | 4x4, 8x8, 16x16 | 4x4, 8x8, 16x16

## Slide 14: TE1-DMVD Common Test Conditions
Alpha condition (Hierarchical B) and Gamma condition (IPPP)
100 pictures
DMVD disabled as anchors
Single-pass picture encoding
H.264 weighted prediction off
IBDI off
Copyright © MediaTek Inc. All rights reserved.
<number>
NumberReferenceFrames = 4
UseAdaptiveFilter = 0
MVCompetition = 0
UseIntraMDDT = 1
UseHPFilter = 1
UseAdaptiveLoopFilter = 1
UseExtMB = 1 (32x32)
UseRDO_Q = 0

## Slide 15: BD-Rates under TE1-DMVD Conditions
Low complexity operating point
  On average, 5.35% and 5.63% bitrate reductions for Alpha and Gamma, respectively
High coding efficiency operating point
  On average, 7.24% and 7.66% bitrate reductions for Alpha and Gamma, respectively
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 16: Complexity Analysis
Normalized run times under TE1-DMVD conditions
  For decoders
    About 30% increase for the low complexity operating point
    About 93% increase for the high coding efficiency operating point
  For encoders
    Faster mode decision can be developed to speed it up
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 17: Conclusion
The proposed low complexity DMVD can achieve about 5.5% bitrate reduction while the decoding complexity is increased by 30%
The proposed high coding efficiency DMVD can achieve about 7.5% bitrate reduction while the decoding complexity is increased by 93%
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 18
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com
Notes: <number>