## Slide 1: In-Loop Adaptive Restoration
Yu-Wen Huang, Chih-Ming Fu, Ching-Yeh Chen, Chia-Yang Tsai, Yongying Gao, Jicheng An, Kai Zhang, and Shawmin Lei
JCTVC-B077
Copyright © MediaTek Inc. All rights reserved.
2nd JCT-VC Meeting in Geneva
21-28 July, 2010
Notes: <number>

## Slide 2: Outline
Introduction
Algorithm description
Compression performance
Complexity analysis
Conclusion
Copyright © MediaTek Inc. All rights reserved.
<number>
Notes: <number>

## Slide 3: Adaptive Restoration
Encoder block diagram with Adaptive Restoration (AR)
We extend the Deblocking Loop Filtering to Adaptive Restoration
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 4: Framework of the Proposed AR
Improved deblocking filter (IDF)
  Quality enhancement for intra blocks
Quadtree-based adaptive restoration (QAR)
  Local adaptation for Wiener filtering and adaptive offsets
Picture-based adaptive offset (PAO)
  Picture-based band offset (PBO): similar to Band Correction in A124
  Picture-based edge offset (PEO): similar to Extreme Correction in A124
Picture-based adaptive clipping (PAC)
  Applied after IDF, QAR, PBO, and PEO
Copyright © MediaTek Inc. All rights reserved.
<number>
IDF
QAR
PAO (PBO+PEO)

## Slide 5: Improved Deblocking Filter (IDF)
Based on H.264 deblocking filter
Changes only for the boundary where at least one of the two sides is intra coded
  Modified boundary strength
    Remove BS=4 to avoid over-smoothing
  Modified thresholds and clipping parameters
    To apply the filter more often but reduce the filter strength
  Mode Dependent Deblocking Filter (MDDF)
    Consider intra prediction modes to apply directional filtering
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 6: MDDF – Case 1
If the two blocks have the same intra prediction mode not parallel to the boundary, we propose to filter along the intra prediction direction
  Solid arrows denote intra prediction directions
  Dotted arrows denote proposed filter directions
  The filtering method keeps the same except the filtering direction
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 7: MDDF – Case 2
If the two blocks have different intra prediction modes, we propose to use horizontal or vertical filtering with weakened strengths.
    Weaken filter strength by reducing clipping parameter: C1 = C1 - 2
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 8: MDDF – Case 3
If the two blocks have the same intra prediction mode parallel to the boundary, we propose to use horizontal or vertical filtering with even more weakened strengths
  Weaken filter strength by C0 = 1 and C1 = C1 - 2
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 9: Quadtree-based Adaptive Restoration (QAR)
Local adaptation can provide coding gain
  Quadtree partitions to signal local adaptation
Besides Wiener filtering, adaptive band offset and adaptive edge offset are used
Each partition can select one of the following modes
  1-filter
  2-filter
  Localized band offset
  Localized edge offset
  No restoration
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 10: Adaptive Loop Filter (ALF)
Wiener filtering
The same as IMQALF in A109 (MediaTek)
1 or 2 filters per partition
Filter properties
  Size: 5x5, 7x7, 9x9
  Footprint: ½-symmetric
  Coefficients: newly derived and transmitted, or time-delayed without any transmitted coefficients
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 11: Localized Band Offset (LBO)
Conceptually similar to Band Correction in A124
Classify pixels of one partition into multiple bands
Send an offset for each band
Support 2 kinds of band classification
  One flag per partition to indicate the selected one
  Uniform 16 bands
  Non-uniform 12 bands
    Similar to the idea of Histogram Equalization
Copyright © MediaTek Inc. All rights reserved.
<number>
min
max
min
max

## Slide 12: Localized Edge Offset (LEO)
Conceptually similar to Extreme Correction in A124
Classify pixels of one partition into multiple categories
Send an offset for each category
Support 2 patterns for pixel classification
  One flag per partition to indicate the selected one
  Cross pattern
  Diagonal cross pattern
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 13: Pixel Classification in LEO
Category 0-5: offset applied
Category 6: no offset
Copyright © MediaTek Inc. All rights reserved.
<number>
Category | Condition | Note
0 | C < 4 neighbors | Local Min
1 | C < 3 neighbors && C = 4th neighbor | Edge
2 | C < 3 neighbors && C > 4th neighbor | Edge
3 | C > 3 neighbors && C < 4th neighbor | Edge
4 | C > 3 neighbors && C = 4th neighbor | Edge
5 | C > 4th neighbor | Local Max
6 | None of the above | Other

## Slide 14: Picture-based Adaptive Offset (PAO)
Arranged as “picture-based band offset (PBO)” followed by “picture-based edge offset (PEO)”
PBO
  Similar to LBO
  LBO is partition-based, while PBO is picture-based
  Only the uniform band classification used in PBO
PEO
  Similar to LEO
  LEO is partition-based, while PEO is picture-based
  Only the cross pattern used in PEO
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 15: Picture-based Adaptive Clipping (PAC)
Send minimum and maximum of original pixels of the current picture to decoders
Apply clipping to ensure all pixels after restoration are in the range of [minimum, maximum]
PAC is applied after IDF, QAR, PBO, and PEO
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 16: In-Loop Filtering AHG Test Conditions
Alpha condition (Hierarchical B) and Gamma condition (IPPP)
An All-Intra condition is added by us to test IDF
  Only I-pictures are used.
About 2 seconds for each test sequence
Multi-pass picture encoding
H.264 weighted prediction on
IBDI on (4-bit increase)
  Showing data when IBDI is disabled is also encouraged
Copyright © MediaTek Inc. All rights reserved.
<number>
NumberReferenceFrames = 4
UseAdaptiveFilter = 0
MVCompetition =1
UseIntraMDDT = 1
UseHPFilter = 4 (SIFO)
UseAdaptiveLoopFilter = 1 (QALF is enabled !!!)
UseExtMB = 2 (64x64)
UseRDO_Q = 1
UseNewOffset = 1

## Slide 17: BD-Rates When IBDI Is On
-2.71% when IDF is on for All-Intra
-1.88% and -2.76% when QAR is on for Alpha and Gamma, respectively
-3.34% and -3.61% when IDF and QAR are on for Alpha and Gamma, respectively
-3.76% when IDF, QAR, and PAO are on for Alpha
  PAO cannot further reduce bitrate for Gamma
Copyright © MediaTek Inc. All rights reserved.

## Slide 18: BD-Rates When IBDI Is Off
-2.73% when IDF is on for All-Intra
-1.88% and -2.75% when QAR is on for Alpha and Gamma, respectively
-3.54% and -3.81% when IDF and QAR are on for Alpha and Gamma, respectively
-4.06% when IDF, QAR, and PAO are on for Alpha
  PAO cannot further reduce bitrate for Gamma
Copyright © MediaTek Inc. All rights reserved.

## Slide 19: Complexity Analysis
Normalized run times when IBDI is on
  QALF enabled in the anchor defined by in-loop filtering AHG
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 20: Test Conditions with QALF Off
Alpha condition (Hierarchical B) and Gamma condition (IPPP)
About 2 seconds for each test sequence
Multi-pass picture encoding
H.264 weighted prediction on
IBDI on (4-bit increase)
  Showing data when IBDI is disabled is also encouraged
Copyright © MediaTek Inc. All rights reserved.
<number>
NumberReferenceFrames = 4
UseAdaptiveFilter = 0
MVCompetition =1
UseIntraMDDT = 1
UseHPFilter = 4 (SIFO)
UseAdaptiveLoopFilter = 0 (QALF is disabled !!!)
UseExtMB = 2 (64x64)
UseRDO_Q = 1
UseNewOffset = 1

## Slide 21: BD-Rates with QALF Off When IBDI Is On
IDF+QAR+PAO can achieve 7.41% bitrate reduction for Alpha
IDF+QAR can achieve 8.04% bitrate reduction for Gamma
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 22: Conclusion
The proposed Adaptive Restoration can achieve bitrate reductions of
  3.76% for alpha cases,
  3.61% for gamma cases, respectively,
  under the in-loop filtering AHG test conditions where the QALF is enabled as anchors
Decoding complexity increased by
  10% for alpha cases,
  14% for gamma cases, respectively.
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 23
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com
Notes: <number>