## Slide 1: TE2: Compressed Reference Frame Buffers (CRFB)
Mehmet Umut Demircin (demircin@ti.com) Texas Instruments Inc., USA
Madhukar Budagavi (madhukar@ti.com) Texas Instruments Inc., USA
Minhua Zhou (zhou@ti.com) Texas Instruments Inc., USA
Salih Dikbas (salih@ti.com) Texas Instruments Inc., USA
Joint Collaborative Team on Video Coding (JCT-VC)
of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11
2nd Meeting: Geneva, 21-28 July 2010

## Slide 2: Compressed Reference Frame Buffer (CRFB)
Objective: Reduce the ME/MC memory access bandwidth
  Total system memory bandwidth limited because of cost and power.
  Memory accesses are power hungry.
  Limited memory bandwidth impacts video quality because of constraints on amount of data that can be loaded for ME.
  Reference pictures use 12 bits/pixel if Internal Bit-Depth Increase (IBDI) tool is turned ON.
Design Constraints:
  Guaranteed compression ratio to enable random access to memory blocks
    IBDI-ON
      12 bit/pixel to 8 bit/pixel compression ratio for 8x8 blocks
    IBDI-OFF
      8 bit/pixel to 4 bit/pixel compression ratio for rows of 64x64 MBs.
  Implemented in the core video coding loop to avoid drift error caused by lossy compression.
  Based on simple compression and decompression algorithms.
  Can only be enabled for high-resolution sequences. (e.g. larger than 720p)

## Slide 3: CRFB in Encoder Block Diagram
Motion
Estimation
motion
vector
Motion
Compensation
Reference
frame buffer(s)
Quantization
VLC encoding
DCT
Inverse
Quantization
IDCT
Input video
Compressed
video stream
Mode
0
Control
(Inter/Intra)
C
UC
UC
C
UC
  → Compress reference frame buffer
→ Decompress reference frame buffer

## Slide 4: CRFB Algorithm - I
Based on simple transform, quantization, DC prediction and entropy coding
Transform:
  2D integer seperable S-transform on 8x8 luma (3 lifting steps) and 4x4 chroma blocks (2 lifting steps).
Quantization:
  Midtread quantizer operates on non-DC transform coefficients.
  Quantization step sizes are powers of 2. (12 quantization indices)
  Simple quantization matrix for finer quantization of low frequency coefficients.

## Slide 5: CRFB Algorithm - II
DC prediction:
  DC coefficients are predicted using left, top, and top-left neighbor blocks.
  Similar to MPEG-4.
  Disabled for IBDI-on mode.
Entropy coding:
  EG0 and EG3 codes used to encode quantized transform coefficients and DC prediction residual.
  Quantization index is unary coded.
Memory Access Unit (MAU) and Rate Control
  IBDI-ON:
    8x8 Y, 4x4 U and 4x4 V pixels
    Minimum QP satisfying the compression ratio is selected.
  IBDI-OFF:
    64 lines of Y, 32 lines of U and 32 lines of V pixels
    Larger memory access unit is selected to enable DC prediction and better statistical averaging.
    Leaky-bucket like simple rate control: unused bits are added to subsequent 8x8 block bit-budget.

## Slide 6: CRFB Encoder Block Diagram
2D
ST
GR
mapping
Q and k
selection
Q
Exp-Golomb
(k)
2D
ST
Rate
Control
Y
U
V
-
128
-
128
Unary Coding
QIdx
DC
Prediction
-
Fixed-Length Coding
kIdx
GR
mapping
Q and k
selection
Q
Exp-Golomb
(k)
DC
Prediction
-
Fixed-Length Coding
kIdx
Compressed Data

## Slide 7: BD-Rate Results (w.r.t. KTA2.6r1)
CS1
 | 5-pt BD-Rate | MAX | MIN
Class A | 0.25 | 0.45 | 0.24
Class B | 0.07 | 0.16 | -0.02
Class C | 0.07 | 0.16 | 0.01
Class D | 0.23 | 0.63 | 0.00
All | 0.13 |  | 
IBDI-ON (12 bit/pixel to 8 bit/pixel)
IBDI-OFF (8 bit/pixel to 4 bit/pixel)
CS2
 | 5-pt BD-Rate | MAX | MIN
Class B | 0.28 | 0.53 | 0.03
Class C | 0.53 | 0.71 | 0.21
Class D | 0.27 | 0.55 | 0.04
Class E | 0.55 | 1.01 | 0.29
All | 0.42 |  | 
CS1
 | 5-pt BD-Rate | MAX | MIN
Class A | 0.00 | 0.00 | 0.00
Class B | 0.16 | 0.80 | 0.00
Class C | 0.76 | 2.27 | 0.09
Class D | 5.98 | 9.37 | 0.01
All | 1.85 |  | 
CS2
 | 5-pt BD-Rate | MAX | MIN
Class B | 0.09 | 0.45 | 0.00
Class C | 1.81 | 6.16 | 0.08
Class D | 5.66 | 10.25 | -0.02
Class E | 0.00 | 0.00 | 0.00
All | 2.02 |  | 

## Slide 8: IBDI-OFF Mode Memory Access Pattern
Memory is read/written in rows of MBs.
Strips of reference frame blocks are cached in on-chip memory for ME.
Reference pixels are read once instead of multiple times, hence the memory bandwidth is further reduced.
Disadvantages: larger on-chip memory, limited vertical search range.
Reference Frame
Cached Block Strip
Inter Block
Search Range
Current Frame