## Slide 1: Mode-dependent residual reordering for Intra prediction residual
Institute of Digital Media Peking University Jul 2010
Xin Zhao, Li Zhang, Siwei Ma, Wen Gao
JCTVC-B102
Notes: In this presentation, a new mode-dependent residual reordering method is proposed for Intra prediction residual. The proposed method is a simplification of the MDDT scheme. The document number is JCTVC-B102

## Slide 2: Problem Statement
Mode-Dependent Directional Transform (MDDT)
C0, R0
C1, R1
C7, R7
Prediction Direction
Residual Distribution
Mode-dependent Transform Matrices
Notes: First I would like to give a brief review of the basic idea of MDDT. In MDDT, for each Intra prediction direction, a specific pair of column and row transform matrices are applied. And both the column and row transform matrices are KLT-based and obtained from off-line training.

## Slide 3: Problem Statement
Mode-Dependent Directional Transform (MDDT)
  MDDT improves the transform for intra prediction residual, but the grow in number of transform matrices also increased the algorithm complexity
  In VCEG-AM20, an orthogonal MDDT (OMDDT) method was proposed. With OMDDT, the number of transform matrices in MDDT is halved, and the matrix multiplication module can be re-used.
  In this contribution, we propose a mode-dependent residual reordering method to further decrease the number of transform matrices
Notes: With MDDT, the transform efficiency for Intra prediction residual in H.264/AVC is improved. But the grow in number of transform matrices also increased the algorithm complexity. In the Kyoto meeting, an orthogonal MDDT method is proposed. With the proposed method, the number of transform matrices in MDDT is halved, and the matrix multiplication module can be re-used. Furthermore, in this contribution, we propose a mode-dependent residual reordering method to further decrease the number of transform matrices

## Slide 4: Proposed Method
Residual Reordering
S, ST
Prediction Direction
Residual Distribution
Single transform matrix
Mode-Dependent Residual Reordering (MDRR)
Notes: The basic idea of the proposed MDRR is show in this slide, for each Intra prediction, a certain kind of residual reordering scheme is implemented between the prediction and transform stages. After the residual reordering stage, different prediction mode will produce similar residual statistics.

## Slide 5: Proposed Method
Magnitude distribution of 4x4 Intra prediction residual
(a) Mode 0 (b) Mode 1 (c) Mode 2
(d) Mode 3 (e) Mode 4 (f) Mode 5
(g) Mode 6 (h) Mode 7 (i) Mode 8
Notes: This figure shows the actual reordering methods for the 9 Intra prediction directions in our proposed method. The residual scanning order for I8MB mode is similar.

## Slide 6: Proposed Method
Mode-Dependent Residual Reordering (MDRR)
Residual scanning order for I4MB, the scanning order for I8MB is similar

## Slide 7: Proposed Method
Mode-Dependent Residual Reordering (MDRR)
  After residual scanning, the original Intra prediction modes are assigned into 3 groups, and only one transform matrix is used for each group
 | Group 1 | Group 2 | Group 3
I4MB modes (0~8) | 0, 1, 3, 7, 8 | 4, 5, 6 | 2(DC)
I8MB modes (0~8) | 0, 1, 3, 7, 8 | 4, 5, 6 | 2(DC)
I16MB modes (0~3) | 0, 1 | 3 | 2(DC)
Notes: After residual scanning, the original Intra prediction modes are assigned into 3 groups, and only one transform matrix is used for each group. The table shows the grouping of different prediction modes in I4MB, I8MB and I16MB macroblock modes.

## Slide 8: Simulation Results
Sequence | Original MDDT |  | Simplified MDDT using proposed MDRR | 
 | BD-PSNR | BD-Rate | BD-PSNR | BD-Rate
BasketballPass_p416x240_50fps | 0.240 | -4.538 | 0.227 | -4.313
BQSquare_p416x240_60fps | 0.348 | -4.264 | 0.365 | -4.469
BlowingBubbles_p416x240_50fps | 0.211 | -3.985 | 0.220 | -4.152
RaceHorses_p416x240_30fps | 0.231 | -4.088 | 0.218 | -3.883
BasketballDrill_p832x480_50fps | 0.237 | -5.215 | 0.226 | -4.976
BQMall_p832x480_60fps | 0.349 | -5.918 | 0.362 | -6.137
PartyScene_p832x480_50fps | 0.267 | -3.933 | 0.274 | -4.027
RaceHorses_p832x480_30fps | 0.186 | -3.016 | 0.188 | -3.052
vidyo1_p1280x720_60fp | 0.438 | -7.675 | 0.381 | -6.735
vidyo3_p1280x720_60fps | 0.528 | -8.239 | 0.528 | -8.231
vidyo4_p1280x720_60fps | 0.359 | -7.209 | 0.338 | -6.804
ParkScene_p1920x1080_24fps | 0.204 | -4.661 | 0.200 | -4.576
Kimono1_p1920x1080_24fps | 0.277 | -6.742 | 0.267 | -6.500
Cactus_p1920x1080_50fps | 0.221 | -5.409 | 0.213 | -5.217
BasketballDrive_p1920x1080_50fps | 0.241 | -7.689 | 0.255 | -8.128
BQTerrace_p1920x1080_60fps | 0.357 | -6.890 | 0.345 | -6.671
Average | 0.293 | -5.592 | 0.288 | -5.492
Best Case | 0.528 | -8.24 | 0.528 | -8.23
Worst Case | 0.186 | -3.02 | 0.188 | -3.05
Notes: This slide shows the simulation results for class B to E sequences. From this table, we can see that the average BD-Rate increase of Simplified MDDT using proposed MDRR compared with the original MDDT is 0.1%. And the average BD-PSNR drop of Simplified MDDT using proposed MDRR compared with the original MDDT is 0.005.

## Slide 9: Conclusion
Under the testing condition specified in the AhG report on alternative transforms with all-Intra conditions, compared with MDDT, average BD rate increase of 0.1% and BD PSNR drop of -0.005dB is observed.
Comparison of the number of transform matrices in MDDT and MDRR
 | Original MDDT | Simplified MDDT with MDRR
I4MB modes (0~8) | 18 | 3
I8MB modes (0~8) | 18 | 3
I16MB modes (0~3) | 8 | 3
Notes: With the simulation results presented in the previous slide, we conclude that the Simplified MDDT using proposed MDRR provides almost the same coding performance as MDDT, but the number of transform matrices has been reduced a lot

## Slide 10
Thanks!