## Slide 1
<number>
Differential Coding of Intra Modes (DCIM)
JCTVC-B109
E. Maani, W. Liu, A. Tabatabai, M. Gharavi
Notes: <number>

## Slide 2: Overview
Motivation:
  Current AVC intra prediction has a coarsely quantized prediction directions (i.e., 8)
  More precision in the prediction direction results in better prediction aka TMuC 0.0 (i.e., 33)
  With inefficient signaling adding more prediction directions will NOT produce compression gain especially in small block sizes (4x4 and 8x8)
    Small block size prediction constitute a large percentage of the blocks in intra prediction of complex images
<number>
Proposal:
  Based on neighbors’ suggested direction (NSD), we propose an efficient signaling of intra prediction direction mode
  JCTVC-A030

## Slide 3: Neighbors’ Suggested Direction
<number>
Current Block
2W+4
W+4
Neighbors’ suggested direction (high precision)
In a neighborhood,
perform edge detection using for example Sobel operators
Neighbors’ suggested direction
Neighbors’ suggested direction
Confidence measure (0,1]
WxW

## Slide 4: Proposed Solution
<number>
Compute neighbors’ suggested direction
Compute confidence measure s of directions
Based on the confidence measure s we introduce 2m+1 new modes:
The following signaling is used for the 2m+10 modes
0--8
mode
9--2m+9
Most probable
rest
1
0XXX
1
0
AVC
Proposed DCIM

## Slide 5: Proposed Syntax
Let k=0, denote the neighbors suggested direction (NSD)
    If neighbor’s suggested direction is useful, send a 1 first indicating that to the decoder
The actual direction is differentially coded with respect to neighbors’ suggested direction
  Then send a unary code to for the signaling of k
For other directions not using neighbor’s suggested direction
  Use conventional methods such as the fixed length codes AVC
<number>
1
1
1
1
1
n
1
0
0
1
0
1
0
10
110
1110
111111…0
111 1
Use NSD flag
Number of context
Based on a confidence measure define n different context
Actual bits
in bit stream

## Slide 6: Experimental Results
Experimental set-up
  Proposed algorithm implemented in KTA 2.6r1
  Maximum deviation from NSD is 4 ( )
  4x4, 8x8, and 16x16 blocks use the proposed method
  All sequences are INTRA coded with QPs (26, 30, 34, 38)
  2 Seconds of video is considered as suggested by In-Loop AhG
  DCT transform is used
  Common conditions recommendation VCEG-AJ10r1 is followed
  Bit rate savings due to the proposed method is reported
<number>

## Slide 7: BD-Rate Results
<number>

## Slide 8: Summary
<number>
Key Features:
  Provides flexibility in finding the more appropriate prediction direction
  A superset to fixed directional modes
    can be mapped into current fixed directional modes
  A novel way for differential signaling of direction to cover smaller block size i.e., 4x4 & 8x8.
  Introduction of confidence parameter and its usage in defining the NSD context and δθ
Proposal:
  TE for intra prediction tools performance comparisons ?
  Interaction with Transform

## Slide 9: BD-R Comparison
<number>