## Slide 1: Entropy Slices for Parallel Entropy Coding K. Misra, J. Zhao and A. Segall JCT-VC B111

## Slide 2: Entropy Slices
Introduction: Entropy Slice
  Introduce partitioning of slices into smaller “entropy” slices
  Entropy slice
    Reset context models
    Restrict definition for neighborhood
    Process identical to current slice by entropy decoder
    Key difference: reconstruction uses information from neighboring entropy slices

## Slide 3: Entropy Slices
We now cite major advantages for the entropy slice concept
  Advantage #1 - Parallelization:
    Entropy slices do not depend on information outside of the entropy slice and can be decoded independently
    Allows for parallelization of entire entropy decoding loop – including context adaptation and bin coding
  Advantage #2 - Generalization
    Entropy slices can be used for all entropy coding engines currently under study in the TMuC and TMuC software
    Moreover, we have software available for PIPE and CABAC
V2V
CABAC
PIPE
UVLC

## Slide 4: Entropy Slices
Advantages #3 – No impact on single thread/core:
  Parallelization capability does not come at the expense of single thread/core applications
  A single thread/core process may
    Decode all entropy slices prior to reconstruction
    OR
    Decode entropy slice and then reconstruct without neighbourhood reset
  This is friendly to any architecture

## Slide 5: Entropy Slices
Advantage #4 –Easy Adaptation to Decoder Design
  Bit-stream can be partitioned into a large number of entropy slices with little overhead
  For example, we will show performance of 32 entropy slices for 1080p on next slide – this would translate to ~128 slices for 4k.
  Decoder can schedule N entropy decoders easily, where N is arbitrary
    One example: for 32 slices, architecture with parallelization of 4 (N=4) would assign 8 slices per decoder.
    Another example: for 32 slices, architecture with N=8 would assign 4 slices per decoder
    Additionally, for large resolutions (4k,8k) possible to scale to 100s of decoders for GPU implementations

## Slide 6: Entropy Slices
Advantage #5 –Coding Efficiency
  Insertion of Entropy Slices results in negligible impact on coding efficiency. For example, if configure the encoder for a parallelization factor of 32, we get:
TMuC 0.3 with PIPE

## Slide 7: Entropy Slices
Advantage #5 –Coding Efficiency
  Insertion of Entropy Slices results in negligible impact on coding efficiency. For example, if configure the encoder for a parallelization factor of 32, we get:
TMuC 0.3 with PIPE

## Slide 8: Entropy Slices
Advantage #6 –Specification
  Entropy slices allow simple and direct specification of parallelization at the Profile and Level stage
  This is accomplished by:
    Specifying the maximum number of bins in an Entropy Slice
    Specifying the maximum number of Entropy Slices per picture
  Allows addition specification of PIPE/V2V configurations
    Maximum number of bins per bin coder in an Entropy Slice
  Additional advantage: straightforward to determine conformance at encoder
TMuC 0.3 with PIPE

## Slide 9: Entropy Slices
Syntax
  Slice header
  Indicate slice is “entropy slice”
  Send only information necessary for entropy decoding

## Slide 10: Conclusions
We have presented the concept of an “entropy slice” for the HEVC system
Advantages include:
  Parallel entropy decoding (both context adaptation and/or bin coding)
  Generalization to any entropy coding system under study
  No impact on single core/thread applications
  Easy adaptation to different parallelization factors at the decoder
  Negligible impact on coding efficiency (<0.01dB)
  Direct path for specifying parallelization at the profile/level stage
We propose study of the entropy slice concept in the HEVC system.