## Slide 1: Parallel Prediction Unit for Parallel Intra Coding JCTVC-B111 Jie Zhao and Andrew Segall

## Slide 2
Overview
  Parallel Prediction Unit
  Parallel intra-prediction (review)
  Syntax
  Performance

## Slide 3: Parallel Intra Prediction
Parallel Prediction Unit
  Goal:
    Reduce the amount of serial dependencies in the intra-predictio process
  Approach:
    Specify a unit/region in the reconstructed frame where intra-coded prediction units will be decoded in parallel
LCU
CU/PU
CU
CU
CU
CU/PU
CU/PU
CU/PU
PPU

## Slide 4: Parallel Intra Prediction
Parallel intra prediction
  Within each PPU we then do the following:
    Divide prediction units into two partitions
    Predict first partition from pixels in reconstructed and neighboring PPUs
    Predict second partition from:
      Pixels in first partition
      Pixels in neighboring PPUs
Second pass blocks
First pass blocks
PPU

## Slide 5: Parallel Intra Prediction
Prediction of First Pass Blocks
  Use only reconstructed pixels from neighboring PPUs
  Prediction uses existing intra-prediction techniques. Boundary pixels are extrapolated by prediction direction.
  For DC prediction, we compute the DC as a weighted function of the distance between the block and the horizontal and left PPU boundaries
  Mode is predicted from first block above and to the left of current block that is either in neighboring PPU or current partition
LCU
CU/PU
CU
CU
CU
CU/PU
CU/PU
CU/PU
PPU

## Slide 6: Parallel Intra Prediction
Prediction of Second Pass Blocks
  Uses pixels in neighboring PPUs AND pixel in first pass blocks
  Note the bottom and right boundaries may be available
    We introduce prediction from the bottom/right neighbors.
      Conceptually we rotate the current block and boundary, perform the prediction and rotate the result back
    Additionally, we enable a weighted prediction of two directions that are out of phase
      For example, mode 1 and mode 10
      Predictions are weighted based on distance from boundary
Mode | Name of Mode
9 | Vertical 2
10 | Horizontal 2
11 | DC 2
12 | Diagonal Down Left 2
13 | Diagonal Down Right 2
14 | Vertical Right 2
15 | Horizontal Down 2
16 | Vertical Left 2
17 | Horizontal Up 2

## Slide 7: Signaling
Signaling
  We signal the PPU size in the sequence header
  We signal the weighting flag in the prediction unit syntax

## Slide 8: Signaling
Signaling
  We signal the PPU size in the sequence header
  We signal the weighting flag in the prediction unit syntax

## Slide 9: Performance
Performance
  We compared our technology with the current, serial approach for intra-prediction
  Conditions
    TMuC 0.3
    Configuration as provided by Software AhG
    PPU of 16x16
  Coding Impact
    HD (Hier-B): 0.48% / -0.01dB

## Slide 10: Performance
Performance
  We compared our technology with the current, serial approach for intra-prediction
  Conditions
    TMuC 0.3
    Configuration as provided by Software AhG
    PPU of 16x16
  Coding Impact
    HD (Hier-B): 0.48% / -0.01dB
    HD (IPPP): 0.25% / -0.006dB

## Slide 11: Performance
Performance
  We compared our technology with the current, serial approach for intra-prediction
  Conditions
    TMuC 0.3
    Configuration as provided by Software AhG
    PPU of 16x16
  Coding Impact
    HD (Hier-B): 0.48% / -0.01dB
    HD (IPPP): 0.25% / -0.006dB
    HD (Intra): 0.50% / -0.02dB*
*Limited number of frames (16)

## Slide 12: Conclusions
Conclusions
  We presented the concept of a parallel prediction unit
  The PPU allows extension of our previously presented parallel intra-prediction to the TMuC design
  Parallelism is achieved by dividing PPU into two sets
    First set predicted from boundaries of PPU
    Second set predicted from reconstructed first set
    Second set uses additional prediction directions
  Results
    HD (Hier-B): 0.48% / -0.01dB
    HD (IPPP): 0.25% / -0.006dB
  Propose further study of proposed technique