## Slide 1: Evaluation result of ＪＣＴＶＣ-B031 (JCTVC-C021, m18028)
Copyright 2010 FUJITSU LIMITED
K.Kazui, J.Koyama, and A.Nakagawa
FUJITSU LABORATORIES LTD.
3rd JCT-VC meeting, Guangzhou/China
2010/10/7-15
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 2: Outline
<number>
Copyright 2010 FUJITSU LIMITED
<number>
At the 2nd JCT-VC meeting, we proposed the scheme which minimizes the loss of coding efficiency in very low delay coding of less than one frame period.
  The document number is JCTVC-B031.
This contribution shows the evaluation result of the proposed scheme using TMuC version 0.7.3.
  The preliminary result shown in JCTVC-B031 was obtained by MPEG-4 AVC/H.264 JM.
  The proposed scheme is compared with the multiple slices scheme which is also implemented into TMuC 0.7.3. The process of a LCTB when multiple slices exist in a picture is similar to that of MPEG-4 AVC/H.264.
The improvements of the proposed scheme from the conventional multiple slices scheme in BD-Bitrate are 9.0% and 15.9% when the sizes of LCTB are 64x64 and 32x32, respectively.
In addition, new buffer model for the coding delay of less than one frame period is proposed.
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 3: Very low delay coding
<number>
Copyright 2010 FUJITSU LIMITED
The vertical intra MB line refresh scheme is used for cyclic refreshment of pictures in very low delay coding.
  The picture-based intra refresh is not suitable for very low delay coding because the bits for an intra picture is much more larger than that for an inter picture. The coding delay is proportional to maximum bits for a picture.
The vertical intra MB line refresh scheme averages the amount of bits for each MB line and minimizes the size of a bitstream buffer. Thus the coding delay less than one frame period becomes possible.
It is necessary to restrict the reference from a MB in a refreshed area to a MB in a non-refreshed area in order to guarantee the correct reconstruction of whole pixels at the end of each refresh cycle.
Vertical intra MB line refresh scheme
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 4: Problem in the conventional standards
It is necessary to insert a slice in each MB line when very low delay coding is applied to MPEG-4 AVC/H.264 in order to restrict the reference of coding tools such as the deblocking filter at the boundary of a refreshed area and a non-refreshed area.
Degradation of the coding efficiency is observed by inserting multiple slices in a picture.
Causes of degradation
  The reset of an entropy coder at the beginning of each slice
  The restriction of the reference for the intra prediction and the MV prediction
  The restriction of a MV
  The overhead of slice headers
<number>
Copyright 2010 FUJITSU LIMITED
Very low delay coding using MPEG-4 AVC/H.264
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 5: Overview of the proposed scheme
New syntax which describes the position of the area boundary between a refreshed area and a non-refreshed area is introduced.
  A slice header is not used for the purpose of separating the refreshed area and the non-refreshed area.
  New syntax improves the coding efficiency because the loss caused by multiple slices is removed.
  Each LCTB is processed in the raster-scan order.
New semantics which restricts the reference from a refreshed area to a non-refreshed area is introduced.
  The term “reference” in the new concept means the action of using the coding parameters in a block which is already reconstructed in order to reconstruct the coding parameters of a processing block.
  The coding parameters include pixel value for intra/inter prediction and in-loop post filtering, motion vector for prediction of motion vector.
  Correct reconstruction of pixels in the refreshed area is guaranteed.
  New motion compensation for blocks in the refreshed area improves coding efficiency by extrapolating pixels in the non-refreshed area in a reference picture. Conventional scheme does not allow such a MV that points pixels in the non-refreshed area.
<number>
Copyright 2010 FUJITSU LIMITED
Asymmetric restriction on reference
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 6: Evaluation method
Comparison
  Proposed scheme
  Conventional scheme
    Insertion of multiple slices in a picture
    Implementation of very low delay coding into TMuC when the high-level syntax and semantics of HEVC are similar to that of MPEG-4 AVC/H.264.
TMuC Software and configuration
  Software version for modification：0.7.3
  Configuration: “Low delay, high efficiency”. The sizes of LCTB are 64x64 and 32x32.
  QP = 22, 27, 32, 37
  The source code in which the proposed scheme and the compared scheme are implemented is attached to this contribution.
Test sequence
<number>
Copyright 2010 FUJITSU LIMITED
Class | Sequence | Length | Refresh cycle
A | Traffic, PeopleOnStreet | 81 | 40 (64x64), 80 (32x32)
B | Kimono, ParkScene, Cactus, BQTerrace, BasketballDrive | 181 (24p) 481 (50p/60p) | 30 (64x64), 60 (32x32)
C | RaceHorses, BQMall, PartyScene, BasketballDrill | 209 | 13 (64x64), 26 (32x32)
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 7: 3 test cases in the conventional scheme
Case 1
  Bits of all slice headers (excluding ALF parameters) and bits of ALF parameters in the first slice of each picture are taken into account.
  Comparison with Case 1 represents the typical coding gain of the proposed scheme.
Case 2
  Bits of all slice headers (including ALF parameters) are taken into account.
  Comparison with Case 2 represents the coding gain when ALF parameters are encoded redundantly.
Case 3
  Bits of all slice headers are not taken into account. (Unrealistic case)
  Comparison with Case 3 represents the coding gain by relaxing the restriction on reference.
Note
  The number of bits for ALF parameters in a slice header is 25-90 Byte. The number of bits for other parameters in a slice header is about 10 Byte.
<number>
Copyright 2010 FUJITSU LIMITED
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 8: Coding gain of the proposed scheme (64x64 LCTB)
<number>
Copyright 2010 FUJITSU LIMITED
Class | Sequence | Case 1 |  | Case 2 |  | Case 3 | 
 |  | BD-PSNR | BD-Bitrate | BD-PSNR | BD-Bitrate | BD-PSNR | BD-Bitrate
A | Traffic | 0.368 | -10.087 | 0.528 | -13.944 | 0.286 | -7.876
 | PeopleOnStreet | 0.190 | -4.033 | 0.353 | -7.332 | 0.151 | -3.206
 | Average | 0.279 | -7.060 | 0.440 | -10.638 | 0.218 | -5.541
B | Kimono | 0.355 | -10.452 | 0.566 | -16.002 | 0.256 | -7.610
 | ParkScene | 0.307 | -8.826 | 0.470 | -12.914 | 0.221 | -6.422
 | Cactus | 0.264 | -10.053 | 0.406 | -15.195 | 0.197 | -7.513
 | BQTerrace | 0.245 | -10.828 | 0.337 | -14.930 | 0.193 | -8.562
 | BasketballDrive | 0.250 | -10.191 | 0.405 | -16.269 | 0.188 | -7.724
 | Average | 0.284 | -10.070 | 0.437 | -15.062 | 0.211 | -7.566
C | RaceHorses | 0.291 | -6.439 | 0.441 | -9.539 | 0.193 | -4.310
 | BQMall | 0.547 | -11.515 | 0.739 | -15.126 | 0.386 | -8.290
 | PartyScene | 0.261 | -4.879 | 0.392 | -7.211 | 0.175 | -3.232
 | BasketballDrill | 0.537 | -11.749 | 0.845 | -17.625 | 0.354 | -7.973
 | Average | 0.409 | -8.645 | 0.604 | -12.375 | 0.277 | -5.951
Average |  | 0.329 | -9.005 | 0.498 | -13.281 | 0.236 | -6.611
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 9: Coding gain of the proposed scheme (32x32 LCTB)
<number>
Copyright 2010 FUJITSU LIMITED
Class | Sequence | Case 1 |  | Case 2 |  | Case 3 | 
 |  | BD-PSNR | BD-Bitrate | BD-PSNR | BD-Bitrate | BD-PSNR | BD-Bitrate
A | Traffic | 0.611 | -16.848 | 0.959 | -24.152 | 0.459 | -12.778
 | PeopleOnStreet | 0.334 | -6.956 | 0.663 | -13.244 | 0.259 | -5.424
 | Average | 0.473 | -11.902 | 0.811 | -18.698 | 0.359 | -9.101
B | Kimono | 0.661 | -18.275 | 1.075 | -27.786 | 0.486 | -13.684
 | ParkScene | 0.577 | -15.997 | 0.909 | -23.238 | 0.419 | -11.843
 | Cactus | 0.471 | -17.457 | 0.743 | -26.473 | 0.349 | -13.030
 | BQTerrace | 0.426 | -18.522 | 0.566 | -25.044 | 0.337 | -14.745
 | BasketballDrive | 0.463 | -18.026 | 0.765 | -28.629 | 0.358 | -14.020
 | Average | 0.520 | -17.656 | 0.812 | -26.234 | 0.390 | -13.465
C | RaceHorses | 0.546 | -11.918 | 0.853 | -17.765 | 0.380 | -8.422
 | BQMall | 0.964 | -19.765 | 1.361 | -26.281 | 0.684 | -14.457
 | PartyScene | 0.593 | -11.115 | 0.857 | -15.519 | 0.441 | -8.388
 | BasketballDrill | 0.928 | -19.737 | 1.536 | -29.693 | 0.629 | -13.877
 | Average | 0.758 | -15.634 | 1.152 | -22.315 | 0.533 | -11.286
Average |  | 0.598 | -15.874 | 0.935 | -23.439 | 0.436 | -11.879
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 10: Example of RD-Curve (Class C BQMall)
<number>
Copyright 2010 FUJITSU LIMITED
64x64 LCTB
32x32 LCTB
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 11: New buffer model for very low delay coding (1/3)
<number>
Copyright 2010 FUJITSU LIMITED
The problem of the buffer model in the conventional standards
  The picture-based CPB model in MPEG-4 AVC/H.264 does not guarantee the arrival time of the last bit of each MB into the CPB.
  In the worst case, the display timing is delayed the decoding period of a picture from the removal time of the picture.
    In the real world, the decoding period of a picture is almost equal to one frame period.
  The display timing of each picture should be equal to that of the picture in the worst case when the frame rate is constant.
  As the result, the coding delay exceeds one frame period.
Buffer model in conventional standards
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 12: New buffer model for very low delay coding (2/3)
<number>
Copyright 2010 FUJITSU LIMITED
Solution
  A picture is divided into M groups. (e.g. in the unit of one LTCB line)
    Each group contains the same number of LCTBs.
  New decoder model is introduced in the hypothetical decoder. The decoding process is invoked at each group.
  The removal time from the CPB is defined for each group. A encoder is required to set the arrival time of the last bit of each group earlier than the removal time of each group.
  The decoding period of each group becomes ( dt / M ). Thus the coding delay caused by the decoding process is reduced to ( 1 / M ) of that in the conventional buffer model.
New buffer model for very low delay coding
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 13: New buffer model for very low delay coding (3/3)
Syntax
  New parameter which describes the number of groups in a picture is added to the VUI parameters.
Semantics
  The removal time of the i-th group in the n-th picture is defined as
  tr( n, i ) = tr ( n - 1 ) + ( tr( n ) - tr ( n - 1) ) * i / M
  tr( n, i ): The removal time of the i-th group in the n-th picture
  tr( n ) : The removal time of n-th picture.
<number>
Copyright 2010 FUJITSU LIMITED
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 14: Conclusion
The coding gain of the proposed scheme from the conventional multiple slices scheme in very low delay coding is measured using TMuC 0.7.3.
The improvements in BD-Bitrate are 9.0% (64x64 LCTB) and 15.9% (32x32 LCTB).
  The gains achieved by the proposed scheme excluding the effect of bit saving of redundant slice headers are 6.6% (64x64 LCTB) and 11.9% (32x32 LCTB).
The proposed scheme only consists of the modification of high-level syntax and semantics. Thus the proposed scheme improves the coding efficiency without increasing computational complexity significantly.
New buffer model for the coding delay of less than one frame period is proposed.
We propose to start an AHG activity on the support of very low delay coding in HEVC. This activity includes:
  Discussion of high-level syntax and semantics in detail
  Further evaluation including a cross-checking
  Improvement of the reference software (including the support of tools not implemented at this time)
<number>
Copyright 2010 FUJITSU LIMITED
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 15
<number>
Copyright 2010 FUJITSU LIMITED
<number>
Copyright 2010 FUJITSU LIMITED
Copyright 2010 FUJITSU LIMITED
<number>
Notes: Copyright 2010 FUJITSU LIMITED
<number>
Copyright 2007 FUJITSU LIMITED
<number>

## Slide 16: Annex: The syntax of a slice used in this evaluation
<number>
Copyright 2010 FUJITSU LIMITED
boundary_position_in_lctb_width specifies the horizontal position of the boundary between a refreshed area and a non-refreshed area in a picture in units of the width of LCTB .
boundary_position_in_lctb_width shall be in the range from 0 to ( (pic_width_in_luma_samples + (1 << (a – 1)) >> a), where a is equal to (( log2_min_coding_unit_size_minus3 + 3 + max_coding_unit_hierarchy_depth ) .
The variable BoundaryPosition is derived as
BoundaryPosition = min( (boundary_position_in_lctb_width * (1 << a)), pic_width_in_luma_samples)
, where a is equal to (( log2_min_coding_unit_size_minus3 + 3 + max_coding_unit_hierarchy_depth ) .
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 17: Annex: Representation of the area boundary used in this evaluation
A refreshed area and a non-refreshed area are located in the left side (not including the area boundary) and in the right side of a picture, respectively. Each area has a region index.
  The region index is calculated automatically both in an encoder and a decoder in this evaluation. Those indexes may be explicitly described in a bitstream.
The region index of a non-refreshed area is equal to (K-1) when that of a refreshed area is equal to K. The region indexes increase one at each recovery point.
  The position of a recovery point in a sequence is calculated using the value of a POC both in an encoder and a decoder in this evaluation. (i.e. the recovery point SEI is not implemented at this time)
  The availability of a reference is judged by comparing the region index of a processing CTB and that of the referred CTB or pixels.
<number>
Copyright 2010 FUJITSU LIMITED
Region indexes assigned for a refreshed area and a non-refreshed area in each picture
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 18: Annex: Restriction of reference used in this evaluation (1/5)
Restriction of reference to adjacent LCTBs
<number>
Copyright 2010 FUJITSU LIMITED
Conventional (multiple slices)
Reference to a LCBT in a different slice is not allowed. (The same restriction as MPEG-4 AVC/H.264)
Proposed
Reference from a LCTB in a refreshed area to a LCTB in a non-refreshed area is not allowed.
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 19: Annex: Restriction of reference used in this evaluation (2/5)
<number>
Copyright 2010 FUJITSU LIMITED
Restriction of reference to collocated CTB for MV Competition
Conventional (multiple slices)
Same behavior as the proposed scheme. (provisional implementation)
Proposed
Reference from a CTB in a refreshed area to a CTB in a non-refreshed area is not allowed.
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 20: Annex: Restriction of reference used in this evaluation (3/5)
<number>
Copyright 2010 FUJITSU LIMITED
Restriction of motion vector
Conventional (multiple slices)
MV which is from a CTB in a refreshed area to pixels in a non-refreshed area is not allowed. (Encoder issue)
Proposal
New motion compensation which extrapolates pixels in a non-refreshed area from those in a refreshed area is applied when a CTB is inside a refreshed area.
Note
MV across a recovery point is not allowed.
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 21: Annex: Restriction of reference used in this evaluation (4/5)
<number>
Copyright 2010 FUJITSU LIMITED
Deblocking filter
Conventional (multiple slices)
No deblocking filter is applied at a slice boundary.
Proposed
No deblocking filter is applied to pixels which are located in a refreshed area adjacent to an area boundary.
Notes: Copyright 2010 FUJITSU LIMITED
<number>

## Slide 22: Annex: Restriction of reference used in this evaluation (5/5)
<number>
Copyright 2010 FUJITSU LIMITED
Adaptive Loop Filter
Conventional (multiple slices)
Same behavior as the proposed scheme. (provisional implementation)
Proposed
Pixels in a non-refreshed area is not used for filtering a pixel in a refreshed area.
Notes: Copyright 2010 FUJITSU LIMITED
<number>