## Slide 1: TE10 Informal Subjective Viewing
TE10 Coordinators

## Slide 2: Date, Time and Place
TE10 Informal Subjective Viewing
Date / Time
  Oct. 8
    From 11am to 5pm, including coffee break and lunch break time
  Oct. 9
    From 2pm to 5pm, including coffee break time
  Note: No additional session/viewing is planned next week.
Place
  Room 3410, on the 4th floor of the 3rd building

## Slide 3: Sequences
TE10 Informal Subjective Viewing
Sequences
  Note: Anchor includes TENTM deblocking filter and Qualcomm QC_ALF
  Subtest 1 (Deblocking/debanding): High Efficiency, I only case
    Kinomo(22,37), BQMall(27,37) and Parkscene(22,37)
    Anchor, Microsoft, NEC, SKKU/SKT, MediaTek(*)
  Subtest 2 (Wiener-based filtering): High Efficiency, Low Delay case
    ParkScene(27,37) and BasketballDrill(27,37)
    Anchor, No-filter, MediaTek(*), Sharp, Toshiba, Post-filter(Qualcomm)
  Subtest 3 (Offset): High Efficiency, Low Delay case
    ParkScene(27,37) and BasketballDrill(27,37)
    Anchor, MediaTek(*)
  (*) MediaTek’s results were reviewed on the second day only.
Best performing post-filtering
in terms of coding efficiency

## Slide 4: Viewing Equipments and Volunteers
TE10 Informal Subjective Viewing
PC
  Windows 7
  RAID with 8 300GB SAS 15000rpm disks
Monitor
  Sony 42’’ LCD LDM-4251TD (2D/3D)
Approximately 20 volunteers made comments and/or joined the discussion on TE10 informal viewing results.
  JCT-VC chairs quickly reviewed.

## Slide 5: Comments of Informal Viewing (1/3)
TE10 Informal Subjective Viewing
[TE10 Subset1] BQMall QP27: MS's result was fluctuating and worse than Anchor. Others were similar to Anchor.
BQMall QP37: SKKU's result was more pulsy than Anchor. NEC's result looked blurred.
Kimono: NEC proposal de-bands both QP=22 and 37. MS's results looked blurred. SKKU's results showed less pulsing than Anchor.
ParkScene: MS's result was flickering. Anchor is better than MS at QP=22. Others were similar to Anchor.
Deblocking filter in Anchor is TENTM’s.
Debanding filtering from NEC showed banding noise reduction.
Edge conscious deblocking filter from SKKU/SKT were not consistent.
Deblocikng filter from Microsoft looked blurring.
Deblocikng filter from MediaTek looked similar to TENTM’s.

## Slide 6: Comments of Preliminary Informal Viewing (2/3)
TE10 Informal Subjective Viewing
[TE10 Subset2] BasketballDrill: Post-filtering was pulsing both QP=27 and 37. Sharp's result showed more tailing than Anchor at QP=37. Toshiba's result showed tailing and worse than Anchor at QP=37. Anchor looked stable than No-filtering at QP=37. ParkScene: Post-filtering was less consistency in temporal and showed smooth tailing than Anchor. Sharp is better than Anchor at QP=27 but bad at QP=37 due to more artifacts (tailing). Anchor is best at QP=37. Loop filtering schemes (Anchor, Sharp, and Toshiba) showed better temporal consistency than Post-filtering (and No-filtering).
In-loop filtering in Anchor is QC_ALF.
In-loop filtering performs better than both post-filtering and no filtering.
Among in-loop filtering proposals, the results were not consistent.

## Slide 7: Comments of Preliminary Informal Viewing (3/3)
TE10 Informal Subjective Viewing
[TE10 Subset3] BasketballDrill: There was a comment on QP=37 that anchor is better. ParkScene: There was comments on QP=37 that MediaTek is better.
The results were not consistent.

## Slide 8: Bitrate (kbps) for Subtest 1 (HE/IO)
TE10 Informal Subjective Viewing
Sequence | Kimono |  | ParkScene |  | BQMall | 
Qp | 22 | 37 | 22 | 37 | 27 | 37
Anchor (TENTM) | 22650.07 | 3919.99 | 54370.16 | 7619.63 | 14539.1 | 4796.01
MediaTek (C142) | 22652.55 (0.011 %) | 3920.82 (0.021%) | 54369.13 (-0.002%) | 7618.53 (-0.014%) | 14539.10 (0.000%) | 4795.99 (0.000 %)
Microsoft (C273) | 22650.20 (0.001%) | 3919.91 (-0.002%) | 54370.30 (0.000%) | 7619.15 -0.006 %) | 14539.34 (0.002%) | 4795.96 (-0.001%)
NEC (C091) | 22655.34 (0.023%) | 3919.20 (-0.020%) | 54372.16 (0.004%) | 7617.55 (-0.027%) | 14540.02 (0.006%) | 4796.33 (0.007%)
SKKU/SKT (C130) | 22650.87 (0.004%) | 3920.66 (0.017 %) | 54371.34 (0.002%) | 7620.29 (0.009%) | 14540.02 (0.006%) | 4797.28 (0.026 %)

## Slide 9: Bitrate (kbps) for Subtest 2 (HE/LD)
TE10 Informal Subjective Viewing
Sequence | BasketballDrill |  | ParkScene | 
Qp | 27 | 37 | 27 | 37
Anchor (QC_ALF) | 2311.29 | 582.18 | 4021.41 | 688.59
No filtering (QC_ALF off) | 2324.06 (100.5%) | 576.32 (99.0%) | 4094.15 (101.8%) | 701.04 (101.8%)
MediaTek (C143) | 2306.12 (99.8%) | 579.64 (99.6%) | 4011.27 (99.7%) | 686.64 (99.7%)
Sharp (C173) | 2303.29 (99.7%) | 580.59 (99.7%) | 4003.66 (99.6%) | 689.24 (100.1%)
Toshiba (C082) | 2314.90 (100.2%) | 578.75 (99.4%) | 4025.93 (100.1%) | 691.74 (100.5%)
Post filtering (C113) | 2325.21 (100.6%) | 577.25 (99.2%) | 4094.87 (101.8%) | 701.52 (101.9%)

## Slide 10: Bitrate (kbps) for Subtest 3 (HE/LD)
TE10 Informal Subjective Viewing
Sequence | BasketballDrill |  | ParkScene | 
Qp | 27 | 37 | 27 | 37
Anchor (QC_ALF) | 2311.29 | 582.18 | 4021.41 | 688.59
MediaTek (C143) | 2316.21 (100.2%) | 584.63 (100.4%) | 4012.05 (99.8%) | 689.23 (100.1%)