## Slide 1
JCT-VC 096
Low-Complexity Rotational Transform
Samsung Electronics Co.,
Felix C. A. Fernandes
October 2010

## Slide 2: 8x8 Secondary Rotational Transform
ROT = secondary transform applied to 16x16, 32x32, 64x64 intra-predicted blocks
8x8 sub-block at top-left corner of DCT block is input to ROT.
DCT
ROT
(8x8 Rotational Transform)
Quantization
residuals
quantized
coefficients
coefficients
8
8
16
16

## Slide 3: ROT Definition
mi = input residuals,
mo = ROT coefficients,
D = DCT matrix,
Rh = horizontal ROT matrix,
Rv = vertical ROT matrix,
Rx, Rz = compound Given’s
rotation matrices.

## Slide 4: Structure of Rh and Rv

## Slide 5: Complexity Reduction Using Lifting Matrices
Consider the planar rotation matrix R(θ):
Factorize R(θ) into lifting matrices:
where and
Approximate u, v, w by rationals of the form k/2m to replace multipliers with adders and shifters.

## Slide 6: Rx(θ) Complexity Reduction

## Slide 7: Rz(θ) Complexity Reduction

## Slide 8: Complexity Analysis
To multiply variable x by constant c, adders and shifters are used:
  Example 1: c = 50 = binary 110010 then x * c = x * 50 = x*(25 + 24 + 21) = x<<5 + x<<4 + x<<1 so, 2 elemental adders required.
  In general, Nadders = Nisolated – 1.
When c has more than 2 consecutive 1’s in binary form, use subtraction:
  Example 2: c = 61 = binary 111101 = 1000001 – 100 then x * c = x * 61 = x * (1000001 – 100) = x<<6 – x<<2 + 1 so, 2 elemental adders required
  In general, Nadders = Nisolated + 2*Nconsecutive – 1.
Product of x and c is usually added to some other quantity. Therefore, Nadders = Nisolated + 2*Nconsecutive
Complexity reduction:
46% reduction on forward transform, 21% reduction on inverse transform.
 | Forward | Inverse
TMuC ROT | 668 | 448
Proposed ROT | 356 | 356

## Slide 9: Simulation Results
Intra high-efficiency configuration, 25 frames
Anchor: TMuC 0.7
Test: TMuC 0.7 ROT replaced by proposed low-complexity ROT
 | BD-Rate (%)
Class A | -0.01
Class B | -0.01
Class C | 0.01
Class D | -0.01
Class E | -0.01
All | -0.00