## Slide 1: TE7: Symmetry-based simplification of MDDT (JCTVC-C102)
Haitao Yang, Jiantong Zhou, Haoping Yu
Huawei Technologies
Notes: <number>

## Slide 2: Introduction
Simplified MDDT (SMDDT) was proposed in JCTVC-B039
  Reduce the number of transforms and the corresponding scan orders based on symmetry of prediction directions
TE7: MDDT simplification (JCTVC-B307)
  Reduce the number of transforms and scan orders
  Reduce the operation counts
SMDDT has been implemented in TMuC0.7
  Extended to accommodate the unified intra prediction
The performance of SMDDT in TMuC is reported in this contribution

## Slide 3: Brief review of SMDDT in JCTVC-B039 (1)
Observation & Motivation
  Symmetry in prediction directions -> symmetry in the dominant patterns of residuals
  -> Similarity in the pattern after alignment
  Residual pattern: the basis image of non-separable KLT for the residual dataset
  Alignment: flip or transpose of the residual pattern based on the symmetry of the prediction direction
(a) Pattern of Mode 0, 1 separately and jointly
(b) Pattern of Mode 3, 4 separately and jointly
(c) Pattern of Mode 5, 6, 7, 8 separately and jointly

## Slide 4: Brief review of SMDDT in JCTVC-B039 (2)
The proposed method
  Grouping of intra prediction modes based on symmetry
  X: no operation; FV: flip around the vertical axis; FH: flip around the horizontal axis
  Train a pair of separable KLT for each group, and apply it to the residual block from the corresponding group
  Several CIF and 720P sequences are used for training the transforms, CfP sequences are not used
  The pattern of group 1 is transposing symmetric, so the horizontal and vertical transform are the same
MODEAVC | 0 | 1 | 3 | 4 | 5 | 6 | 7 | 8
SMDDT mode | 0 | 0 | 1 | 1 | 2 | 2 | 2 | 2
Fwd blk operation | X | T | FV | X | X | T | FV | FH+T
Bwd blk operation | X | T | FV | X | X | T | FV | T+FH

## Slide 5: Extend SMDDT in TMuC
Mapping relationship among prediction modes, MDDT modes and SMDDT modes, and the block operations
Scan orders of transform mode 0, 4 and 5 in the MDDT implementation are used

## Slide 6: Simulation results
Software platform: TMuC 0.7
Test condition: JCTVC-B300
RD performance
Subjective evaluation: no preference in the viewing experience compared with the anchor

## Slide 7: Complexity analysis
Memory requirement (for directional prediction modes)
  The number of transforms: 16 -> 5
  The number of scan orders: 8 -> 3
Computational complexity
  Transform is implemented as matrix multiplication in the current SMDDT, which is the same as MDDT
  The flip and transpose of residual blocks can be easily implemented especially in the hardware design, and the complexity is negligible

## Slide 8: Conclusion
SMDDT performance
  Approximately the same in terms of objective performance and subjective quality
SMDDT complexity
  The number of transforms and scan orders in MDDT are reduced
Suggestion
  Adopt SMDDT as an improvement of the current MDDT in TMuC

## Slide 9
Thank You
www.huawei.com