## Slide 1: Comments on V2V Coding for HEVC
<number>
March 31, 2010
Dake He, Gergely Korodi,
Paul Imthurn, Joel Jamias,
Daniel O’Loughlin, Gaelle Martin-Cocher
Research In Motion Ltd.
Notes: <number>

## Slide 2: V2V Coding for HEVC
<number>
TMuC software
  Enabled (PIPE) when symbol_mode=2
  PIPE makes use of 12 V2V codes (Codeset 1)
Tool Experiment 12
  PIPE is evaluated against CABAC, LCEC
Tool Experiment 8
  Codeset 1 is evaluated against another set of 12 V2V codes (Codeset 2) from RIM, defined for the same probability set.

## Slide 3: TE8 Results
<number>
Codesets | Loss | Enc. Thru | Dec. Thru | Cross-checked
BAC (JM11/KTA) | 0.159 | 57.7 | 144.4 | Yes
BAC (JM17) | 0.159 | 130.7 | 136.1 | No
Codeset 1 | 0.147 | 68.7 | 110.4 | Yes
Codeset 2 | 0.122 | 222.0 | 251.1 | Yes
Codesets are tested on bernoulli bin sequences generated according to probabilities defined by PIPE. Each sequence consists of 1billion bins.
Loss (in percentage) is measured against the entropy
Encoding and decoding throughput data show the million bin symbols processed per second.
Results are cross verified by TI.
Test environment: Core-i7 860@2.80GHz, Linux, g++ 4.4.1

## Slide 4: Hardware Results
<number>
Note that hardware results are not yet cross verified.

## Slide 5: Hardware Results
<number>
Design | Mean | High Range | Low Range
Codeset 1 | 1.68 | 2.56 | 0.80
Codeset 2 | 8.18 | 8.70 | 7.66
95% Confidence Interval for Bins per Clock Cycle
Note that hardware results are not yet cross verified.

## Slide 6: Tree Design
Implementation is constrained by design.
Conflicting objectives
  Compression efficiency
  Decoding throughput, encoding throughput
  Size (storage complexity)
  Power consumption in hardware
Under the constraint of compression efficiency
  A tradeoff between size and decoding throughput cannot be avoided.
Power consumption
  More area does not necessarily mean higher power consumption
  Higher clock rate => higher power consumption
Choice:
  Design the trees for high throughput and low power consumption
<number>

## Slide 7: Implementation
PIPE in TMuC
  Bin decoder reads one bit at a time same as CABAC.
V2V codes are known.
  Bin decoder can read and process as many bits as possible.
<number>

## Slide 8: An example
<number>
Parsed Sequence | Probability | Codeword
00 | 0.090000 | 000
010 | 0.063000 | 1100
011 | 0.147000 | 001
100 | 0.063000 | 1101
101 | 0.147000 | 010
110 | 0.147000 | 011
1110 | 0.102900 | 100
11110 | 0.072030 | 1110
111110 | 0.050421 | 1111
1111110 | 0.117649 | 101
Codeset 1
Codeset 2

## Slide 9: Interaction with Context Modeling
Context modeling and bin decoding are two stages in a pipeline.
  Design choice made for one will directly affect the other.
3 tools on how to improve throughput of context modeling.
PIPE is intended to improve throughput of bin decoding
Obviously, a match in throughput is preferred.
<number>
Bin decoding
Context modeling

## Slide 10: Interaction with context modeling
Context model should not be stalled too frequently due to an empty bin buffer.
Bin decoders need to provide a higher throughput than the context model.
Example:
  For an overall throughput of 4, bin decoders might run at 6 bins/cycle.
<number>

## Slide 11: Recommendations
Consider an alternative set of V2V codes, e.g., Codeset 2 tested in TE8 for applications demanding high throughput.
  These codes can be used in both operational modes: parallel or interleaved.
Define throughput requirements, possibly depending upon profiles.
Define size requirements, possibly depending upon profiles.
Adopt the implementation of Codeset 2 for improved throughput
Adopt solutions for context modeling in TE8 to improve throughput.
<number>