## Slide 1: Fine granularity slices
JCTvc-C154
Rickard Sjöberg, per wennersten
ericsson AB

## Slide 2: two slice problems
Problem 1 - The TMuC software does not support slices
  Important to get slices working in the TM source code as soon as possible for tool testing, e.g. PIPE/V2V terminating bit cost
  New tools should not be slice ignorant
Problem 2 - Text currently only support slice boundaries on maximum CU resolution (JCTVC-B205)
  Common conditions specifies max CU size of 64x64
  This is 16 times larger than a 16x16 macroblock
  Makes slice size control difficult, e.g. to create slices of max 1500 bytes
  For highly active and hard-to-compress areas, one single CU may be larger than the target number of slice bytes

## Slide 3: possible solutions
Option 1 – Reduce max CU size to improve slice granularity
  TE12 results show that the impact of lowering max CU is large
  Using 32x32 gives average 5% bit-rate increase for random access and low delay (JCTVC-C259)
Option 2 – Increase the QP
  Complicates encoder and reduces the subjective quality
  Very large QP increase may be needed to reduce max CU size
    PartyScene QP22: 2630 bytes QP27: 1923 bytes QP 32 1343 bytes
Option 3 – Enable slice boundaries for other CU sizes than 64x64
  Straightforward solution
  Currently the CU is the root of PU and TU trees
Document C154 contains
  Proposal to enable smaller CU size slice boundaries
  Proposal to use FLC instead of UVLC for slice address
  Proposal to remove end_of_slice_flag for LCEC in the TMuC source code

## Slide 4: proposal 1 - slices
We propose to define slices as a sequence of minimum CU blocks instead of maximum CU blocks
Fig 1 - 64x64 block split down to 8x8 blocks
Slice address specified by min CU block number
Decoder starts by decoding the largest possible CU at that starting coordinate

## Slide 5: proposal 2 - FLC
Slice address signaling is currently using UVLC which may lead to very long VLC code words, close to 32 bits
Entropy of the address is not matched by the UVLC
We propose to replace UVLC coding of slice start by fixed length coding (FLC) with one-bit shortcut for the first block
1920x1080 example: Each picture contains of 32,640 min CU:s of size 8x8
Block nr | UVLC | FLC
0 | 1 | 1
1 | 010 | 0000000000000000
2 | 011 | 0000000000000001
... |  | 
32639 | 00000000000000111111110000000 | 0111111101111111
1 or 16 bits (average = 16.00 bits)
1-29 bits (average for all block numbers = 26.99 bits)
Bitrate saving of 11 bits per slice = 0.1% for 1500 byte slices

## Slide 6: Syntax and semantics, 1st draft
first_sctb_is_zero_flag indicates whether the slice address is 0 or not. If first_sctb_is_zero_flag is 1, the variable SliceAddress is set to 0 and the decoding starts with the first LCTB in the picture.
first_sctb_in_slice_minus_1 specifies the address of the first smallest coding tree block in the slice and shall be represented by Ceil(Log2(NumSCTBsInPicture-1)) bits in the bitstream where NumSCTBsInPicture is the number of SCTB:s in a picture. The slice decoding starts with the largest coding unit possible at the slice starting coordinate given by the address.
The slice address is specified as follows:
SliceAddress = first_sctb_in_slice_minus_1 + 1
slice_header( ) { | C | Descriptor
first_sctb_is_zero_flag | 2 | u(1)
if(first_sctb_is_zero_flag == 0) { |  | 
first_sctb_in_slice_minus_1 | 2 | u(v)
} |  | 

## Slide 7: proposal 3 - fix for LCEC
We noted that an end_of_slice_flag codeword is sent for each max CU in the TMuC code even though it is not necessary for VLC:s
In the TMuC specification, end_of_slice_flag codewords are only sent for V2V/PIPE
All end_of_slice_flag codewords in the TMuC 0.7 anchor streams were counted and the bitrate savings of removing it was calculated
Since removing end_of_slice_flag for LCEC is a quick fix we propose to do it asap
Coding conditions | Avg | Worst case
Random Access | -0.5 % | -2.1% BQTerrace_1920x1080_60qp37.bin
Low delay | -0.7 % | -4.6% Vidyo4_720p60qp37.bin
All-Intra | -0.1 % | -0.3% Kimono1_1920x1080_24qp37.bin

## Slide 8: proposal 4 – Max CU signaling
Late contribution (reflector e-mail, off-line discussions)
CU issues with current TMuC text JCTVC-B205_draft007.doc:
Current TMuC signals both CU width and height although we do not have rectangular CUs in the design
CU width and CU height are unconstrained
No restrictions on MaxCodingUnitHierarchyDepth
Current signaling is broken
Proposed cleanup: Revert to JCTVC-A205_draft002.doc

## Slide 9: proposal 4 – Max CU syntax
Old text: JCTVC-B205_draft002.doc
seq_parameter_set_rbsp() |  | 
log2_min_coding_unit_size_minus3 |  | ue(v)
max_coding_unit_hierarchy_depth |  | ue(v)
seq_parameter_set_rbsp() |  | 
max_coding_unit_width |  | ue(v)
max_coding_unit_height |  | ue(v)
max_coding_unit_hierarchy_depth_correct |  | u(1)
log2_min_transform_unit_size_minus2 |  | ue(v)
Current text: JCTVC-B205_draft007.doc

## Slide 10: proposal 4 – Max CU syntax
Issues
We do not have rectangular CUs, only square CUs
max_coding_unit_width and max_coding_unit_height are unconstrained
While loop design is not straightforward
The while loop does nothing
No restrictions on MaxCodingUnitHierarchyDepth
max_coding_unit_width specifies the maximum width of a coding unit
max_coding_unit_height specifies the maximum height of a coding unit
max_coding_unit_hierarchy_depth_correct equal to 0 specifies that the coding unit hierarchy depth is not incremented. max_coding_unit_hierarchy_depth_correct equal to 1 specifies that the coding unit hierarchy depth is incremented by 1.
The variable MaxCodingUnitDepth is derived as
AddCUDepth = 0 While ( max_coding_unit_width >> max_coding_unit_hierarchy_depth_correct ) > ( 1 << ( log2_min_transform_unit_size_minus2 ) + AddCUDepth ) ) ) { AddCuDepth } MaxCodingUnitHierarchyDepth = max_coding_unit_hierarchy_depth_correct + AddCUDepth
Current text:

## Slide 11: proposal 4 – Max CU syntax
Old text:
log2_min_coding_unit_size_minus3 specifies the minimum size of a coding unit.
The variable MinCodingUnitSize is derived as
MinCodingUnitSize = 1 << ( log2_min_coding_unit_size_minus3 + 3 )
max_coding_unit_hierarchy_depth specifies the maximum hierarchy depth for coding units.
The variable MaxCodingUnitSize is derived as
MaxCodingUnitSize = 1 << ( log2_min_coding_unit_size_minus3 + 3 +
max_coding_unit_hierarchy_depth )
The bitstream shall not contain data that result in a value of MaxCodingUnitSize that is greater than 128.

## Slide 12: summary
Proposal 1
  Define slices as a sequence of minimum CU blocks instead of maximum CU blocks
Proposal 2
  Use FLC instead of UVLC for slice address
Proposal 3
  Remove end_of_slice_flag for LCEC in the TMuC source code
Proposal 4
  Revert coding of minimum and maximum CU size to the syntax and semantics of JCTVC-B205_draft002.doc and change software accordingly