## Slide 1: TMuC 0.7 results with sequence dependent QPs
JCTVC-C155
Kenneth Andersson, Rickard Sjöberg
Ericsson AB

## Slide 2: Summary
This informative contribution investigates performance for random access and low delay when using bitrates closer to CfP conditions instead of common conditions B300.
  RD curves shows that a fixed QP range cause high rate points for some sequences
  High rate points can cause optimization of codec performance for high rates
  Despite large rate differences, using sequence specific QPs has a small effect on BDrate performance using common conditions as anchor
  Sequence dependent QPs can potentially better address application bitrates and also produce better rate points for subjective assessment
  A positive side effect is that worst case simulation time is reduced by about 20%

## Slide 3: Background
Common conditions B300 uses the same fixed QP set for all sequences
  QP 22 results in high bitrates (>40Mbps) for some of the common condition sequences, far from application bitrates in broadcast and video communication
  At low QP it is hard to distinguish coding artifacts for some sequences (could potentially be verified at informal viewing at the meeting)

## Slide 4: Experimental setup
Anchor:
  TMuC 0.7 for B300 using QP = 37, 32, 27 and 22
Test:
  TMuC 0.7 for B300 using sequence specific QPs
    For simplicity the max and min QPs from Samsungs CfP configuration have been used for generation of two inbetween QPs e.g. in total 4 QPs

## Slide 5: Low-delay high-efficiency
Anchor: QP=37, 32, 27, 22
Test using: QP=32, 30, 28, 26

## Slide 6: Low-delay high-efficiency
Anchor: QP=37, 32, 27, 22
Test using: QP=36, 32, 29, 26

## Slide 7: Low-delay high-efficiency
Anchor: QP=37, 32, 27, 22
Test using: QP=40, 36, 33, 30

## Slide 8: Random access high-efficiency
Anchor: QP=37, 32, 27, 22
Test using: QP=33, 31, 28, 26

## Slide 9: Random access high-efficiency
Anchor: QP=37, 32, 27, 22
Test using: QP=35, 32, 28, 25

## Slide 10: Random access high-efficiency
Anchor: QP=37, 32, 27, 22
Test using: QP=41, 37, 34, 30

## Slide 11: BDrate performance using Linux cluster
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0,3 | 0,3 | 0,3 | -0,3 | -0,3 | 0,0
Class B | -0,4 | -0,1 | -0,2 | -0,5 | -0,2 | -0,4
Class C | 0,1 | -1,1 | -1,1 | 0,1 | -0,9 | -0,9
Class D | 0,0 | -0,3 | -0,5 | 0,0 | -0,5 | 0,0
Class E |  |  |  |  |  | 
All | -0,1 | -0,4 | -0,5 | -0,1 | -0,5 | -0,4
Enc Time[%] | 98% |  |  | 97% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0,4 | 0,0 | 0,1 | -0,2 | 0,1 | -0,2
Class C | 0,1 | 0,6 | 0,8 | 0,2 | 0,3 | 0,3
Class D | 0,0 | 0,4 | 0,2 | 0,1 | 0,1 | 0,2
Class E | 0,2 | -0,5 | 0,5 | 0,0 | -1,8 | -0,1
All | -0,1 | 0,2 | 0,4 | 0,0 | -0,2 | 0,1
Enc Time[%] | 99% |  |  | 98% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 

## Slide 12: Conclusions
The use of sequence specific QPs has a marginal effect on BDrate measurements compared to B300, e.g. RD curves for TMuC at various QP behave similar
Sequence specific QPs can avoid future optimization of codec performance at bitrates far from application bitrates
Sequence specific QPs can in most cases give rate points better suited for subjective evaluation
The advantage of keeping one fixed set of QPs for all sequences is simplicity and a large span of QP values.