## Slide 1: Parallel adaptive loop filter
Tomoyuki Yamamoto
Tomohiro Ikai
SHARP Corporation
3rd Meeting: Guangzhou, CN, 7-15 October, 2010
Notes: <number>

## Slide 2: Contents
TE10 experiment
Proposed/Evaluated system
Experimental results
Conclusion
<number>
Notes: <number>

## Slide 3: TE10 experiment
Category
  Subtest 2:Wiener-based in-loop filters
    JCTVC-C083 [TE coordinators (NEC and TOSHIBA)]
Anchor
  TMuC 0.7
    Sum-modified Laplacian based ALF
Crosscheck & Complexity analysis
    JCTVC-C145 [MediaTek]
    JCTVC-C071 [Zhejiang Univ.]
<number>
Subtest | Proponent | Method name[JCTVC-B310]
2 | MediaTek | Quadtree-based Adaptive Restoration
 | Qualcomm (Anchor) | Adaptive Filter based on Combination of Sum-Modified Laplacian Filter Indexing
 | Sharp | Parallel adaptive loop filter
 | Toshiba | Quadtree-based Adaptive Loop Filter
Table 1 Cross checkers
Notes: <number>

## Slide 4: Proposed/Evaluated system
Concept
  Proposed system combines De-blocking filter and Wiener-based filter
Benefit
  improve coding efficiency
  process filters in parallel
<number>
De-blocking filter ( DF )
Wiener-based filter ( ALF )
post-DF signal
pre-DF signal
Conventional
system
Proposed system
De-blocking filter ( DF )
Wiener-based filter ( ALF )
Notes: <number>

## Slide 5: Proposed/Evaluated system
Parallel friendly feature
  mainly pre-DF signal is used
  only one post-DF signal is used
Outcome by the features
  DF and most of ALF can be processed in parallel
    pre-DF spatial filters(#1 and #2) are independent each other
post-DF signal
pre-DF signal
spatial fitler#1
spatial fitler#2
weighting
+
DF
ALF
Notes: <number>

## Slide 6: Proposed/Evaluated system
Other specification
  Filter shape
    Diamond 1/2 point-symmetric filter with dc offset
  Signaling
    Filter coeffs. are intra-predicted and signaled in slice header.
    Filter control(on/off) flags are signaled in CU.
    Conventional 1 input ALF or proposed 2 input ALF can be switched by alf_parallel_mode in slice header.
<number>
5x5: 15 coeffs.
7x7: 24 coeffs.
9x9: 34 coeffs.
slice header
CUs
CU
coeffs.
alf flag
alf_parallel_mode
Notes: <number>

## Slide 7: Experimental results (Summary)
<number>
Note: The number of encoding pass is 16, which is the same as the anchor.
 |  | BD-rate Y | BD-rate U | BD-rate V
Intra Only (optional) | Class A | -0.9 | -0.2 | 0.3
 | Class B | -0.9 | -0.8 | -0.5
 | Class C | -0.5 | -1.2 | -1.0
 | Class D | -0.8 | -1.1 | -1.0
 | Class E | -0.5 | 0.1 | -0.3
 | Average | -0.7 | -0.7 | -0.6
 | Encoding Time | 100 % |  | 
 | Decoding Time | 93 % |  | 
Randam Access (mandatory) | Class A | -0.7 | -0.1 | -0.1
 | Class B | 0.0 | -1.1 | -1.0
 | Class C | -0.5 | -1.2 | -0.9
 | Class D | -0.8 | -1.1 | -0.7
 | Class E | N/A | N/A | N/A
 | Average | -0.4 | -1.0 | -0.8
 | Encoding Time | 100 % |  | 
 | Decoding Time | 96 % |  | 
Low Delay (mandatory) | Class A | -0.1 | -0.9 | -0.8
 | Class B | -0.3 | -0.9 | -0.6
 | Class C | -1.0 | -0.8 | -0.7
 | Class D | -0.2 | -0.1 | 0.1
 | Class E | N/A | N/A | N/A
 | Average | -0.4 | -0.7 | -0.5
 | Encoding Time | 100 % |  | 
 | Decoding Time | 96 % |  | 
Notes: <number>

## Slide 8: Experimental results (BD-rate Y details)
<number>
# | Sequences | IntraOnly | RandamAccess | LowDelay
S01 | Traffic | -1.0 | -2.1 | N/A
S02 | PeopleOnStreet | -0.7 | 0.6 | N/A
S03 | Kimono | -0.2 | 0.2 | 0.6
S04 | ParkScene | -1.7 | -1.3 | -1.0
S05 | Cactus | -0.9 | 0 | 0
S06 | BasketballDrive | -0.7 | 0.2 | 0.7
S07 | BQTerrace | -0.8 | 1.0 | -0.7
S08 | BasketballDrill | -0.7 | -1.0 | -0.6
S09 | BQMall | -0.7 | -0.6 | -0.5
S10 | PartyScene | -0.4 | -1.1 | -0.7
S11 | RaceHorses | -0.3 | 0.5 | 0.4
S12 | BasketballPass | -0.9 | -0.4 | -0.1
S13 | BQSquare | -0.4 | -1.7 | -3.0
S14 | BlowingBubbles | -0.8 | -0.7 | -0.3
S15 | RaceHorses | -1.0 | -0.3 | -0.6
S16 | Vidyo1 | 0 | N/A | 0.4
S17 | Vidyo3 | -0.9 | N/A | 0.1
S18 | Vidyo4 | -0.5 | N/A | -1.1
Average | Class A | -0.9 | -0.7 | 0
 | Class B | -0.9 | 0 | -0.1
 | Class C | -0.5 | -0.5 | -0.3
 | Class D | -0.8 | -0.8 | -1
 | Class E | -0.5 | 0 | -0.2
 | All | -0.7 | -0.4 | -0.4

## Slide 9: Conclusion
Parallel adaptive loop filter
  Evaluated in TE10 subtest 2 proposal
    JCTVC-C083 [TE coordinators (NEC and TOSHIBA)]
  Crosscheck & Complexity analysis
    JCTVC-C145 [MediaTek], JCTVC-C071 [Zhejiang Univ.]
  Features
    combine DF and Wiener-based filter
      using pre-DF and post-DF signal
    benefit
      coding efficiency
      parallelism
Experimental results
    0.7 % / 0.4 % / 0.4 % bit-rate reduction
      in IntraOnly / RandamAccess / LowDelay
    Encoding time ratio is 100 %
    Decoding time ratio is 93 to 96 %
<number>
Notes: <number>