## Slide 1: Enhanced Switching of Interpolation Filter for HEVC
Tomonobu Yoshino, Sei Naito, Shigeyuki Sakazawa (KDDI corp.)

## Slide 2: Introduction
About this contribution
  Propose a new syntax for Switch Interpolation Filter (SIF) technology
Background
  AIF requires huge computational cost
  Switch Interpolation Filter (SIF) approach
  A lot of candidates contributes to high coding efficiency
Related Work
  Single-pass SIFO (JCTVC-A121)
Proposal
  Enhanced syntax for SIF
  Flexibility of pre-defining filter coefficients

## Slide 3: Overview of Enhanced SIF syntax
Concept
  Flexible syntax for SIF
Assumption
  6-tap symmetric interpolation filter
Feature
  Pre-define a lot of filter coefficient candidates
  Update filter coefficients
  Update the number of filter coefficient candidates
Variety of coefficient set
  Define the coefficients for 1/2-pel position
  Select coefficient set independently for horizontal/vertical (separable filter)

## Slide 4: Proposal (1) : Filter coeffcients
Pre-define filter coefficients
  Pre-define filter coefficients
  Encode coefficients for ½-pel position (pos_b & pos_h)
  Generate the other (¼ -pel) coefficients based on linear interpolation
Choose best pre-defined filter slice by slice
Fractional-pel
Integer-pel
Define coefficients for position b & h

## Slide 5: Proposal (2) : Syntax
Picture Parameter Set
  Flag : Identify ESIF ON/OFF
  The number of pre-defined filter coefficient sets
  Filter coefficients
Slice header
  Flag : Identify whether ESIF is available for the current slice or not
  Idx_hor / Idx_ver : Indicate the selected coefficient set for pos_b / pos_h, if ESIF available in the current slice

## Slide 6: Coding Conditions
Coding condition : N11113
  Constraints Set 2 (IpPp)
Software : Implemented on JM17.0
Search Method : EPZS
Evaluation : VCEG-AI11 (BD-bitrate, BD-PSNR)

## Slide 7: Filter Coefficients
No.1 : [ 13 -40 155 155 -40 13]
No.2 : [ -5 -28 161 161 -28 -5]
No.3 : [-30 30 128 128 30 -30]
No.4 : [-22 38 112 112 38 -22]
No.5 : [ 7 24 97 97 24 7]
No.6 : [-26 73 81 81 73 -26]
No.7 : [ 5 -20 143 143 -20 5]
No.8 : [ 8 -40 160 160 -40 8] (same as H.264)
Case 1 (4 sets) : No.5 - No.8
Case 2 (8 sets) : No.1 - No.8

## Slide 8: Experimental result (Case 1: 4 sets)
Class | Sequence | BD-bitrate[%] | BD-PSNR[dB]
B1 (1080p) | Kimono | -3.51 | 0.15
 | ParkScene | -1.79 | 0.07
B2 (1080p) | Cactus | -0.60 | 0.02
 | BasketBallDrive | -2.84 | 0.10
 | BQTerrace | -4.98 | 0.13
C (WVGA) | BasketBallDrill | -1.20 | 0.05
 | BQMall | -1.23 | 0.06
 | PartyScene | -0.34 | 0.01
 | RaceHorses | -1.18 | 0.05
D (WQVGA) | BasketBallPass | -3.18 | 0.15
 | BQSquare | -0.87 | 0.03
 | BlowingBubbles | -0.79 | 0.03
 | RaceHorses | -0.70 | 0.03
E (720p) | Vidyo1 | -2.77 | 0.13
 | Vidyo3 | -2.53 | 0.12
 | Vidyo4 | -4.40 | 0.18
Average |  | -2.06 | 0.08

## Slide 9: Experimental result (Case 2: 8 sets)
Class | Sequence | BD-bitrate[%] | BD-PSNR[dB]
B1 (1080p) | Kimono | -3.86 | 0.17
 | ParkScene | -2.45 | 0.09
B2 (1080p) | Cactus | -0.68 | 0.02
 | BasketBallDrive | -3.00 | 0.11
 | BQTerrace | -4.72 | 0.12
C (WVGA) | BasketBallDrill | -1.36 | 0.05
 | BQMall | -1.56 | 0.07
 | PartyScene | -0.43 | 0.02
 | RaceHorses | -1.50 | 0.06
D (WQVGA) | BasketBallPass | -3.45 | 0.16
 | BQSquare | -0.43 | 0.02
 | BlowingBubbles | -1.10 | 0.04
 | RaceHorses | -0.98 | 0.05
E (720p) | Vidyo1 | -3.24 | 0.14
 | Vidyo3 | -4.14 | 0.20
 | Vidyo4 | -3.74 | 0.15
Average |  | -2.29 | 0.09

## Slide 10: Complexity
Class | Enc | Dec
B1 |  | 
B2 |  | 
C |  | 
D |  | 
E |  | 
Class | Enc | Dec
B1 |  | 
B2 |  | 
C |  | 
D |  | 
E |  | 
Case 1 (4 sets)
Case 2 (8 sets)

## Slide 11: Low-complexity approach
BD-PSNR (v.s. H.264) [dB]
Computing time
Sequence | EAIF | [1]
A | 0.45 | 0.33
B | 0.35 | 0.29
C | 0.36 | 0.25
D | 0.42 | 0.27
Sequence | EAIF | [1]
AIF processing time [msec] | 2490.6 | 802.2
Reduction ratio [%] | -- | 67.8
[1] “Low-complexity Scheme for Adaptive Interpolation Filter Based on Amplitude Characteristic
Analysis”, ICIP2010, Sep. 2010

## Slide 12: Conclusion
Proposed ESIF (Enhanced Switch Interpolation Filter)
Support a new syntax for flexible SIF design
  Adaptively updating filter coefficients and the number of filter sets
  Encode filter coefficients for ½-pel position (b & h)
BD-bitrate against H.264 reached 2.3%
Flexibility of pre-defined filter coefficients is important to optimize the coding performance
Suggestion : Flexible syntax for defining filter coefficients

## Slide 13
Thank you
Tomonobu Yoshino
E-mail : to-yoshino@kddi.com
Phone : +81 49 278 7587
FAX : +81 49 278 7439