## Slide 1
<number>
TE12.3: Results for planar prediction tests by Nokia
JCTVC-188
Jani Lainema, Kemal Ugur, Oguz Bici
3rd JCT-VC meeting, Guangzhou China
October 2010

## Slide 2: Background
<number>
Planar Prediction is used to reconstruct smooth regions in a visually pleasing way
  Signal the bottom-right sample and reconstruct the macroblock using upper row, left column and signalled sample
  1 bin/bit for Intra CU to indicate if planar mode is active
Step – 1: Interpolate rightmost and bottom samples
Step – 2: Bi-linear interpolation of middle samples

## Slide 3: Results: Intra
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.0 | -0.9 | -0.8 | -0.7
Class B | 0.0 | 0.1 | 0.1 | -0.8 | -0.7 | -0.6
Class C | 0.0 | 0.0 | 0.0 | -0.9 | -0.8 | -0.7
Class D | -0.1 | 0.0 | 0.0 | -0.9 | -0.7 | -0.6
Class E | 0.0 | 0.0 | 0.1 | -0.8 | -0.2 | -0.6
All | 0.0 | 0.0 | 0.0 | -0.9 | -0.6 | -0.6
Enc Time[%] | 104 % |  |  | 121 % |  | 
Dec Time[%] | 80 % |  |  | 97 % |  | 
<number>

## Slide 4: Results: Random Access and Low Delay
<number>
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.0 | -0.3 | -0.3 | -0.2
Class B | 0.0 | 0.0 | -0.1 | -0.2 | -0.2 | -0.2
Class C | 0.0 | -0.1 | 0.1 | -0.2 | -0.2 | -0.1
Class D | 0.0 | 0.0 | -0.1 | -0.2 | -0.3 | -0.2
Class E |  |  |  |  |  | 
All | 0.0 | 0.0 | -0.1 | -0.2 | -0.2 | -0.2
Enc Time[%] | 101 % |  |  | 67 % |  | 
Dec Time[%] | 78 % |  |  | 86 % |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.1 | 0.0 | 0.0 | 0.0 | -0.1
Class C | 0.0 | -0.1 | 0.1 | 0.0 | 0.0 | 0.1
Class D | 0.0 | 0.2 | 0.2 | 0.0 | 0.1 | -0.1
Class E | 0.0 | 0.3 | -0.2 | 0.0 | -0.7 | 0.2
All | 0.0 | 0.1 | 0.0 | 0.0 | -0.1 | 0.0
Enc Time[%] | 99 % |  |  | 103 % |  | 
Dec Time[%] | 95 % |  |  | 79 % |  | 

## Slide 5: Indicating planar mode in LCEC
According to low complexity results the current signalling for planar mode is not optimal
  ~0.9% objective penalty in low complexity intra configuration
  1 bit used to indicate if Intra CU is planar coded (typically 10-15% of CUs)
Joint coding of planar_flag and intra_split_flag seems to compensate majority of the inefficiency giving 0.6% gain over the anchors
Propose to include joint coding of planar and split flags to future LCEC
<number>
codeword | planar_flag | intra_split_flag
1 | 0 | 0
01 | 0 | 1
00 | 1 | 0
 | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.6 | -0.9 | -0.8
Class B | -0.6 | -0.9 | -0.8
Class C | -0.6 | -0.8 | -0.8
Class D | -0.5 | -0.7 | -0.6
Class E | -0.7 | -0.8 | -1.0
All | -0.6 | -0.8 | -0.8
Enc Time[%] | 72 % |  | 
Dec Time[%] | 96 % |  | 

## Slide 6
<number>

## Slide 7
<number>

## Slide 8
<number>

## Slide 9
<number>

## Slide 10
<number>