## Slide 1: Evaluation of intra prediction based on repetitive pixel replenishment (JCTVC-C189)
3rd Meeting: Guangzhou, CN, 7-15 Oct, 2010
Notes: My name is Kenichi Iwata from Renesas Electronics Corporation.
I’m going to present a Renesas’ response for the CfP. A126.

## Slide 2: Introduction
Previous work (JCTVC-B033)
  Renesas proposed intra prediction based on repetitive pixel replenishment (Intra RPR)
    using more pixels
    using more directions
  BD-PSNR gain of predicted image against CfP alpha anchor
    average of 1.33dB and up to 3.30dB
  Performance on TMuC at Basketball Drill (Class C)
    BD-Bitrate : -4.78%, BD-PSNR : 0.22dB
This contribution presents more evaluation results of Intra RPR.
Notes: Bits of Intra-picture averages 26% in alpha anchor, and 53% at most.
So, we focused on a much reduction of intra-bit and improve quality. It also good effect on following picture.
In AVC coding, intra-frame prediction use only neighboring pixel, we propose more pixels to create predicted image.
Basic idea is based on that 2D picture has it own correLAtion, periodic texture.
Similar texture often exists in a frame as shown in this slide.
We reduced this overlapping redundancy using block-matching-based intra vector prediction.
In this scheme, we can use more pixels than the AVC intra for intra prediction.
riPEtitive
repLEnishment

## Slide 3: Motivation
Basic idea
  NOT enough quality of predicted image by conventional intra prediction caused by using only neighboring pixels.
  Applying 2-D template matching to intra prediction.
Examples fit for
block matching
rather than AVC.
Traditional issue
  Nearer image is more similar at the most case.
  But, nearer image has more not-coded pixels in reference block.
  How these pixels are processed greatly affects coding efficiency.
Coded pixel area
Not-coded pixel area
Vector
Prediction
Invalid to be used
Notes: Bits of Intra-picture averages 26% in alpha anchor, and 53% at most.
So, we focused on a much reduction of intra-bit and improve quality. It also good effect on following picture.
In AVC coding, intra-frame prediction use only neighboring pixel, we propose more pixels to create predicted image.
Basic idea is based on that 2D picture has it own correLAtion, periodic texture.
Similar texture often exists in a frame as shown in this slide.
We reduced this overlapping redundancy using block-matching-based intra vector prediction.
In this scheme, we can use more pixels than the AVC intra for intra prediction.
riPEtitive
repLEnishment

## Slide 4: Repetitive pixel replenishment
If reference block includes a not-coded area, intra vector is multiplied as (2Vx, 2Vy), and adaptively padding such region by using new reference pixel as shown in Fig. (b).
This scheme is especially effective to predict the cyclic patterns.
(a) Intra vector prediction
(b) Adaptive padding
Predicted block
(Vx, Vy)
(2Vx, 2Vy)
Copy
Copied from
(Vx, Vy) region
Copied from
(2Vx, 2Vy) region
-SR
+SR
(Vx, Vy)
Current block
Prediction block
-SR
X
Y
0
Search range
(Coded area)
SR: Search Range
Not-coded area
Notes: In our proposal, search point covers 33x16
In this contribution, intra vector prediction is conducted by each 8x8 block unit and searches 16 blocks range.
The motion vectors are signaled by calculating PMV to neighboring 8x8 blocks. The coding mode of the intra vector prediction is identified by I_NxN mode and multiplexed 1-bit intra vector flag. We apply the intra vector prediction only to I slice.
We can expand prediction block in N, integer times basis.

## Slide 5: More Pixels, More Directions
Current block
Predicted block A
RPR block B
Coded block
Not-coded area
Predicted block
[-2, -3]

## Slide 6: More Pixels, More Directions
Current block
RPR block B
Coded block
Not-coded area

## Slide 7: Predicted Image of Anchor (P01S08R1C1, Frame 0)

## Slide 8: Predicted Image of Proposal (PxxS08R1C1, Frame 0)
Notes: Here is predicted image of Anchor and Renesas’ proposal.
Predicted image of Renesas’ proposal was improved significantly, as you can see.
We understood the predicted error is reduced by our scheme.

## Slide 9: Performance evaluation of Intra RPR on TMuC
Condition
  Intra RPR parameter setting
    Search range: horizontal [-16, 16], vertical [-16, 0]
    Template block size: 8x8 (fixed)
    Search precision: integer pixel
  TMuC condition
    Version 0.1
    LCU size : 16x16
    Tool configuration : ADI, CIP, ALF, IBD, HAD, SRD, RDQ
  Experimental condition
    QP : 22, 27, 32, 37
    First 20 pictures of all sequence, Intra-only

## Slide 10: Experimental results
BD-rate reduction
  Y : 0.8%，U : 1.2%, V : 1.3%
Complexity
  Encoding time : About 2 times against w/o Intra-RPR
        (Not optimized yet)

## Slide 11: Performance results of Intra RPR on TMuC
Results of each sequence

## Slide 12: Conclusion
Renesas proposed intra prediction based on repetitive pixel replenishment (Intra RPR).
  using more pixels
  using more directions
Performance on TMuC
  BD-rate: -0.8 % (Y), -1.2% (U), -1.3% (V)
  up to -4.1% (Y), -5.8% (U), -6.3% (V)
  Encoding time : About 2 times against w/o Intra-RPR
Further examination of Intra RPR in TE6
  Implement to novel TMuC (or TM)
  Adaptive unit size
  Harmonization with other intra coding tools
Notes: We will keep working on performance evaluation with TMuC following common tests condition in AHG on Intra Prediction.

## Slide 13: [Informative] Experimental results on TMuC 0.7
Condition
  TE common experimental condition
  Enable all other intra coding tool used for Anchor
  Intra RPR template block size: 8x8, 16x16, 32x32, 64x64
  First picture only

## Slide 14
Notes: Thank you for your attention.