## Slide 1: TE6: Overlapped Block Intra Prediction (OBIP)
Kai Zhang, Xun Guo, Jicheng An, Mei Guo, Yu-Wen Huang and Shawmin Lei
MediaTek Inc.
Presented by Shawmin Lei
3rd JCT-VC Meeting in Guangzhou
7-15 October, 2010
Notes: <number>

## Slide 2: Outline
Overview
Introduction
Proposed OBIP algorithm
Experimental results
Conclusions
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 3: Overview
An Overlapped Block Intra Prediction (OBIP) method is proposed
  The idea is analogous to OBMC.
  Generate multiple predictors using the modes from the current block and the neighboring blocks
  Generate prediction of the current block using the weighted sum of these predictors
Coding performance
  All intra high efficiency – BD-rate reduction of 1.0%
  All intra low complexity – BD-rate reduction of 1.7%
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 4: Outline
Overview
Introduction
Proposed OBIP algorithm
Experimental results
Conclusions
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 5: Prior Directional Intra Prediction
Single-directional prediction
  In H.264/AVC
    8 directional prediction modes and DC
  In TMuC
    Up to 33 directional modes and DC
  Work well in simple texture characteristics
Multi-directional prediction
  Bi-directional intra prediction (BIP)
    Use combination of two modes
    Need additional mode bits
<number>
Copyright © MediaTek Inc. All rights reserved.
Notes: <number>

## Slide 6: Motivation of OBIP
Texture of images will extend cross block boundaries.
One direction per block may be too rough.
Texture characteristic of a block has correlation to its neighboring blocks
<number>
Copyright © MediaTek Inc. All rights reserved.
Notes: <number>

## Slide 7: Outline
Overview
Introduction
Proposed OBIP algorithm
Experimental results
Conclusions
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 8: Proposed OBIP Algorithm
Basic concept
  Inspired by the well-known overlapped block motion compensation (OBMC) idea
  Utilize the mode correlations among neighboring blocks
    Modes of the current block, the left block and the upper block
    A linear combination of 3 possible predictors for each pixel position
Advantages
  Provide bi-directional prediction with little signaling overhead
  Not much complexity increase for decoder
<number>
Copyright © MediaTek Inc. All rights reserved.
Notes: <number>

## Slide 9: Illustration of OBIP
Assume the current block is being predicted
  The modes of the left block A and upper block B are also used
  For each pixel in block C, up to 3 predictors are generated
    If ModeA = ModeB = DC, only ModeC is used, no flag needed
    Else if ModeA = ModeB = ModeC, only ModeC is used, no flag needed
B
C
A
ModeA
ModeB
ModeC
<number>
Copyright © MediaTek Inc. All rights reserved.
Notes: <number>

## Slide 10: Generation of OBIP Pixels
Assume a pixel S(i, j) is being predicted
  PC(i, j) – predictor using ModeC
  PA(i, j) – predictor using ModeA
  PB(i, j) – predictor using ModeB
The prediction P(i, j) for S(i, j) can be calculated as
  is the weighting value on PX(i, j) when the current
  block mode is ModeC
<number>
Copyright © MediaTek Inc. All rights reserved.
Notes:   Three possible predictors PC(i, j), PA(i, j), and PB(i, j) can be generated with ModeC, ModeA and ModeB respectively
<number>

## Slide 11: An Example of OBIP Process
ModeA, ModeB, and ModeC are vertical, horizontal and diagonal directions, respectively
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 12: An Example of Weighting Values
<number>
Copyright © MediaTek Inc. All rights reserved.
Notes: <number>

## Slide 13: Implementation on TMuC
We still keep the TMuC anchor intra prediction modes.
The extra 9 OBIP modes are added
  Corresponding to the H.264 intra prediction modes
  Applied to 4x4 and 8x8 blocks only
If the neighboring blocks are one of 17 or 34 “single-directional” modes,
  The predictor based on this mode is formed as it is,
  But the weighting coefficients are determined based on the mode mapped from 17 or 34 modes to 9 closest H.264 modes
OBIP on/off switching at TU level
Due to incompatibility, OBIP doesn’t support Edge-Based Prediction or Planar Prediction.
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 14: Outline
Overview
Introduction
Proposed OBIP algorithm
Experimental results
Conclusions
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 15: Experimental Results
Anchor – TMuC0.7
Test conditions – JCTVC-B300
Thank Microsoft for cross verifying our results (C272).
<number>
Copyright © MediaTek Inc. All rights reserved.
 | Intra HE |  |  | Intra LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.0% | -0.9% | -1.3% | -1.8% | -1.2% | -1.1%
Class B | -0.9% | -0.5% | -0.5% | -1.4% | -0.8% | -0.8%
Class C | -1.1% | -0.7% | -0.7% | -1.8% | -1.0% | -0.8%
Class D | -1.2% | -0.5% | -0.6% | -1.7% | -0.9% | -0.8%
Class E | -0.7% | -1.1% | -0.6% | -1.7% | -0.3% | -0.8%
All | -1.0% | -0.7% | -0.7% | -1.7% | -0.8% | -0.8%

## Slide 16: Computation Time
Encoding time and decoding time:
  Encoding time is almost 1.83x compared with current anchor
  Decoding time is almost 1.02x compared with current anchor
  Note that the execution time provided here is an average of the executions in our computer farm (i.e. computer clusters) environment.
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 17: Conclusions
An overlapped block intra prediction (OBIP) algorithm has been investigated
Average BD-rate reduction is 1% and 1.7% for high efficiency and low complexity respectively
The complexity of OBIP will not increase much for the decoder
We only have time to modify our old OBIP proposal to fit in TMuC, and don’t have time to optimize it.
  We propose to continue the investigation of this technique in a Test Experiment.
<number>
Copyright © MediaTek Inc. All rights reserved.

## Slide 18
<number>
Copyright © MediaTek Inc. All rights reserved.