## Slide 1: JCTVC-C216: TE12.3: results for edge based prediction
Virginie Drugeon

## Slide 2: Outline
Edge based prediction in TMuC 0.7.1
Results for TE12 configuration
Additional results
Conclusion

## Slide 3: Edge based prediction in TMuC 0.7.1
Edge detection using the Sobel operators in the neighboring blocks
Extrapolation of the reference pixels along the direction of the detected edge

## Slide 4: Results for TE12 configuration
TMuC 0.7.1 with
  #define BUGFIX51 1 in TypeDef.h
  Parameter „EdgePredictionEnable“ modified in the configuration file
    Reference: EdgePredictionEnable: 1
    Alternative setting: EdgePredictionEnable: 0
Bug fix 51:
  Effect of bug: turn off edge based prediction for low complexity
  Anchors had to be changed to show the effect of edge based prediction for low complexity
Compiler: gcc 4.4.3
Linux 64 bits

## Slide 5: Results for TE12 configuration
Results for intra only configuration
Very little impact of edge based prediction when all intra tools are enabled
Competition with unified intra prediction
Lack of harmonization with important intra tools: MDDT, adaptive residual scan, ROT, AIS

## Slide 6: Additional results
Second approach: intra tools are turned off and only one tool is turned on for comparison
CIP, ROT, AIS, MDDT, adaptive scan and unified intra are turned off
TMuC 0.7.1 with
  #define BUGFIX51 1 in TypeDef.h
  Parameter „EdgePredictionEnable“ modified in the configuration file
    Reference: EdgePredictionEnable: 0
    Alternative setting: EdgePredictionEnable: 1
Only two seconds of each sequence encoded

## Slide 7: Additional results
Results for intra only configuration
Good for content with sharp edges
Little impact for content with textures such as trees

## Slide 8: Conclusion
Little impact of EBP for TE12 test configuration
Results with other test configurations show the potential of the technique
Harmonization with some intra tools is lacking. Better gain is expected if EBP is harmonized with:
  MDDT
  Adaptive scan
  AIS
Proposal: further study edge based prediction harmonized with other intra tools in the context of a tool/core experiment