## Slide 1: Encoding complexity reduction for Intra prediction by Disabling NxN Partition
J. Kim, Y.Jeon, S.Park, B.Jeon
JCTVC-C218

## Slide 2: Introduction
In TMuC, two kinds of prediction sizes are defined for intra PU
  2Nx2N and NxN
  signaled by intra_split_flag
PU
PU
2Nx2N
NxN

## Slide 3: Introduction
So encoder tests both prediction sizes for every depth
Depth D
PU
2Nx2N
Depth D
PU NxN
PU
2Nx2N
PU
2Nx2N
PU
2Nx2N
PU
2Nx2N
PU
NxN
PU
NxN
PU
NxN
PU
NxN
Depth D+1
PU
2Nx2N
PU
2Nx2N
PU
2Nx2N
PU
2Nx2N
Depth D+2
●●●
Prediction size is same when
  intra_split_flag=1 (NxN) in depth D
  intra_split_flag=0 (2Nx2N) in depth D+1

## Slide 4: Introduction
Encoder tests target blocks with same prediction size twice for every depth
  In both cases,
  - Target block is same
  - Prediction size is same
  - Neighboring pixels for intra prediction is same
  - So the predicted block is same
Same process done twice because TMuC has two ways for signaling intra prediction size.
The redundant process only increases encoder complexity

## Slide 5: Introduction (Summary)
TMuC has two ways for signaling intra prediction size
  intra_split_flag=1 in depth D
  intra_split_flag=0 in depth D+1
This redundant structure makes encoder to test same case twice
Removing one of them is more helpful
  Easily done by having only one partition type for intra
  Having 2Nx2N is better (90% of PUs are coded with 2Nx2N while only 10% of PUs are coded with NxN)

## Slide 6: Proposed method
Allow only one partition type for intra (2Nx2N)
  - intra_split_flag is not needed
  - Removes the redundant process at encoder
But the NxN splitting should be allowed at least in minimum CU
  Without intra_split_flag,
    Minimum CU can not be split further

## Slide 7: Proposed method (Summary)
prediction_unit( x0, y0, currPredUnitSize ) {
…
if( PredMode == MODE_INTRA ) {
…
if(entropy_coding_mode_flag) {
if(currCodingUnitSize== MinCodingUnitSize) {
intra_split_flag
}
…
}
}
if( chroma_format_idc != 0 )
intra_chroma_pred_mode
}
…
Allow intra_split_flag only when a CU is the minimum CU

## Slide 8: Test condition
Coding conditions
  Intra high efficiency
Computing platform
  Windows XP, 64-bit professional, Xeon(E5520), 2.5GHz, Memory 16GB
Comparison
  Anchor : TMuC 0.8
  Proposed : Modified TMuC 0.8 (NxN splitting for intra is allowed only in minimum CU)
Measurement
  Encoding time (%)
  BD-Rate (%)

## Slide 9: Simulation results
Under Intra HE, 5% time-saving is achieved by the proposed scheme(2Nx2N only) relative to anchor (2Nx2N, NxN)
Class | A | B | C | D | E | Avg.
EncT (%) | 95.6 | 94.8 | 97.3 | 96.9 | 93.1 | 95.5
BDR (%) | 0.1 | 0.1 | 0.2 | 0.1 | 0.4 | 0.2

## Slide 10: Simulation results
Under Intra HE,
Time consumed for CIP : 18%
  (JCTVC-C092) TE12: Report on Combined Intra Prediction evaluation
  82% time is consumed for (CIP=0) relative to (CIP=1)
Time consumed for ROT : 41%
  (JCTVC-C268) TE 12: Report on evaluation of MDDT and ROT
  59% time is consumed for (MDDT=1 && ROT=0) relative to (MDDT=1 && ROT=1)
Time saving by the proposed scheme is not too big because of the complex intra tools (CIP & ROT)

## Slide 11: Simulation results
Time saved by the proposed method becomes relatively small because the time consumed for CIP and ROT are too big
At encoder, the proposed scheme does not affect on CIP and ROT because CIP and ROT are evaluated after best intra prediction partition size is decided

## Slide 12: Simulation results
When CIP and ROT are turned off for both anchor and the proposed,
- only 64% time is needed for the proposed scheme(2Nx2N only) relative to anchor (2Nx2N, NxN)
Class | A | B | C | D | E | Avg.
EncT (%) | 64.6 | 63.9 | 63.8 | 64.2 | 64.3 | 64.2
BDR (%) | 0.4 | 0.3 | 0.4 | 0.2 | 0.5 | 0.4

## Slide 13: Summary
Current TMuC has redundancy in signaling of partition size for intra prediction
The redundancy only increases encoder complexity
The redundancy can be easily removed by allowing intra_split_flag only in minimum CU
By adding a condition for intra_split_flag, encoder complexity can be greatly reduced with negligible loss