## Slide 1
TE4: Report on VLC for Coded Block Flag
(JCTVC-C262, m18303)

## Slide 2: Current Coded Block Flag Coding
At CU level
  Coded block flags for Y, U and V component are coded jointly
At block level
  1 bit flag for each transform block
Blk0
Blk1
Blk2
Blk3
A coding unit

## Slide 3: Proposed Solution on Coded Block Flag at Block Level
When available, for each of Y,U and V component, group the four coded block flags of the same video component and code with a single codeword
15 possible combinations to be coded
VLC table selection and codeword mapping is performed in a similar manner as that for other VLC syntax elements
Different VLC tables used for intra and inter blocks
Blk0
Blk1
Blk2
Blk3
A coding unit

## Slide 4: Test Conditions
Test conditions
  The same test conditions used in TE12 are used here, with the following changes:
    LCEC_PHASE2 enabled
    RQT disabled

## Slide 5: Test Results on Coded Block Flag
All intra | New CBF coding
low complexity | 
WQVGA30_RaceHorses | -0.3
WQVGA50_BasketballPass | -0.2
WQVGA50_BlowingBubbles | -0.4
WQVGA60_BQSquare | -0.3
WQVGA AVE | -0.3
WVGA30_RaceHorses | -0.2
WVGA50_BasketballDrill | -0.1
WVGA50_PartyScene | -0.4
WVGA60_BQMall | -0.2
WVGA AVE | -0.2
720p60_Vidyo1 | -0.1
720p60_Vidyo3 | -0.1
720p60_Vidyo4 | -0.2
720p AVE | -0.2
1080p24_ParkScene | -0.2
1080p24_Kimono | -0.2
1080p50_BasketballDrive | -0.2
1080p50_Cactus | -0.2
1080p60_BQTerrace | -0.3
1080p AVE | -0.2
PeopleOnStreet | -0.1
Traffic | -0.2
4kx2k AVE | -0.2
Average | -0.2

## Slide 6: Test Results on Coded Block Flag (cont. 1)
Low delay | New CBF coding
low complexity | 
WQVGA30_RaceHorses | -0.1
WQVGA50_BasketballPass | -0.2
WQVGA50_BlowingBubbles | -0.2
WQVGA60_BQSquare | -0.1
WQVGA AVE | -0.2
WVGA30_RaceHorses | -0.2
WVGA50_BasketballDrill | -0.2
WVGA50_PartyScene | -0.3
WVGA60_BQMall | -0.1
WVGA AVE | -0.2
720p60_Vidyo1 | 0.0
720p60_Vidyo3 | -0.2
720p60_Vidyo4 | -0.1
720p AVE | -0.1
1080p24_ParkScene | -0.2
1080p24_Kimono | -0.2
1080p50_BasketballDrive | -0.2
1080p50_Cactus | -0.2
1080p60_BQTerrace | -0.2
1080p AVE | -0.2
Average | -0.2

## Slide 7: Test Results on Coded Block Flag (cont. 2)
Random access | New CBF coding
low complexity | 
WQVGA30_RaceHorses | -0.1
WQVGA50_BasketballPass | -0.2
WQVGA50_BlowingBubbles | -0.2
WQVGA60_BQSquare | -0.2
WQVGA AVE | -0.2
WVGA30_RaceHorses | -0.2
WVGA50_BasketballDrill | 0.0
WVGA50_PartyScene | -0.2
WVGA60_BQMall | -0.1
WVGA AVE | -0.2
1080p24_ParkScene | -0.2
1080p24_Kimono | -0.1
1080p50_BasketballDrive | -0.1
1080p50_Cactus | -0.2
1080p60_BQTerrace | -0.2
1080p AVE | -0.2
PeopleOnStreet | -0.1
Traffic | -0.2
4kx2k AVE | -0.1
Average | -0.2

## Slide 8: Conclusions
The proposed solution for block level coded block flags provides about 0.2% average coding gain, with each of three low complexity configurations.
Results verified by Toshiba (JCTVC-C288)
We recommend the coding scheme to be adopted into TMuC.