## Slide 1: TE6.a: report of line-based coding
Xiulian Peng
Jizheng Xu
Feng Wu
Microsoft

## Slide 2: Outline
Line-based coding revisit
  Which has been presented in JCTVC-A118
TE results
Conclusion

## Slide 3: Line-based coding
Basic unit – a line
  A row of pixels
  A column of pixels
  Length – 4, 8 or 16
The prediction parameter of each line is derived from the reconstructed area
  Local training
  Predefined directional filter
  Template matching
  One of the above three derivation methods is used. The selection is transmitted to the decoder.

## Slide 4: Local training
Reference pixels for the current pixel
  Three upper pixels to predict the current pixel in a row
  Three left pixels to predict the current pixel in a column
The prediction weights are calculated according to the surrounding statistics
  Wiener filter
Decoder can make the same derivation and no overhead is needed

## Slide 5: Predefined directional filter
19 predefined prediction patterns
  Correspond to different directions and different degrees of sharpness of edges
  Avoid over-fitting that may happens in the local training method
  One of the filter that shows the best prediction performance in the surrounding area is chosen
Decoder can make the same derivation and no overhead is needed

## Slide 6: Template matching
Template matching to search for a good prediction for one line
  The line to be coded has short distance to the template, which leads to a better prediction performance than block-based template matching
Decoder can make the same derivation and no overhead is needed

## Slide 7: Overhead for a block (PU)
Row-by-row coding or column-by-column coding
Transform or not
Prediction methods
  Local training
  Predefined directional filter
  Template matching

## Slide 8: Experimental results – class A
 | All Intra High Efficiency | All Intra Low Complexity
Sequence | BD-bitrate | BD-bitrate
Traffic_2560x1600_30_crop | -1.0% | -0.7%
PeopleOnStreet_2560x1600_30_crop | -1.5% | -1.7%
Average 1600P | -1.3% | -1.2%

## Slide 9: Experimental results – class B
 | All Intra High Efficiency | All Intra Low Complexity
Sequence | BD-bitrate | BD-bitrate
Kimono1_1920x1080_24 | -0.7% | -0.6%
ParkScene_1920x1080_24 | -0.7% | -0.4%
Cactus_1920x1080_50 | -3.1% | -3.4%
BasketballDrive_1920x1080_50 | -2.4% | -2.7%
BQTerrace_1920x1080_60 | -4.4% | -5.1%
Average 1080P | -2.3% | -2.4%

## Slide 10: Experimental results – class C
 | All Intra High Efficiency | All Intra Low Complexity
Sequence | BD-bitrate | BD-bitrate
BasketballDrill_832x480_50 | -4.2% | -5.1%
BQMall_832x480_60 | -3.0% | -3.7%
PartyScene_832x480_50 | -2.3% | -3.0%
RaceHorses_832x480_30 | -1.2% | -1.4%
Average WVGA | -2.7% | -3.3%

## Slide 11: Experimental results – class D
 | All Intra High Efficiency | All Intra Low Complexity
Sequence | BD-bitrate | BD-bitrate
BasketballPass_416x240_50 | -2.0% | -2.4%
BQSquare_416x240_60 | -3.4% | -4.7%
BlowingBubbles_416x240_50 | -1.8% | -2.4%
RaceHorses_416x240_30 | -1.2% | -1.4%
Average QWVGA | -2.1% | -2.7%

## Slide 12: Experimental results – class E
 | All Intra High Efficiency | All Intra Low Complexity
Sequence | BD-bitrate | BD-bitrate
vidyo1_720p_60 | -2.0% | -2.1%
vidyo3_720p_60 | -2.3% | -2.2%
vidyo4_720p_60 | -1.3% | -1.3%
Average 720P | -1.9% | -1.9%

## Slide 13: Overall performance
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.3 | -0.6 | -0.7 | -1.2 | -0.4 | -0.6
Class B | -2.3 | -1.0 | -0.9 | -2.4 | -0.6 | -0.8
Class C | -2.7 | -1.1 | -1.3 | -3.3 | -1.1 | -1.2
Class D | -2.1 | -0.9 | -0.9 | -2.7 | -0.8 | -0.8
Class E | -1.9 | -0.7 | -0.6 | -1.9 | -1.2 | -1.1
All | -2.1 | -0.9 | -0.9 | -2.4 | -0.8 | -0.9
Enc Time[%] | 172% |  |  | 229% |  | 
Dec Time[%] | 208% |  |  | 301% |  | 

## Slide 14: Conclusion
Various methods to provide accurate predictions for one line
Line-based coding improves the coding performance by making the prediction distance shorter