## Slide 1: TE10, Subset 1: Report of Content-Adaptive Deblocking
Zhiwei Xiong
Xiaoyan Sun
Jizheng Xu
Microsoft

## Slide 2: Outline
Content-adaptive deblocking revisit
  Which has been presented in JCTVC-A118
  General idea: a stronger deblock for large blocks (smooth regions)
TE results
Conclusion

## Slide 3: Content-adaptive deblocking
Perform a strong and long filter to some TU boundaries
  Apply to smooth region to further reduce blocking artifacts
Deblocking is changed to TUs, which satisfy the following conditions
  The two adjacent TU’s related to the TU boundary are both in intra-coded CU’s
  The sum of luminance variance in the two TU's is smaller than a certain threshold
  The smaller transform size between the two TU's is larger than a certain value
  The larger transform size between the two TU's is larger than a certain value

## Slide 4: The proposed deblokcing filter

## Slide 5: Experiments
TMuC0.7
Implemented for I-frames

## Slide 6: Experimental results - intra
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.3 | 0.0 | 0.0 | 0.2 | 0.0 | 0.0
Class B | 0.3 | -0.1 | -0.1 | 0.3 | 0.0 | 0.0
Class C | 0.1 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class E | 0.4 | -0.3 | -0.2 | 0.3 | -0.2 | -0.1
All | 0.2 | -0.1 | -0.1 | 0.2 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 

## Slide 7: Experimental results – random access
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.1 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0
Class B | 0.1 | -0.2 | 0.1 | 0.1 | -0.1 | -0.1
Class C | 0.0 | -0.2 | -0.1 | 0.0 | 0.0 | 0.0
Class D | 0.0 | -0.1 | 0.0 | 0.0 | -0.1 | 0.1
Class E |  |  |  |  |  | 
All | 0.1 | -0.1 | 0.0 | 0.0 | -0.1 | 0.0
Enc Time[%] | 100% |  |  | 102% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 

## Slide 8: Experimental results – low delay
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.0
Class C | 0.0 | -0.2 | 0.0 | 0.0 | 0.0 | 0.1
Class D | 0.0 | 0.0 | 0.0 | 0.0 | -0.1 | 0.0
Class E | 0.3 | -0.2 | 0.0 | 0.1 | -0.1 | 0.0
All | 0.0 | -0.1 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 98% |  |  | 97% |  | 

## Slide 9: Visual quality evaluation
Less blocking artifacts
Refer to the doc JCTVC-C273.doc
Flickering
  All I-frames
  Should be consistent when RA and LD
Blurring
  Does not mean visually worse

## Slide 10: Conclusion
A stronger deblocking applied to large smooth region
Little impact on the objective quality and complexity
Better visual quality by further reducing blocking artifacts
May be more useful for even higher resolution videos
Propose to consider a stronger deblocking for large blocks in the design